## Slide 1: Conceptual Design of the LMQXFA Test Cryostat
Don Mitchell
Preliminary Design Review
25 APR 2016

## Slide 2: Agenda
Convert Test Stand #4 to test LMQXFA Coldmass
General overview
P&ID
Existing test stand components
Proposed modifications
Vacuum Vessel preliminary design and analysis
Design challenges
Estimated costs
Schedule
Summary

## Slide 3: IB1 – Test Stand
Test Stand #4
Test Stand #6
“Jessica” Test Cryostat

## Slide 4: Proposed LMQXFA Test Stand #4
Reuse as much of the existing test stand as possible.
Feedcan
Turn-a-round can
Alignment of cryostat in X and Y. Minimum alignment along axis.
New Test Cryostat

## Slide 5: LMQXFA Coldmass
Weight = 32,957 Lbs
10140 mm

## Slide 6: LQXFA Cryostat
Aluminum construction to minimize weight (crane limitation)
Weight = 3,500 Lbs
Initial design parameters:
½” wall thickness
1 ¼” reinforcement ribs
Reinforced base to support coldmass

## Slide 7: LMQXFA Cryostat with Coldmass
Total weight = ~37,250 Lbs

## Slide 8: LMQXFA Cryostat with Coldmass - sectioned
Coldmass supported at 3 points

## Slide 9: LMQXFA Test Stand #4 - sectioned

## Slide 10: Present Cryogenic Capabilities
With proper cryostat provisions (pumping line with cross-overs, cool-down return, thermal shield), the cryogenic process of LQX and MQX testing will be similar to the testing of the present LHC IR quads.
Lead flows
To compressor suction
GN2 vent
Pumps
LHe/GHe
supply
LN2 supply
Fill valves
J-T HX
Cool-down/
warm-up return
Reliefs, quench
recovery
J-T valve
Return End
Cryostated cold mass with external pumping line
Interconnect
Feed Box
1.9 K saturated liquid
1.9 K subcooled liquid
4.5 K saturated liquid

## Slide 11: Existing Feedcan Piping Layout
Heat exchanger is external to the Coldmass.
The original coldmass is small relative to the LMQXFA coldmass.

## Slide 12: Existing Feedcan Piping Layout
Feed Box Connections
  Heat exchanger (for present LHC IR quadrupoles, inner line is pumped 1.9 K two-phase and annular area is subcooled 1.9 K liquid)
  Magnet He supply (two for instrumentation, one for power bus, one capped)
  Beam pipe for warm bore/magnetic measurements
  Cool-down return
  Thermal shield LN2 supply and return

## Slide 13: Proposed Feedcan Layout
Heat exchanger moved internal to the Coldmass, 2 locations.
Piping no longer matches the feedcan pipe locations. Possible re-route with flex-hose.

## Slide 14: Existing Turn-a-round Can Layout
Existing can does not match the new piping layout.
Items to consider:
Instrumentation can
Liquid level probe
Cooldown line
Bus/Cable routing
HX location

## Slide 15: Inner Triplet Busbars Integration Proposal (until a 18kA cable is developed and proven)
Courtesy of Cedric Eymin
18kA
18kA
2kA
200A
2kA
200A
2.8kA,
12Hz fast decay
External busbars
(round cable type)
Splices
+ | 13
+ | 11
 | 2
 | 2
 | 2
 | 24
 | 36
 | 18
Total 108
Internal busbars
(stabilized Rutherford cable)
In Q2 cold masses

## Slide 16: Proposal
Increase diameter of cryostat
Design new end-can
Reuse the existing Feedcan

## Slide 17: Vacuum Vessel Design and Analysis
6061-T6 Aluminum Construction
½” wall
1 ¼” reinforcement ribs
2” thick base plates
3,500 Lbs
Initial design

## Slide 18: Vacuum Vessel Loading
10,900 Lbs
10,900 Lbs
11,757 Lbs
14.5 psi external pressure
Vessel under its own weight

## Slide 19: Vacuum Vessel FEM
Combination of 8-node 2-D quads and 10-node 3-D tets plus mating conditions

## Slide 20: Vacuum Vessel Loading
14.5 psi external pressure, Gravity, Magnet Loading

## Slide 21: Vacuum Vessel FEA Results - Preliminary
Model validation:
1G loading
  Reaction Forces:
    Weight = 3,440 Lbs
Under Vacuum:
Δ = .007 inch

## Slide 22: Fully Loaded Cryostat – Vacuum, Magnet, Gravity

## Slide 23: FEA Results
Δ = .024 inch
σmax = 4,814 psi
Plenty of margin for redesign and optimization. Design to meet ASME B&PV code.

## Slide 24: Design Challenges
Recent input from CERN is still developing
  Location of internal heat exchangers – bottom two holes
    (we assumed the top two holes)
  Bus bar or cables, where to route them?
Re-routing items in the turn-a-round can
  Ports don’t line up
  Warm up / Cool down line in turn-a-round can
  Routing is difficult
  Do we design something new?
Do we need a larger Cryostat due to the large Coldmass diameter?

## Slide 25: Cryostat Components
Cool-down line
Heat Exchanger pipe
Aluminum Heat Shields
Al-SS transition
Vacuum Vessel
MLI
Bellows

## Slide 26: Cryostat Estimated Costs
Vacuum vessel: $ 90,000
Heat exchanger corrugated pipes (2): $ 7,000
Cryogenic pipes: $ 8,000
G10 pipe supports: $ 10,000
Coldmass supports (3): $ 25,000
Aluminum Heat Shields: $ 50,000
Al-SS transition pipes (4):$ 3,600
Flex hoses: $ 5,000
Alignment Stands (2): $10,000
MLI: $ 1,200
New end-can not costed
Total: $ 209,800 (BOE: previous history and best guess)

## Slide 27: Labor Estimated Costs
FTE:
Skill | FY16 | FY17 | FY18 | FY19 | Total
Engineer | .25 | .25 | .25 | .25 | 1.0
Design | 0 | .2 | .3 | .3 | .8
Technician | 0 | 0 | 0 | 1.0 | 1.0

## Slide 28: Schedule

## Slide 29: Summary
Preliminary study has begun
  Collected existing IB1 Test Stand #4 CAD data
  Design requirements are still coming together
  Basic FEA shows that a vacuum vessel can be designed to:
    Meet ASME B&PV code
    Work within the weight limitations of the IB1 crane
    More iterations are needed
  Identified the major components required
  Preliminary cryostat system being 3-D modeled
Initial cost estimate for cryostat: $210,000
Minimal Engineering, Design, and Technician support over the next 4 years – next priority, CD-1 Review
Functional Test Cryostat ready by January 2020