## Slide 1: Program overview: motivation, target parameters, timeline
A.V. Zlobin
15 T dipole design review
28 April 2016

## Slide 2: Current HFM R&D Program
As a part of the National HFM collaboration develop accelerator magnets with world record parameters
  Small-aperture 15-16 T Nb3Sn dipole suitable for VHEppC (phase 1)
    background field for small 1-2 T HTS inserts
  Large-aperture 15 T Nb3Sn dipole with stress management (phase 2)
    background field for 5+ T HTS inserts
Magnet cost optimization
Superconductor and structural material R&D for 15-20 T accelerator magnets
  Nb3Sn composite wires
  Large Rutherford cables

## Slide 3: Program Timeline
VLHC
HL-LHC
LARP
VHEppC
Record field 13.8 T
HFDA HFDM-LM 43.5 mm Dipole mirror
10 T dipole
TQC TQM-LQM
90 mm 200 T/m Quadrupole quadrupole mirror
HFDC (R&W)
40 mm 10 T dipole
MBHDP
60 mm 11 T dipole
MBHSP MBHSM
60 mm 11 T dipole Dipole mirror
D20 (LBNL)
50 mm dipole
13.5 T (1997)
HD2 (LBNL)
35 mm dipole
13.8 T (2008)
Ph1 Ph2

## Slide 4: Program Reviews
This plan was presented at the DOE magnet meeting in July 2015 in Washington DC. “There is a consensus we need to build demonstrations of 16 T Nb3Sn magnets to define the ultimate limit of Nb3Sn technology. The FNAL proposal to develop 16 T block cosine theta (BCT) suits this need, but must be a collaborative effort and needs to be done on a time scale commensurate with the GARD budget constraints”.
FNAL accelerator advisory committee (AAC) review in Dec 2015 confirmed that “the HFM program is reasonable and aligned with P5 goal of increasing performance toward 15 T, for accelerator class magnets”.
The program is being integrated into Magnet Development program (MDP) and will be reviewed later as its key part.

## Slide 5: Magnet Design Options
FRESCA2 (CERN),
16 T, 2017
RD3c (LBNL),
10 T, W&R, 2003
DCC017 (BNL),
10 T, R&W, 2007
HFDC (FNAL),
~6 T, R&W, 2004
MBHSP (FNAL)
11.7 T, 2011-2014
MBHDP (FNAL)
11.5 T, 2015
HFDA (FNAL)
10 T, 2003-2006
D20 (LBNL),
13.5 T, 1997
Cos-theta coil design
HD2 (LBNL),
13.8 T, 2008
Block coil design
HD2 (IHEP, China),
12-15-20 T, 2020-2025
Common coil design
LBNL: CCT
FNAL: BCT

## Slide 6: Magnet Concept Choice
2013 DOE review of HEP:
Recent efforts toward high field magnets have not been as successful as expected. Despite a doubling of the critical current density in Nb3Sn, recent test magnets with a gap have not improved upon the earlier D20 field results of about 14 T... Given the lack of progress in increasing the bore field, it may be worthwhile to consider designing, fabricating, and testing a cos-theta magnet like D20 but using the recent advances in 2D/3D design techniques and the best available Nb3Sn strand to see if there are any fundamental limitations to the present approach.
Fermilab has large experience with accelerator magnets based on the Nb3Sn superconductor and cos-theta coils

## Slide 7: Design Approach and Concept
Approach:
use the available tooling and FNAL fabrication and test infrastructure to reduce the magnet R&D cost and time
Design concept:
Coil aperture: 60 mm
  sufficient coil aperture is needed to accommodate beam, beam screen, cold bore, etc.
  coil stress and energy density strongly depend on coil ID
  coils with large aperture require stress management => magnet cost
  aperture optimization is a collective effort of accelerator, magnet and cryogenic experts
Coil design: modified cosθ,4 layers, graded
Cold mass design: collarless, cold iron yoke, OD<610 mm
Design optimization parameters: Bmax, field quality, coil volume, azimuthal stress, quench protection

## Slide 8: Coil Design Study
4L-1
4L-2
4L-3
4L-4
4L-5
Parameter | Cable 1 | Cable 2
Number of strands | 28 | 40
Mid-thickness, mm | 1.870 | 1.319
Width, mm | 15.10 | 15.10
Keystone angle, deg | 0.805 | 0.805

## Slide 9: Mechanical Structure
Thin coil-yoke spacer (no collar)
2-piece vertically split yoke
Yoke clamp: SS C-clamps (v.1) vs. Al I-clamps (v.2)
Skin: SS bolted skin from 11 T dipole (v.1) vs. welded skin (v.2)
Cold mass OD<610 mm (VMTF Dewar limit)
Axial support: thick SS rods and end plates
HD2 structure:
cold mass OD=705 mm
Al shell thickness 40 mm

## Slide 10: Magnet Design Specifications

## Slide 11: Strands and Cables
Magnet short sample estimated based on the cable test data:
  11.1 kA (Bap=15.3 T) at 4.5 K
  12.2 kA (Bap=16.7 T) at 1.9 K
RRP150/169
RRP108/127

## Slide 12: Magnet Engineering Design
Coil design
  layers #1 and #2
  layers #3 and #4
    end parts optimization
Coil tooling
  winding, curing, reaction, impregnation
Cold mass design
  yoke, clamps, skin, end plates
Cold mass assembly tooling
  yoke clamping
  skin welding

## Slide 13: Coil Fabrication Infrastructure
To avoid infrastructure and stuff conflicts with LARP, new coil fabrication line has been created in IB3A (next to SCRD Lab).
SCRD techs are being trained to wind short coils.

## Slide 14: Test Goals
Demonstration of 15-16 T field level
Study and optimization of
  magnet quench performance
    training, degradation, memory, effect of coil pre-load
  ramp rate sensitivity
  operation margin
  quench protection
    heater efficiency, radial quench propagation, coil quench temperature
  field quality
    geometrical harmonics, coil magnetization, iron saturation, dynamic effects

## Slide 15: Instrumentation
Instrumentation
Voltage taps
Strain gauges
Quench antenna
Rotating probes
Temperature sensors
Vertical Magnet Test Facility (FNAL)
Test temperature range 1.9-4.6 K
Quench antenna
Voltage taps

## Slide 16: Conclusions
R&D of a 60-mm aperture 15 T Nb3Sn dipole demonstrator for future VHEppC has started at Fermilab:
  Magnet design study phase is complete
  Magnet and tooling engineering design and parts procurement are in progress
  Cable for inner coils was developed, fabricated and tested
  Cable for outer coils is available from the 11 T dipole
  Practice outer coil (layers #3 and #4) is being wound
  Magnet fabrication and first tests are planned for 2017
  Schedule is coordinated with CERN FCC Design Study Report

## Slide 17: Publications
IPAC2015
A.V. Zlobin, N. Andreev, E. Barzi, V.V. Kashikhin, I. Novitski, “Design concept and parameters of a 15 T Nb3Sn dipole demonstrator for a 100 TeV hadron collider”, IPAC2015.
CEC/ICMC2015
V.V. Kashikhin, N. Andreev, E. Barzi, I. Novitski, A.V. Zlobin, “Magnetic and structural design of a 15 T Nb3Sn accelerator dipole model”, CEC/ICMC2015, Tucsan (AR), June 2015.
MT-24
I. Novitski, N. Andreev, E. Barzi, J. Carmichael, V. V. Kashikhin, D. Turrioni, M. Yu, A. V. Zlobin, “Development of a 15 T Nb3Sn Accelerator Dipole Demonstrator at Fermilab”, IEEE Trans. on Appl. Supercond., 2016.
E. Barzi, N. Andreev, P. Li, V. Lombardo, D. Turrioni, A. V. Zlobin, “Nb3Sn RRP® Strand and Cable Development for a 15 T Dipole Demonstrator,” IEEE Trans. on Appl. Supercond., 2016.

## Slide 18: Program Presentations and Discussions
The program was presented and discussed inside the National magnet collaboration and at
  October 2014 – FCC meeting at ASC2014
  March 23-27, 2015 – FCC meeting in WDC
  June 2015 – ICFA magnet mini-workshop
  July 14-15, 2015 – magnet meeting at FNAL
  July 28, 2015 – magnet workshop at WDC
  December 9, 2015 – FNAL AAC
  December 17, 2015 – DOE briefing on FNAL GARD program
  February 8-10, 2016 – LTSW2016
  April 10-15, 2016 – FCC meeting in Rome