## Slide 1
2.2.1 Findings
The conceptual electrical design of the APA and the grounding solutions to be adopted have been presented during the review. PSL is working in coordination with BNL and the ProtoDune project management to finalize the design and proceed to procurement and production.
Information and feedback from the 35ton tests may be of limited use given the noise problems experienced during the tests and the difficulty in disentangling effects due to the 35t environmental noise, design faults in the cold electronics (CE) and possible weaknesses in the APA electric and grounding design.
This potential risk is mitigated by the warm and cold electric tests that are planned in the QA procedures prior to installation at CERN
Electrical/Grounding

## Slide 2
2.2.2 Comments
The use of the mesh is supported by data from the 35ton test but the electrical specs have not been fully defined yet. A full electrical characterization as a function of frequency has not been shown.
The use of separate boxes to host CE is relatively new in the design history of the APA and will be tested in realistic conditions just at CERN. As a consequence, the grounding design should be configurable in order to react to unexpected problems in the commissioning phase.
Material selection (electric components suitable for cryogenic application) is, in principle not particularly challenging but tests and procurement time is critical for the schedule of the project.
The current design focuses on ease of access of electronics (boxes) and components (CR boards, G plane bias board ); however, these solutions pose potential issues on grounding that should be addressed.

## Slide 3
2.2.3 Recommendations
Consider a configurable design in the most critical ground attachment points
Give high priority on electric component selections suitable for cryogenic operation and include procurement and test in the APA production schedule
Consider extending the scope (beyond the proposed 10%) of the cold and post-cooling tests to identify damages affecting electrical performance after thermal cycles
As the electrical design of the HV Wire Bias Filter Board and the CR Wire Board matures, the overall HV wire bias distribution design including all Printed Circuit Boards and wire connections should be reviewed by the DUNE Grounding and Shield Committee.