## Slide 1
Eric Prebys*
Fermilab/UC Davis
3 August 2017
*for the Mu2e Collaboration
Beam Delivery and Out of Time Extinction in the Mu2e Experiment at Fermilab

## Slide 2: The Search for m+N  e+N
m
~105 MeV e-
When captured by a nucleus, a muon will have an enhanced probability of exchanging a virtual particle with the nucleus.
This reaction recoils against the entire nucleus, producing a mono-energetic electron carrying most of the muon rest energy
Very clean experimental signature!
The virtual particle could be
  a photon, in which case, meg searches will also see a signal
  A neutral, heavy boson, in which case there which case they will not!
Can only occur in the Standard Model through virtual neutrino mixing – but at a rate 38 orders of magnitude below anything we could detect.
Virtually all models beyond the Standard Model predict this will happen, most at a rate we could detect (already rules out or constrains many).
Any signal will be unambiguous proof of new physics!

## Slide 3: Experimental Technique and Beam Needs
The general technique is to use protons to make pions, which quickly decay to muons, which are captured on an Aluminum target.
Previous experiments were rate-limited by the need to gate off after individual protons to eliminate prompt backgrounds, which predominantly come from radiative pion capture.
Mu2e will get around this by using a bunched beam of protons, and then waiting for the pions to decay before opening the live window.
This will allow the experiment to achieve a single event sensitivity that is a four order of magnitude improvement of the previous best measurement.

## Slide 4: The Challenge of Producing the Mu2e Beam
All protons at Fermilab come from the Linac/Booster system.
The Booster magnets operate in a 15 Hz offset resonant circuit, which
  Sets a fundamental clock for all all accelerator sequencing
    1/15 second = 1 “tick”
  Sets a fundamental “batch” of protons
    1.6 msec long
    Up to 5x1012 protons
Because the Booster magnets have no flat top, it cannot produce the beam structure required by the Mu2e Experiment.
  This is why the experiment (then called MECO) was originally proposed for Brookhaven
Luckily for us, when the Tevatron shut down in 2011, it freed up some equipment, specifically…

## Slide 5: Reduce, Reuse, Recycle…
The Recycler
  8 GeV storage ring made of permanent magnets
  Originally used to store antiprotons for the Tevatron
  Now used for
    pre-stacking protons for NuMI beam
    Bunching each 1.6 msec booster batches into 4 2.5 MHz bunches with ~1x1012 protons each for g-2 and Mu2e
The Debuncher Ring
  Together with the Accumulator, it was originally used to collect and store Antiprotons for the Tevatron
  Now:
    Used to temporally separate 3.1 GeV/c muons and protons for the g-2 Experiment
  Future:
    Used to circulate and slow extract beam for Mu2e

## Slide 6: Mu2e Proton Delivery
Booster
Main Injector/Recycler
Delivery Ring (formerly pBar Debuncher)
Mu2e
Two Booster “batches” are injected into the Recycler (8 GeV storage ring). Each is:
  4x1012 protons
  1.7 msec long
These are divided into 8 bunches of 1012 each
The bunches are extracted one at a time to the Delivery Ring
  Period = 1.7 msec
As the bunch circulates, it is resonantly extracted to produce the desired beam structure.
  Bunches of ~3x107 protons each
  Separated by 1.7 msec
Exactly what we need

## Slide 7: Resonant Extraction
Extracting all the beam at once is easy, but we want to extract it slowly over ~35 ms (~35,000 revolutions)
Use nonlinear (sextupole) magnets to drive a harmonic instability
Extract unstable beam as it propagates outward
  Standard technique in accelerator physics
Extraction Field
Septum
Unstable beam motion in N(order) turns
Lost beam
Extracted beam

## Slide 8: Extinction
Because out-of-time protons could produce prompt backgrounds, it is critical that there be nothing between the proton bunches at the 10-10 fractional level.
This is referred to as “extinction”
In addition to the challenge of achieving this level of extinction will be the challenge of verifying that we have achieved it (“Extinction Monitoring”)
<1 proton every 250 pulses!

## Slide 9: Principle of Beam Line Extinction
A magnet is used to deflect out-of-time beam into a downstream collimator
Ideally, we would use a square pulse to kick out-of-time beam out of (or in-time beam into) the transmission channel, but the 600 kHz bunch rate makes this impossible with present technology.
We will therefore focus on a system of resonant magnets or “AC Dipoles”.
  Even this isn’t trivial
Think miniature golf

## Slide 10: Dual Harmonic Waveform
AC Dipole driven by two harmonics
  300 kHz (half bunch frequency) to sweep out of time beam into collimators
  4.5 MHz (15th harmonic) to maximize transmission of in-time beam
  Beam transmitted at nodes!
Higher harmonic optimized for maximum transmission: 99.5%
Single harmonic would hit collimator too soon

## Slide 11: Extinction Collimation: Two Separate Collimation Issues
AC dipole shifts distribution along x’ axis in phase space
Beam core: out of time beam will be steered into the collimator or collimators 90° downstream of the AC dipole
Admittance of downstream collimation system
High amplitude beam tails will be steered into the collimation channel, so they must be cleaned up 90° upstream of the AC dipole
Phase space distribution of out of time beam at location of AC dipole

## Slide 12: Additional Problem: Slow Extraction Tails
Beam that strikes the electrostatic septum during slow extraction results in a large tail in phase space, which can result in beam being scattered into the transmission channel.
Requires an additional collimator
X Phase space at exit from Delivery Ring
Nominal beam envelope
This causes problems

## Slide 13: Summary: Collimator Needs and Locations
Extinction Collimator (+90°, 1m Tungsten)
AC Dipole
Halo Collimator (-90°, 1m Steel)
Tail Collimator (1m Steel)

## Slide 14: Simulation Procedure
Longitudinal development in Recycler and Delivery Ring simulated by numerical integration model (I. Kourbanis, S. Werkema)
Beam propagation and evolution of third-order resonance in Delivery Ring simulated by Synergia (V. Nagaslaev)
Extraction interaction with electrostatic septum simulated by MARS (V. Nagaslaev)
Beam line propagation and interaction with collimators simulated with G4Beamline as a function of AC dipole deflection angle to produce transmission tables (E. Prebys)
Transmission tables convoluted with longitudinal distributions to optimize harmonic content of AC dipole magnets transmission of in-time beam and extinction of out-of-time beam (E. Prebys)

## Slide 15: Performance
DR Extraction
Extinction Transmission
Beam on Target
Simulation Results | 
Fraction of DR extracted beam outside of ±125 ns: | 2.1×10-5
In-time beam transmission: | 99.5%
Beam line extinction: | <5×10-8
Total extinction: | 1.1×10-12
Extinction Requirement: | <1.0×10-10
Almost two order of magnitude margin
Beam Window
Notes: DR = Delivery Ring

## Slide 16: Extinction Monitor*
No confidence in extinction unless we can verify it!
Must measure extinction to 10-10 precision
  Roughly 1 proton every 250 bunches!
Required ~108 dynamic range precludes direct measurement
  Particles in bunches would blind detector to out of time particles
Focus on statistical technique
  Designed a monitor to detect a small fraction of scattered particles from target
    10 - 50 per in-time bunch
  Statistically build up precision profile for in time and out of time beam.
Requirement: 90% C.L. for 10-10 extinction after 6 x 1016 p.o.t.
  Signal rate per p.o.t. must be > 2.3 / 6 x 106 = 0.4 x 10-6
  i.e. 16 for a 4 x 107 bunch
*P. Kasper

## Slide 17: Extinction Monitor Design*
Selection channel built into target dump channel
Spectrometer based on 8 planes of ATLAS pixels
Optimized for few GeV/c particles
~ 1 track per 106 on target
*P. Kasper, L. Bartoszek, M. Jones, A* Gaponenko

## Slide 18: Summary
Mu2e had developed innovative techniques to deliver the beam structure required by the experiment, including the stringent limits on out-of-time beam (“extinction”)
We have a robust technique for verifying that we have achieved the required level of extinction.
A projects are well on track to meet the schedule of the experiment as a whole.