## Slide 1: Brief Introduction to Wire-Cell
Xin Qian
BNL
For the Wire-Cell Team
http://www.phy.bnl.gov/wire-cell/

## Slide 2: Challenges of Event Reconstruction in LArTPCs
Event topology:
  Tracks, showers, unknown vertex in LArTPCs
  Simple tracks in collider’s gas TPCs
Wire vs. Pixel readout
  Large LArTPCs has to use wire readout due to power consumption of electronics and costs
  Puedo-3D detector

## Slide 3: Review of Existing Approaches
2D matching  3D
Wire-Cell Approach

## Slide 4: Wire-Cell Imaging
slicing
tiling
merging
solving
LArTPC Signal Formation

## Slide 5: Solving for Images
C: charge in each (merged) cell
G: Geometry matrix connecting cells and wires
W: charge in each single wire
B: Geometry matrix connecting merged wires and single wires
VBW: Covariance matrix describing uncertainty in wire charge
True Hits
Fake Hits
u1
u2
v2
v3
At fixed time
v1
Use two-plane as an example
Red points are true hits
Blue ones are fake hits

## Slide 6: Same formulism for DUNE Wrapped Wire
C: charge in each (merged) cell
G: Geometry matrix connecting cells and channels
W: charge in each single channel
B: Geometry matrix connecting merged channels and single channels
VBW: Covariance matrix describing uncertainty in channel charge
Xiaoyue Li (Stony Brook)

## Slide 7
More 3D events can be found at
http://www.phy.bnl.gov/wire-cell/bee/
Bee: interactive 3D display (Chao Zhang)
With Charge
Without Charge

## Slide 8: The Usage of Connectivity
We can add penalty to χ2 based on connectivity and single channel assumption
  For example, if we remove a merged cell that are connected to good cells in the adjacent time slice, we can add penalty in χ2 to increase the chi-square value  less chance to be chosen as the optimal solution
For later pattern recognition, we can also cluster with all merged cell, and then remove bad ones taking into account connectivity

## Slide 9: Connectivity information
Use the connectivity information to choose the optimal imaging solution
  Penalty term added in chisquare
Without Connectivity
With Connectivity

## Slide 10: Parallel vs. Perpendicular APA
Perpendicular APA
X-Z View
X-U View
X-V View
Parallel APA
The improvement in imaging is from every 2D view!

## Slide 11: Strategy Comparison
2D Matching
Start with 2D (time+wire x 3)
2D pattern recognition
  Particle track/cluster information
Matching 2D patterns into 3D objects
  Time information (start/end of clusters)
  Geometry information
  Some charge information to remove ambiguities in matching
3D Tomography
Start with 2D (wire+wire+wire at fixed time slice)
2D image reconstruction
  Explicit Time + Geometry + Charge information
  Some connectivity information can be used
3D image reconstruction
  Straight forward
3D pattern recognition
  Particle track/cluster information (tracks, showers)
Each approach uses the same set information in different order!

## Slide 12: Discussion (Pros)
Wire-Cell Imaging tells us which hits CANNOT be associated together
  Hits from different time slice CANNOT be associated together (time information)
  Hits from wires that are not crossing each other CANNOT be associated together (geometry information)
  Hits with “different” charge is UNLIKELY to be associated together (charge information)
Advantages:
  Utilize full TPC information (time/geometry/charge)
  Natural way to suppress electronics noise
  Track/shower hypothesis not used, delay the pattern recognition process  better automated
  Expected to be better for complicated topologies

## Slide 13: Discussions (Cons)
Likely worse performance for 2-plane configuration
  With 2-plane configuration, the power of the geometry information is strongly reduced
  It is important to use track/shower hypothesis early to reduce ambiguities
Stringent requirements on TPC performances
  Relative time among hits from different planes
  Charge reconstruction from induction plane
    Use this feature for calibration purpose
  Also dead channels (more sensitive to inefficiency)
High resources requirement on the memory and speed

## Slide 14: Wire-Cell Pattern Recognition
Given the 3D images, pattern recognition is performed with the track and shower hypotheses
Operations are all “local” i.e. Hough transformation, Crawler, Vertex fitting/merging …
Too many different topologies  many corner cases

## Slide 15: Wire-Cell Solve the Reconstruction Problem?
No!
  The 3D pattern recognition is still an open question  Pandora 3D pattern recognition, PMA, LineCluster …
  With recognized pattern, how to do the fine tracking?  Projection Matching Algorithm
  Energy calculation, angle determination, PID …
What’s the ultimate solution for pattern recognition?
  Human-directed pattern correction is being developed with modern web-based tools  Bee 2.0
  Deep learning?

## Slide 16: Related Technical Progress
Bee:
  Improved on memory usage and UI responsiveness and added object picking.
  Further performance improvements and a UI redesign coming.
Wire Cell:
  Excellent results from prototype noise removal on MicroBooNE data.
  Porting to Wire Cell Toolkit is underway.
  LArSoft Noise Subtraction Service Interface developed.
  WCT NSS implementation will provide first LS/WC integration.
  Will adopt service-based model for future WC imaging, etc, integration.
Brett Viren
Chao Zhang
David Adam

## Slide 17: Summary
Advantages and disadvantages of Wire-Cell approach are discussed
Wire-Cell imaging is in a good shape
More work is needed for the 3D pattern recognition
Bee 2.0 is under development
Integration with LarSoft is in progress