## Slide 1
Does the Photon Detector System design enable validation and refinement of the DUNE photon detector requirements?
Optical system
Yes, but.
Findings:
The design requirement for the PDS light yield for DUNE and protoDUNE is 0.1 pe/MeV for events at the CPA. The PDS is primarily needed for proton decay, atmospheric neutrinos, and Supernova neutrino bursts. The typical energy of neutrinos from a SN extends to below 10 MeV.
Comments:
The 0.1 pe/MeV requirement seems marginal for DUNE, and hence is a marginal design goal for protoDUNE.
Details of the SN burst trigger still need to be worked out.
Recommendations:
Efforts should continue to improve both main light collection schemes and to develop the ARAPUCA scheme. Further R&D should continue in parallel with protoDUNE toward higher-light-yield schemes.
Mechanical
Yes.
The level of design and planning prior to the shipment to CERN is impressive. It is expected that the development of the mechanical system of the photon detectors for DUNE will be similar. Therefore, lessons learned while assembling protoDUNE will be valuable for DUNE itself.
SiPM
Electronics
protoDUNE Photon Detector Design Review

## Slide 2
protoDUNE Photon Detector Design Review

## Slide 3
Are Photon Detector System risks captured and is there a plan for managing and mitigating these risks?
Optical system
Not completely.
Findings:
Estimates that predict meeting the 0.1 pe/MeV requirement also estimate 0.5% of the primary UV ends up wave-shifted and captured in the lightguide bars (Himmel, Slide 14). Actual measurements give ~0.1% (Whittington, Slides 14, 16) , with recently-achieved improvements of about factor of 2 (Mufson, Slide 13).
MicroBooNE saw huge rates of single pe.
Comments:
While this risk is identified, neither current default scheme is likely to meet the requirement.
MicroBooNE is a different experiment, but efforts to understand the high photon rate.
Recommendations:
See Charge 1.
Add MicroBooNE-like photon rates to the risk ProtoDUNE Registry.
Mechanical
Not completely
Once the detectors reach CERN, the procedures are in outline form only. These need to be fleshed out and solidified by next May when delivery is expected there. This will require the approval of CERN, a different system than the proponents have little experience with. While the proponents may understand this, these bureaucratic delays may add delays that the experiment may not be able to absorb. Also getting permission for source testing procedures at CERN needs to be obtained as quickly as possible. The time risk associated with this integration is not in the registry. Efforts should start immediately to mitigate these risks and complete and get approval for the assembly procedures at CERN as quickly as possible.
Recommendation:
Add time risk associated with integration with risk registry.
protoDUNE Photon Detector Design Review

## Slide 4
protoDUNE Photon Detector Design Review
SiPM
Electronics
35t noise in PDS
35t PDS noise pickup from TPC
ESH
From Mike Andrews: Each of the presentations addressed the relevant ESH issues and how they were addressing/mitigating them. In addition, they addressed the integration of both their home institutions ESH support and oversight, as well as, interfaces with Fermilab ESH support when necessary.

## Slide 5
Does the design lead to a reasonable production schedule, including QA, transport, installation and commissioning?
Mechanical
Yes, with two exceptions.
Findings:
Estimated production time of the radiator plates is 8 months, including initial QA, putting pressure on the schedule. .
Comments:
The design seems well in hand for production. They are to be complemented on the vigilance that has been placed on wiring mistakes as a lesson learned from the 35 T experience.
ARAPUCAs arrays lack installation plan, drawings, cable plant, etc. Extra engineering needs to be added at this point to assure that these to assure that these can be installed in the given APA design. As per the above, the existing engineering resources are going to be saturated with the transition of the detectors to CERN.
Recommendation:
Added manpower for production and testing of radiator plates is needed.
Added resources for the detailed ARAPUCA design must be identified.
SiPM
Electronics
protoDUNE Photon Detector Design Review

## Slide 6
protoDUNE Photon Detector Design Review
SiPM
Electronics

## Slide 7
Does the documentation of the Photon Detector System technical design provide sufficiently comprehensive analysis and justification for the Photon Detector System design adopted?
Optical system
Recommendation:
A study should be performed documenting the impact of PDS light yield on SN physics, specifically at values of 0.1, 0.05, 0.01 pe/MeV at the CPA.
Mechanical
SiPM
Electronics
protoDUNE Photon Detector Design Review

## Slide 8
protoDUNE Photon Detector Design Review

## Slide 9
Is the Photon Detector system scope well defined and complete?
Optical system
Yes.
  Are all Photon Detector System interfaces to other detector components: APA, cryostat and DAQ systems documented, clearly identified and complete?
Mechanical
Yes (APA, cryostat).
No (DAQ).
  Do the electronics feedthrough port and TPC integrated 3D models adequately represent the mechanical, electrical and electronic interfaces to the Photon Detector System?
Yes (TPC).
No (electronics feedthrough port).
Findings:
The PDS feedthroughs are currently being redesigned to accommodate new connectors.
  Is the cabling, power and calibration well defined and understood? Is the grounding and shielding understood and adequate?
Mechanical
Yes, with one exception.
Comments:
ARAPUCA cabling within the PD modules differs from the other schemes: cables extend across the APA and there are different numbers of SiPMs and readout channels.
SiPM
Electronics
protoDUNE Photon Detector Design Review

## Slide 10
protoDUNE Photon Detector Design Review

## Slide 11
Are the Photon Detector System 3D model(s), top level assembly drawings, detail/part drawings and material and process specifications sufficiently complete to demonstrate that the design can be constructed and installed?
Mechanical
Yes.
Photon detector mechanical system design, scope and interfaces seem to be well defined up to the flange.
Cable strain due to thermal contraction is a concern. Are the connectors and strain relief sufficient to absorb this strain?
Drawings for the photon detector bars and the SiPM holders are well advanced.
Recommendations:
Testing of cable and connector strain relief under thermal contraction are needed.
protoDUNE Photon Detector Design Review

## Slide 12
protoDUNE Photon Detector Design Review

## Slide 13
Are operation conditions listed, understood and comprehensive?
SiPM
Electronics
  Is there an adequate calibration plan?
Optical system
Partly.
Findings:
A UV-LED/optical fiber/diffuser system will have diffusers mounted on the CPAs.
Comments:
The design of the UV-LED system is nearing completion. It is more a monitoring system (devices working and stable) than a calibration system.
Recommendations:
A calibration plan, including, for example, channel-to-channel timing offsets, t0 timing for the TPC, light yield and resolution vs. 3D position, should be developed.
protoDUNE Photon Detector Design Review

## Slide 14
protoDUNE Photon Detector Design Review

## Slide 15
Are the Photon Detector System engineering analyses sufficiently comprehensive for safe handling, installation and operation at the CERN Neutrino Platform?
Mechanical
Yes.
An engineering analysis of the deflection of the channels that support the plastic sheets was done and was found to be minimal. The attachment of the channels to the APA was designed to be tolerant of APA torsion.
  Is the installation plan sufficiently well developed?
Mechanical
Partly.
The schedule is tight. Schedules exist at each partner institute. Integrated schedule was shown, but not discussed. Worry is that overlaps and double counting of staff (between institutes and at CERN) are not properly taken care off. Who is in charge of monitoring the schedule?
We discussed that CSU has a plan of sending people to CERN for installation and commissioning. What about the other institutes?
Recommendations:
Project and institute leaders to produce installation and commissioning plan with staff profiles making sure that there is no double counting of staff at the institutes and at CERN.
A plan for the coordination APA installation/testing with PD installation/testing is necessary. No plan was shown to us.
  Is the design for installation tooling adequate for installing the photon system?
Mechanical
Yes.
protoDUNE Photon Detector Design Review

## Slide 16
protoDUNE Photon Detector Design Review
Have applicable lessons-learned from previous LArTPC devices been documented and implemented into the QA plan?
SiPM
Electronics

## Slide 17
  Are the Photon Detector System quality control test plans and inspection regimes sufficiently comprehensive to assure efficient commissioning and adequate operational performance of the NP04 experiment?
Optical system
Test plans for the PD modules are highly developed and involve detailed tests after each assembly step.
From Mike Andrews: The attention to QA/QC was also addressed within the presentations. However, the Photon Detector group should continue to develop a draft of their Quality Control Plan which reference the specific QC procedures that were discussed throughout the day. This will help with consistency in understanding the process.
Mechanical
Comment:
While plans for commissioning exist, some open issues have been identified. Group should be commended to have established a rapport with protoDune safety officer at CERN. Details of installation need to be decided and planned with protoDune team at CERN
Recommendation:
Establish close contact between PD and CERN teams on installation issues.
SiPM
Electronics
protoDUNE Photon Detector Design Review

## Slide 18
protoDUNE Photon Detector Design Review