## Slide 1: 3.9 GHz components design
Nikolay Solyak (from behalf of LCLS-II design team)
3.9GHz Review, FNAL, May. 26, 2016
Speaker:

## Slide 2: Outline
3.9 GHz system functionality
Requirements
Cavity design modification
HOM design
Coupler design
Heating issues
Frequency Tuner
BPM; Gate-valve; HOM absorber.
Conclusion

## Slide 3: FLASH and XFEL - ACC39 performance
3
ACC39 routinely operates at 18.9 to 19.7 MV/m
  Capable of operation at 22 MV/m
    - Limitation set by thermal interlocks – concern about compromising HOM’s on cavities 3 & 5 (trimmed 2-post style)
Amplitude stability ≤ 2x10-5 pulse-to-pulse
Phase stability ≤ 0.003° pulse-to-pulse

## Slide 4
LCLS-II
36MV/CM

## Slide 5: LCLS-II reqs.(PRD and FRD)
Two CMs; 8 cavity / each
9 Cu plated bellows
Coupler orientation as per XFEL
~150 W heat load/cryomodule (2K)
BPM at downstream end (1.3GHz type)
No magnet
Table 3. Tuning/stability requirements
LCLSII-4.1-PR-0097-R2

## Slide 6: Cavity gradient and Q0 requirements (recent data from XFEL cavity production)
Recent XFEL production cavities (INFN-Zenon);
At 2K the all cavities have Qo in range ~(2-3)·109 (except 2)
No field slope up-to ~17 MV/m; Quench at 20-23 MV/m, VTS
No Q degradation after welding to HV
P.Perini, INFN
Risk: LCLS-II cavity (cw) requirements more stringent than XFEL (pulse) !!!
 Require Prototyping and Testing
Chart: 
| 2.1144564467938403 | 2.1847542151507953 | 2.1993784365288072 | 2.2227591205605215 | 2.2800495662949194 | 2.2862823061630215 | 2.3074993729621265 | 2.3291139240506324 | 2.4268003165391714 | 2.489851150202977 | 2.5129745971046158 | 2.5463603653473568 | 2.5648173961527734 | 2.5806451612903225 | 2.6062322946175636 | 2.6195899772209565 | 2.6436781609195399 | 2.6674398376340966 | 2.7291604865025212 | 2.7955028866605893 | 2.9677419354838706 | 3.0986864264061973 | 3.1539252656839216 | 3.2033426183844012 | 3.3022254127781765 | 3.3333333333333335 | 3.3798677443056575 | 3.4716981132075468 | 3.5127911416571207 | 3.6234738085860569 | 3.6726546906187623 | 3.7581699346405228 | 3.8032244729226949 | 3.8365304420350288 | 3.8884192730346574 | 4.1856232939035483 | 4.2553191489361701 | 4.3233082706766908 | 4.4465925567907201 | 4.6300956215400095
before 150C | 5602.9128 | 5279.183 | 5097.917 | 5142.0548 | 4053.9735 | 3599.4363 | 3545.7134 | 4516.4016 | 3881.7419 | 3290.3387 | 3299.4759 | 2775.2601 | 2469.4622 | 2216.0659 | 2275.4991 | 2203.7301 | 2419.166 | 2284.251 | 2072.9665 | 1900.4954 | 1219.5161 | 942.705 | 942.7047 | 776.8382 | 834.749 | 725.8391 | 719.8831 | 761.4148 | 588.0233 | 463.9871 | 405.3948 | 339.3732 | 388.172 | 358.8539 | 331.7895 | 209.4896 | 162.9363 | 145.743 | 120.4671 | 109.982
after 150C | 3869.2307 | 3869.2307 | 3807.2258 | 3093.3668 | 2855.4136 | 2743.3073 | 2549.0371 | 2424.1863 | 2320.0204 | 2113.6129 | 2037.4783 | 1940.9312 | 1797.0497 | 1654.3859 | 1381.2192 | 1131.2836 | 899.8842 | 797.2129 | 742.404 | 652.6629 | 562.9604 | 514.219 | 464.0023 | 398.04 | 378.1082 | 296.8642 | 314.2448 | 299.2054 | 276.2431 | 218.756 | 154.2655 | 120.8387 | 114.2158 | 109.9856 | 83.066 | 77.6369 | 70.2866 | 64.2078 | 54.9928 | 47.1367 | 42.8825

## Slide 7
FLASH-like Cryomodule Layout:
XFEL/LCLS2 Cryomodule Layout
3.9 GHz Cryomodule Options
1.3GHz like Cryomodule Layout:
ey
ex
Dex (%) ~ 6.0 %
Dey (%) ~ 24.0 %
 | 1.3GHz-like | XFEL
Δεx (%) | 6 .0 | 0.09
Δεy (%) | 24.4 | 0.15
Effect of large field asymmetry and cavity orientation
Emittance growth in 3.9 GHz system

## Slide 8: Cavity/coupler design issues and proposed modifications for LCLS-II CW operation
Cavity, bellows and Helium vessel
HOM coupler
Power Coupler
Blade-Tuner with piezo

## Slide 9
Cavity drawings: FLASH  XFEL  LCLS-II
FNAL/FLASH design
INFN/Zenon
modification
(starting point for LCLS2)
Additional modifications to meet requirements.
LCLS-II:

## Slide 10
INFN = modified FNAL design of the cavity for XFEL project. Modifications are done to simplify/improve production (Zenon) and tuning. Drawings and 3D models are available (thanks INFN team)
CW operation in LCLS-II is more severe regime for the cavity. Some minor modifications are needed to reduce risks and eliminate tuning and heating problems.
Proposed modifications in cavity RF design.
Issue #1: Frequency of lowest dipole mode trapped in coupler end of the cavity is too close to operating mode frequency, 3.9 GHz. As a result the tuning of notch frequency is difficult and 3.9 GHz frequency power leak is significant.
    Solution: Move away frequency of this mode
    Modification: Reduce beam pipe and bellow diameter from 40 to 38mm.
Issue #2 : Overheating of the HOM antenna (quench ~20MV/m at cw/VTS)
  Modification: Increase length of bump
Issue: Heating of bellow between cavities
  Modification: reduce bellow ID from 42 to 38mm
LCLS-II 3.9 GHz cavity design

## Slide 11
Reduce beam pipe diameter from 40mm to 38mm.
FLASH: Lowest Dipole HOMs. Beam Pipe Ø 40 mm and Bellows Ø 42 mm.
F = 3.992 GHz, QE = 3.6e4
F = 4.047 GHz, QE = 8.0e4
LCLS2: Lowest Dipole HOMs. Beam Pipe Ø 38 mm and Bellows Ø 38 mm.
8.35mm
Ø38 mm
F = 4.092 GHz, QE = 2.7e4
F = 4.188 GHz, QE = 7.4e3
In current design lowest mode is closer (min ~10-20 MHz vs. 100MHz in simul.) to operat. mode
Lowest dipole mode frequency shifted by 100 MHz up away from operating mode frequency.
No modification of cavity cells.
Add small conical transition between beam pipe and end cell.
  A. Lunin/T.Khabiboulline

## Slide 12: Modification of HOM coupler
Reduce penetration of antenna inside HOM to reduce heating  F-part modification
Increase wall thickness on the top of HOM can to prevent cracks and vacuum leak
To modify length of HOM feedthrough
(choice of feedthrough design: Fermilab vs. XFEL)

## Slide 13
HOM F-part modification to reduce antenna heating
G = 3.2e8 
G = 1.74e9 
  Current design HOM antenna quenches at ~20 MV/m in VTS. Expected that quench limit will even lower in CW regime at HTS and CM.
RF power dissipation on HOM antenna reduced by factor of 5.4 after modification
  A. Lunin/khabiboulline
Reduce penetration to beam pipe. Increase length of bump in F-part
Current design
Modified design
5.8mm
7.8mm

## Slide 14
HOMs Resonant Losses in the 3.9GHz LCLS-II cavity (run #1)

## Slide 15
HOM can thickness increase from 1.0 mm to 1.3 mm.
  Thickness of hat is a concern:
  Was broken when h=1mm (FLASH).
  XFEL design has thickness of 1.15 mm  one prototype cavity has a leak.
  Proposal to have 1.3mm.
1.3mm
Wall=1.3 mm
Knob pulled up by 0.1 mm
Conclusion: 1.3mm is acceptable thickness of can wall

## Slide 16: Notch filter tuning requirements
Tuning accuracy ±2MHz  P < 0.1 W
For 1.3 GHz HOM accuracy for notch filter frequency ~0.5MHz
Passband of the 3.9 GHz notch filter (left) and corresponding power radiated through HOM coupler at nominal accelerating gradient (right)

## Slide 17: HOM and pick-up feedthrough:
XFEL design (used for 1.3GHz and 3.9 GHz)
Antennaa are modified for 3.9 GHz
Field probe for 3.9 GHz (modified 1.3GHz design)
All feedthroughs are ordered in Kyocera for 24 cavities

## Slide 18
3.9 GHz: Power removed by HOM coupler
A. Sukhanov
Simulation model includes copper plated bellows between cavities
HOM frequencies have random distribution ~ 1MHz rms
Max values of R/Q for each mode is used (vs. cavity to cavity distance) – overest.
QHOM < 106 for most dangerous modes (Pmax < 7W, prob. 10-2 per 2 HOMs)
R/Q of monopole modes in cavity chain

## Slide 19: HOM antenna heating issues
Maximum power flux to HOM coupler up to 4W:
< 0.5 W – leakage from operating mode
Max power flux to 2K is 0.1W (from power dissipated in cable)
Part of this will be dissipated in cable (0.6dB/m) and will heat HOM antenna.
Heat removal from feedthrough (2K) and from the cable intercepts (5K and 50K) is essential part of design.
Choice of cable and specs is part of current activity. Use the same cables as in 1.3GHz CM, but ~1m shorter.

## Slide 20: Beamline components heating: wakes
Bunch length (sigma) | 1mm
8x (Cavities + bellow) | 135.5 V/pC
CM (8cav/9bellow/gaps) | 151.64 V/pC
Wake power (300µA; σ=1mm) is 13.65 W per CM, and only 9.5 W above beam pipe cut-off frequency
CM11
CM2
BLA
BLA
SS Beam Pipe (L=2.5m)
CM1
CM2
BLA
SS Beam Pipe (L=2.5m)
A
B
Components in 2 CM’s | Power Deposition, [W] |  | 
 | A (baseline) |  | B
 | No HOM, PC | HOM PC | HOM PC
BLA (1 or 2) | 16.2 | 13.5 | 10.5
SS tube 2.5m | 1.65 | 1.4 | 2.2
Bellows (17) | 0.36 | 0.3 | 0.4
Gate Valve (4) | 0.6 | 0.45 | 0.7
Spool (2) | 0.02 | 0.02 | 0.03
HOMC (32) | 0 | 0.5 | 0.75
FPC (16) | 0 | 2.7 | 4.1
Total power in 2 CMs ~19 W

## Slide 21: Heating of bellows from operating mode RF

## Slide 22: Chimney Power Limit
Chart: Chimney diameter, mm
| 55 | 60 | 76.199999999999989 | 101.6
Scaling from ILC cav (HTS) | 25 | 29.7521 | 47.9871 | 85.3104
HZB (ILC) | 30
JLAB-12GeV upgrade cav | 54
LCLS2-1.3GHz;19MV/m; Q=2e10 | 19.37
- Cryoload at 2K
 | Nominal parameters | Max in CM | Max power (VTS/HTS)
Eacc (MV/m) | 13.4 | 14.9 | 16.4 (+10%)
Q0 | 2.e9 | 2.e9 | 1.5e9
P/cav (W) | 14.3 | 17.7 | 28.6
LCLS2-1.3 GHz
LCLS2-3.9 GHz
Chimney the heat load limit is at least 30 W (ID= 60.2 mm (short)  73mm (long part))
Max power in individual cavity
Avrg power per cavity in CM

## Slide 23
Cavity Mechanical Resonances
(Stiffness of the Tuner = 40 kN/mm)
218.9 Hz
T#1
231.7 Hz
T#2
370.8 Hz
T#3
719.7 Hz
T#5
506.2 Hz
L#1
526.1 Hz
T#4
L#2
785.1 Hz
L#3
1076.4 Hz
T#6
865.7 Hz
k=0.75 Hz/µm
k=4.75 Hz/µm
k=0.75 Hz/µm
Chart: 
| 0 | 10 | 20 | 40 | 60 | 100
L#1 | 221.4 | 359.1 | 433.2 | 506.2 | 537.4 | 562.6
L#2 | 686.5 | 708.1 | 733.5 | 785 | 825 | 870.9
L#3 | 1022.4 | 1033.6 | 1046.4 | 1076 | 1108 | 1166
Longitudinal modes
Transverse modes
Frequencies (Hz) of Longitudinal modes L#1-L#3 vs. Stiffness of the Tuner (kN/mm)
  I. Gonin

## Slide 24
Dressed Cavity LFD and dF/dP
  I. Gonin

## Slide 25: Modification of 3.9 GHz power coupler for LCLS-II CW operation
Coupler was designed for pulse operation (P=50kW, DF=2%).
LCLS-II requirements: Pmax=2kW cw; quasi – TW regime:
    W/o modification inner conductor of warm part will be overheated up to 1000 K.
Proposed modifications:
    Shorter antenna (QL~2.7e7 vs. 1.5e6)
    Increase thickness of copper plating on inner conductor from 30 µm to 120 µm
    Reduce length of 2 inner bellows in inner conductor from 20 to 15 convolutions.
    Increase thickness of ceramics in cold window to move parasitic mode away.
Original FNAL design (FLASH & EXFEL)
Warm inner part and WG
Cold part
Warm outer part

## Slide 26
For solving the inner conductor overheating problem we propose to reduce the length of two inner bellows from 20 to 15 convolutions and to increase the thickness of a copper plating on the inner conductor from 30 to 120 microns.
Coupler THERMAL ANALYSIS
Temperature, K
Cu plating thickness, µm
SS Inner Conductor | Tmax K | Losses@50K | Losses@5K
30 µm plating | 1000 | 9.2 | 0.8
100 µm plating | 507 | 9.3 | 0.8
150 µm plating | 427 | 9.4 | 0.8
Losses (W) at 5K and 50K
T=150K
T=320K
Assumptions
Pin=2kW TW,
10μm on outer,
RRR=50; ASE,
10% roughness
ε=9.8, tan=3e-4,

## Slide 27
Main coupler antenna configuration
Beam Pipe Ø40 mm
  A. Lunin
Beam PipeØ38 mm
Nominal power coupler antenna positions in the 3.9 GHz cavity for XFEL (left) and LCLS-II (right);
QL=2.5e7

## Slide 28: Trapped modes in cold ceramic window
Two nearest trapped modes in the coupler ceramic window (simulations)
Trapped mode resonances measured in the 3rd harmonic power coupler (shift -20MHz). Transmission losses more than 3 dB, bandwidth ~ 0.5 MHz.
Set-up for ceramic measurement.
ε=9.71; tanδ=3.6E-4 (averaged over 5 modes)
The inner and outer diameters of ceramic changed symmetrically by 0.25 mm each, which shifts down by 33 MHz the frequency of nearest parasitic mode and, thus, secures of ~50 MHz isolation from the operating mode. (sensitivity of parasitic mode frequencies vs. ceramic radius is ±65.6 MHz/mm)

## Slide 29
Coupler MECHANICAL DESIGN
COMSOL solid model and mechanical boundary conditions.
Solid model of 15 convolutions stainless steel bellows with 120 μm copper plating.
Von Misses stresses for 0.5 mm longitudinal deformations of each bellows.
 | MPa/mm
Inner conductor, transverse, | 38
Outer conductor, transverse, | 45
Inner conductor, longitudinal | 253
Outer conductor, longitudinal | 98
Summary of stresses in 15 convolutions bellows
Typically copper bellow endurance limit for infinite cycles is from 83 to 166 MPa or 300 MPa for a low cycle fatigue strength CPI feed-back)

## Slide 30: Tuner SUMMARY/STATUS
Use XFEL 3.9GHz slim blade tuner (INFN) with minor modifications to meet LCLS-II requirements.
Modification introduced:
  #1 -adding fine/fast piezo tuner
  #2 replacement of the Sanyo/HD actuator on Phytron electromechanical actuator.
Note: Piezo-capsule and Phytron actuator selected for 1.3GHz tuner. Both active components passed several lifetime and rad. hardness tests
Yu.Pischalnikov, SRF Cavity Tuner

## Slide 31: INFN slim blade tuner modifications – adding Fine/Fast (piezo) tuner
Moved second ring, welded to He Vessel. to accommodate 66mm piezo-stacks
Two PI piezo-capsules (4 piezo-stacks). Will deliver more than 10kHz.
Even one piezo can deliver required fine tuning stroke >1kHz.
Yu.Pischalnikov, SRF Cavity Tuner
Evgueni Borissov
INFN (EuXFEL) tuner

## Slide 32: BPM and HOM absorber
Concept: Use 1.3GHz beam line components (ID=78mm) in transition between cavity string:
BPM,
Gate-valve,
Beamline HOM absorber (~10 W)

## Slide 33: Conclusion
Design is completed and Technology of all components exist (based on FNAL/XFEL/INFN).
To meet LCLS-II requirements cavity, coupler, HV and tuner designs are modified to reduce risks and improve performance at cw operation.
Simulations and studies for the dressed cavity and beamline components are done to prove proposed modifications and predict performance in LCLS-II cryostat.
Prototypes of Cavity and Auxiliaries (Tuner, main coupler, magnetic shielding, feedthroughs,…) will be tested in HTS (DV) before major procurement starts.

## Slide 34
Thanks:
T.Khabiboulline, I.Gonin, A.Lunin, S.Kazakov, R.Stanek, C.Ginzburg, E.Harms, H.Edwards, C.Grimm, M.Foley, Y.Pischalnikov, T.Arkan, A.Rowe, A.Grassellino, G.Wu, O.Prokofiev, J.Ozelis, A.Saini, J.Kaluzny, S.Yakovlev, M.Hasan, T.Peterson, Y.Orlov, Y.He, E. Borissov, …

## Slide 35: Back-up slides

## Slide 36: LCLS-II 3.9GHz Cryomodule, (F10014857 in Team Center)
XFEL cavity orientation (z-rotation:180 deg)
8 - 3.9GHz cavities
Power couplers from both sides
2-coldmass supports
Interconnection sliding bellow
38” OD vacuum vessel pipe
One thermo shields:50K
5K intercept

## Slide 37: LCLS-II. 3.9GHz Cavity String (F10014812)
3.9 cavity Style-A
3.9 cavity Style-B
Gate Valve
Blade tuner
Spool piece
Spool piece
and BPM

## Slide 38: 4.8
750
Comparison
3.9 GHz vs. 1.3 GHz:
Iris Aperture: 30mm vs. 70mm (ratio 2.34)
Ep/Eacc ; 2.26 vs. 2.0 (13% higher)
Hp/Eacc(mT/MV/m) 4.86 vs. 4.26 (14% higher)
R/Q (Ohm) 750 vs. 1000
BCS resistance ratio (f2) (9 times higher)
FLASH

## Slide 39
Vendor | Times Microwave |  |  | Huber+Suhner |  |  |  | Gore Type 42
Cable Type | TFlex-401 | TFlex-401t | SFT-304 | 32022 | 32039 | SF229 | 3288LM (SF329) | Gore Type 42
Inner Cond OD [in] | 0.0641 | 0.062 | 0.062 | 0.0359 | 0.06 | ? | ? | 0.089
Outer Cond ID [in] | 0.208 | 0.185 | 0.185 | 0.106 | 0.191 | ? | ? | 0.196
Outer Cond OD [in] | 0.249 | 0.227 | 0.227 | 0.109 | 0.20 | ? | ? | 0.225
Cable OD [in] | 0.27 | 0.250 | 0.250 | 0.144 | 0.250 | 0.20 | 0.20 | 0.29
Material of Conductor | CuAg | CuAg | CuAg | CuAg | CuAg | CuAg | AlCuAg | CuAg
Dielectric | PTFE (εr=2.04) | ePTFE | ePTFE | Microporous PTFE | Extruded TFE | Low density PTFE | Microporous PTFE | ePTFE (εr=1.4)
Velocity % | 69.5 | 69.5 | 76 | 76.3 | 70.3 | 82 | 82 | 
Attenuation [dB/m] at 1 GHz | 0.26 | 0.22 | 0.22 | 17dB/100ft at 2GHz | 12dB/100ft at 2GHz | 0.18 | 0.18 | 0.3
Outer Braid | CuAg | CuAg | CuAg+ Polymide/Al+CuAg | CuAg+ Polymide/Al+SS | CuAg+ Polymide/Al+SS | Polymide/Al+CuAg | Polymide/Al+AlCuAg | CuAg+ Mechanical Shield
Jacket Material | FEP | TEFZEL 750 | FEP | FEP | FEP | FEP | ECTFE | TEFZEL
Temperature Rating [C] | -65 to +125 | -55 to +200 | -55 to +200 | -55 to +200 | -55 to +200 | -55 to +125 | -65 to +165 | -100 to 150
Shielding | >100 dB | >100 dB | >110 dB | >110 dB | >110 dB | >90 dB | >90 dB | >110 dB
Radiation Resistance [Rad] | 1e5 | 3e7 | 1e5 | 1e5 | 1e5 | 1e5 | 2e8 | 1e8
Material of Connectors | Brass | Brass | Brass | Brass | Brass | Brass | Brass | Be Cu
Price of 3m long assemblies(min is 250) | $147 | $175 | $157 | $146 | $192 | $266 | $341 | $756

## Slide 40: Lead Intercepted Power (3.9 GHz)
Power Flow [W] | 2K | 5K | 50K | 300K
0 | 6.30 | 189.88 | 287.86 | -484.04
1 | 18.06 | 217.86 | 358.44 | -394.68
2 | 29.84 | 246.19 | 435.51 | -298.46
3 | 41.63 | 274.95 | 520.27 | -194.23
4 | 53.49 | 304.20 | 614.21 | -80.58
5 | 65.44 | 334.01 | 719.21 | 44.26
6 | 77.43 | 364.58 | 837.66 | 182.56
7 | 89.46 | 396.08 | 972.68 | 337.22
8 | 101.50 | 428.79 | 1128.35 | 512.10
9 | 113.61 | 462.98 | 1310.21 | 712.38
10 | 125.80 | 499.07 | 1525.91 | 945.19
Narrow Leads
Power Flow[W] | 2K [mW] | 5K [mW] | 50K [mW] | 300K [mw]
0 | 9.27 | 164.76 | 242.83 | -416.87
1 | 21.91 | 193.01 | 313.60 | -326.02
2 | 34.61 | 221.87 | 393.03 | -226.41
3 | 47.43 | 251.44 | 483.14 | -116.22
4 | 60.39 | 281.94 | 586.51 | 6.86
5 | 73.47 | 313.74 | 706.51 | 145.86
6 | 86.67 | 347.22 | 847.86 | 304.90
7 | 100.05 | 383.02 | 1017.10 | 489.75
8 | 113.67 | 422.00 | 1223.63 | 708.57
9 | 127.78 | 465.89 | 1481.52 | 973.22
10 | 142.70 | 517.64 | 1812.94 | 1301.92
Wide Leads

## Slide 41
Wide cooling leads
(45mm x 2.5x10 mm2)
Narrow cooling leads
(45mm x 2.5x2.5 mm2)
Thermal simulation for HOM cable (TFlex401) Pantenna= 9uW (140mT with modified design, 63 mT with original design)
Cable is OK up to 9 W input power flow
(80°C cable limit).
zoom
M.Hasan/T.Khabiboulline

## Slide 42
TFlex 401 cable after 500 MRad γ-radiation in Sandia (7 days)
Modification: FEPTefzel for outer conductor
New antenna design has better thermal performance
Preliminary analysis shows that the TFlex-401t/Huber-SF329 cable used for the 1.3GHz cryo-module will work for up to 8W power flow out of the HOM ports for the 3.9GHz cryo-module
Wide Leads are critically needed
Conclusion
Y.Pischalnikov/T.Khabiboulline/M.Hasan