## Slide 1: Protodune Cosmic Ray tagger (CRT)
Camillo Mariani
ProtoDUNE DAQ Review
November 3rd and 4th

## Slide 2: Introduction
CRT motivations
  System overview and trigger signals
    CRT Readout
      CRT Event Builder

## Slide 3: ProtoDUNE CRT
System will be positioned in the front and back of the TPC
identify muon present in beam halo
tag this muon send trigger info to TPC
System will also have some panel on top of the TPC
Muon veto, send trigger info to TPC
Trigger will be generated as an OR of the X and Y panels
Send to the TPC trigger board within 500 ns.
Hit info or ADC info in separate data stream.
CRT modules consist of two layers of 64 scintillator strips with WLS fibers connected to a single multi-anode PMT
CRT Readout Electronics

## Slide 4: System Overview and Trigger Signals
DAQ
Each PMT board:
Readout 64 channels - provide hits or ADC info
  Hits processing require 120 ns
  ADC processing require 32 ms
Board trigger does not know about other boards
Trigger board:
Collect info from all PMT boards
Provide hit info pattern (through DAQ)
Form a trigger signal (based on single board info)
  2 trigger out available
    Geometrical overlapping modules in < 500 ns
    OR of all modules in < 500 ns
Data stream contains 32 bit timestamp can be used for data merging offline, only when a proper bit is asserted in the main data stream.
CRT
Electronics
Module hit Pattern
Data to CRT DAQ
CRT front-end
readout board N
CRT front-end
readout board 1
PMT data
to CRT DAQ

## Slide 5: CRT Readout
Launches independent threats (C++) to manage each USB board
  USB communication using libusb
Separate CRT run control process (perl/python) connect to the ProtoDUNE run control via TCP/IP sockets
  CRT run control communicate with the USB streams using message queues
Binary data are written independently for each of the USB stream on disk
CRT Readout
control thread
ProtoDUNE Run Control
CRT Run Control
CRT USB board thread

## Slide 6: CRT Event Builder
CRT Event Builder written in C++ and designed to:
  Read raw data from the CRT DAQ
    Independent, unsorted data stream for each of the USB, consisting of data packets from individual CRT modules
    Compute and apply pedestal calculation
    Apply offline thresholds
    Time-order hits within individual data USB stream
    Merge all USB data stream in time-order, grouping them into CRT events
CRT Readout
control thread
ProtoDUNE Run Control
CRT Run Control
CRT USB board thread

## Slide 7: Component testing
All components tested already
Component that need to be produced will be visually inspected after production and then tested
Plan to have a full electronic test stand at Virginia Tech

## Slide 8: Risks
No rick identified for now

## Slide 9: Conclusion
System was used in 3 different experiments - did not cause major issues.
Have years of running and extensive commissioning experience
Full test stand planned
Detector is very new to ProtoDUNE so lots of specific details of the system needs to be addressed
  i.e. cable length need to be decided
  location of the electronics boards for triggering
We will use similar triggering and data margining schemes as the beam instrumentation.