## Slide 1: A New Concept for High Power RF Couplers
Dr. Chen Xu
On behalf of SRF group

## Slide 2: Outline
1. The TEM coupler and its limitation.
2. The TE11 mode coupler
  RF design
  Thermal design
3. The practical concerns
4. Summary

## Slide 3: Outline
1. The TEM coupler and its limitation.
2. The TE11 mode coupler
  RF design
  Thermal design
3. The practical concerns
4. Summary

## Slide 4: Attenuation rate and loss on TEM coupler
The impedance is related to the radii a and b
The loss on the inner and outer conductors are inversely proportional to the radii.
Epeak is not reaching the breakdown field.
The most critical point of couplers design is the inner conductor cooling.

## Slide 5: Limitation of the Conventional TEM coupler
Weakest design point is the inner conductor cooling.
Considering the water and Cu interface in 1 Dimension, the maximum power allowed is based on the water temperature drop. when 100ºC is maximum, the maximum loss can be obtained.
Based on a certain k ~ 300W/m2/K (pipe radius dependent), the maximum water cooling capability (line density) is 942W/m the water pipe radius is 5mm.
We want to optimize the coax line by using a/b as the free parameter. When impedance is 75Ω, the loss is smallest. The loss rate on inner conductor (line density) is 7W/kW/m.
TEM couplers has a large RF loss in the inner conductor, that
can lead to a maximum power operation.
Q: heat flux W/m2, k: Kapitza conductivity ΔT: interface temperature drop

## Slide 6: Outline
1. The TEM coupler and its limitation.
2. The TE11 mode coupler
  RF design
  Thermal design
3. The practical concerns
4. Summary

## Slide 7: Characteristics of TE11 coaxial mode
The TE11 mode could be used for the high power coupler applications.
The loss on the inner and outer conductor are proportional to the radii ratio.
The inner conductor loss can be dramatically reduced but the total RF loss does not increase.
Reduced RF loss on the inner conductor can minimize the design challenge of cooling. In this design, we plan to not use water cooling.

## Slide 8: The TEM/TE11 coaxial section optimizations
The inner and outer conductor loss on the TE11 and TEM modes.
With a cutoff frequency, the loss on TE11 on the inner and outer conductor are proportional to the radii ratio.
The loss reduction on inner conductor reduce the design challenge on inner conductor cooling.
Increase the maximum RF power delivery.

## Slide 9: RF windows design.
A standard sapphire window is added in the center with two choke structure on either side of the inner and outer conductor. This is a standard technique used in various of high power coaxial coupler.
We can avoid using the choke structure, because it might increase the possibility of multipacting. We choose to use a smooth transition to match the RF power without reflection.
In some cases, we can put windows elsewhere.
Should delete the “.” in the title

## Slide 10: How to convert from Klystrons: mode convertor
The output from a RF source is usually a standard rectangular waveguide.
The RF power is delivered in the TE10 mode which is the fundamental mode of a rectangular waveguide.
It is convenient transfer the RF power from TE10 rectangular mode to TE11 mode coaxial antenna, which we discussed above. Both modes are dipole polarized modes.

## Slide 11: Coupler assembly setup
The coaxial coupler with TEM mode utilizes the standard door knot convertor, while the coaxial coupler with TE11 mode utilizes the designed convertor above.
To conveniently located the waveguide, we use an E-bend rectangular waveguide which is commercially available.
A standard H bend is added.
Full assembly is shown.
Frequency: 1.3 GHz | S:1:1 (TE10) | S:2:1 (TEM) | S:2:2 (TE11_V) | S:2:3 (TE11_H)
S:1:1 (TE10) | -24.9 | -38.3 | -0.0244 | -62
S:2:1 (TEM) | -38.3 | -0.0134 | -38.3 | -86.7
S:2:2 (TE11_V) | -0.0244 | -38.3 | -24.9 | -62.3
S:2:3 (TE11_H) | -62 | -86.7 | -62.3 | -57.2

## Slide 12: Outline
1. The TEM coupler and its limitation.
2. The TE11 mode coupler
  RF design
  Thermal design
3. The practical concerns
4. Summary

## Slide 13: Thermal Anchor without break RF performance
One feature of the TE11 coaxial mode is that, the horizontal plane is a perfect electric boundary condition.
  Therefore, we can insert a metal plate without compromising the RF performance.
  This plate can be used to thermal anchor the temperature of the inner conductor.
  The temperature of inner conductor will be reduced to a low temperature and further reduce the dynamic loss.
  However, this flat plate will introduce some more dynamic loss itself.
Such feature is not available on TEM couplers, i.e, inserting a flat plate will destroy the TEM field pattern.

## Slide 14: The cooling scheme and anchors
The geometry setup for the thermal anchors and the materials setup.
  Use the same materials properties.
    Stainless steel with Cu plating. The plated thickness is 10um. Windows are polycrystalline Sapphire, and the loss tangent is 10-4.
  The thermal anchors locations are the same as the cERL/Berlin Pro couplers.
  2K+ 5K+70K and the bellow is can be added in the air side. (not see RF)
  Materials properties are heritage from the TEM couplers. (TTF3, cERL coupler)
  The inner conductor is cooled by the window and the end plate. Comparable static loss with TEM couplers. No active water cooling is necessary.
Dynamic loss (W) | TEM | TE11
2K | 0.1022 | 0.0715
5K | 0.7451 | 1.0438
70K | 4.4455 | 4.9163
300K | -13.1693 | -6.0317
Water Cooling | 7.8764 | N/A

## Slide 15: Dynamic loss Comparison of TEM and TE11 couplers
When two couplers deliver 200kW travelling wave, the dynamic loss on the inner conductor are 335.04W and 93.59W and the outer conductor are 162.62W and 346.9W, while the RF window volume loss are 2.49W and 2.07W for TEM and TE11 modes respectively when the whole couplers are at room temperature.
RRR helps reduce the outer conductor loss,
since the outer conductor is well cooled.
The total loss will be much smaller and no
Active water cooling.
Black body radiation:Q = εσA(T4 -T04 )
  where ε is the emissivity (1×10-2), and σ is Stefan–Boltzmann constant (5.670367×10−8 W/m2/K4) and A is the surface area (0.025m2), and T and T0 are the tip and environment temperatures.
  Now we estimate the black body radiation for this TE11 couplers. To transmitted 115kW and 200kW RF power, the tip temperatures reduced to 337K and 421K. Therefore, the max emitted power increased to 0.41W and 1.01W respectively.
The total RF loss on TE11 couplers is around >40% of the TEM couplers.
Dynamic loss (W) | TEM (115kW) | TEM (200kW) | TE11 (115kW) | TE11 (200kW)
2K | 0.656 | 0.871 | 0.772 | 1.024
5K | 3.025 | 3.943 | 5.877 | 8.338
80K | 15.994 | 22.376 | 111.932 | 166.615
300K | 165.685 | 314.692 | 116.484 | 228.806
Water Cooling | 293.496 | 488.436 | N/A | N/A
Total Loss | 478.856 | 830.317 | 235.064 | 404.783

## Slide 16: Outline
1. The TEM coupler and its limitation.
2. The TE11 mode coupler
  RF design
  Thermal design
3. The practical concerns
4. Summary

## Slide 17: Coupling to a Cavity
When the beam loading is high, the external Q of couplers are usually small to match the loaded Q of the cavity. Typically, external Q is around 104~105.
Moreover, the couplers should have limited beam kick by reducing the coupler insertion length.
The TE11 couplers have at least 10 times higher coupling capability than TEM couplers at the same invasive length.
Compared with waveguide, the TE11 coupler can be a variable couplers.
Compared with TEM couplers, the TE11 coaxial coupler requires smaller insert length.
Similar coupling strength as waveguide, but variable with center conductor.

## Slide 18: Variable coupling and Multipacting simulation
Track3p code simulates the possibility of multipacting.
We use the second yield curve from an Oxygen-free Cu and Sapphire windows to conduct this simulation at different forwarding RF power levels. No Multipacting was found.
On customized elliptical bellow can be added on the outer conductor and make the center conductor moving respected to the cavity.
The center conductor and the RF window are moving along with the mid part of the outer conductor when the coupler is inserted or retracted respected to the cavity.

## Slide 19: Summary
In this presentation, we propose a new type of TE11 couplers for high power SRF Linac. This new coupler uses coaxial TE11 mode to transmit RF power and it could deliver higher forward RF power without complex water cooling system.
If a higher RF power is needed, this coupler needs small active cooling capability for the inner conductor to minimize the cyromodule engineer effort.
It has >40% of total RF loss at the same forward RF power level with a conventional TEM coupler and the static loss is comparable to a conventional TEM coupler.
This TE11 coaxial coupler could be used as a variable coupling antenna without an obvious multipacting issue.

## Slide 20: Acknowledgements
I thank to Ilan Ben-Zvi and Tianmu Xin from BNL, Haipeng Wang from Jefferson National Accelerating Facility, Liling Xiao from SLAC for the useful discussions.
Next step
Mechanical design with stress and bellow if needed.
Prototype.
Commissioning with a cavity.