## Slide 1
Zhihong, Zheng 02.23.2017
Multipacting Free Coupler Design and Commissiong for FRIB

## Slide 2: Outline
Motivation of FRIB FPC optimization - severe multipacting observed
Failure of magnetic coil trial to suppress multipacting in FPC
Analytical model to reveal multipacting mechanism at FRIB FPC and potential mitigation method
Structural optimization of FRIB FPC and further upgrade before prototype
Comparison tests between original and optimized coupler (MPF)
Summary

## Slide 3: Motivation of FRIB FPC optimization
Due to heavy multipacting, coupler input power was stopped at 2 kW CW, while operating power was up to 5kW CW.
With magnetic coil we can suppress multipacting when cavity is detuned.
Magnetic coil did not help while cavity was on resonance (Failed).
Magnetic coil
Current probe
probe
coil
Multipacting current vs. peak RF power (pulse) while cavity is detuned.

## Slide 4: Questions after Cryomodule Test
Whole coupler
Question 1: What leads to multipacting in coupler?
  Simulations shows that it is caused by the coaxial structure in coupler
  The multipacting appears at region of peak transverse electric field
Question 2: Why can we suppress coupler multipacting by magnetic coil when cavity is detuned, but failed when it is on resonance?
  When cavity is on resonance, coupler is short at transmission end
  When cavity is detuned, coupler is open at transmission end
Take away bellows
Take away taper
Transmission end.
antenna coupler with strong over coupling

## Slide 5: Why Magnetic Coil Method Does Not Work?
Case | Node 1 | Node 2 | Node 3
Cavity detuned (open circuit) | Epeak(weak) | Bpeak | Epeak(heavy)
Cavity resonance (short circuit) | Bpeak | Epeak(heavy) | Bpeak
Multipacting appears at region of peak transverse electric field ().

## Slide 6: Analytical Model for Multipacting
Developed model[1] to predict RF power at which coupler has two-point multipacting:
(1)
Impact energy of electron:
(2)
Coaxial couplers | Operating power | Predicted P1 | Predicted K1 | Prediction | Multipacting test results
SNS coupler | 0~550 kW (pulse) | 898 kW | 13.5keV | No | No problem
Dewar test antenna | 0~0.2 kW (CW) | 5 kW | 1.49keV | No | No problem
FRIB HWR coupler | 0~5 kW (CW) | 2.1 kW | 0.679keV | Yes | Heavy (2~6.5 kW)
Table 1: Model verification by three different coaxial couplers (Yes=has multipacting, No=no multipacting)
P1 is more sensitive to structure.
X
√
X
√
Increase coupler impedance to increase P1 to avoid multipacting.
[1] Z. Zheng et al, “Prediction and Suppression of Two-Point 1st Order Multipacting”, Nucl. Instr. Meth. Phys. Res. A 735 (2014) 596-601
X
√
√
X
X
Notes:   where , are the inner and outer conductor radius, e is electron charge, m is electron mass, ω is RF circular frequency, n is the order of two-point multipacting, η is the wave impedance in vacuum (377Ω), A is 1 for traveling wave and 0.25 for standing wave (superposition theorem).
  where 𝑟_1, 𝑟_2 are the inner and outer conductor radius, e is electron charge, m is electron mass, ω is RF circular frequency, n is the order of two-point multipacting, η is the wave impedance in vacuum (377Ω), A is 1 for traveling wave and 0.25 for standing wave (superposition theorem).

## Slide 7: Draft of MPF Coupler Design
  Taper is made near the 3-3/8’’ flange which connects coupler to cavity.
λ/4 match section impedance:
VSWR ≈ 1.08 for 75Ω load at transmission end.
Node 1
Node 2
Node 3
Baseline coupler: R=50Ω,r2=21mm,r1=9mm.
P1_node2=17kW.
P1_node3=14kW.
P1_node1=7kW.
Notes: Based on the analysis of cryomodule test, it is known that heavy multipacting will appear at node 2 while cavity is on resonance.

## Slide 8: Multipacting Comparison between Original and MPF Coupler
Normalized multipacting intensity
Coupler RF power (standing wave in coupler) /kW
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Baseline coupler for cavity detuned | 0.026025 | 0.20652 | 0.6354 | 1 | 0.68683 | 0.41211 | 0.25839 | 0.19006 | 0.13739 | 0.11894
Baseline coupler for cavity resonance | 0.011491 | 0.33454 | 0.51559 | 0.36335 | 0.27547 | 0.2443 | 0.21888 | 0.20426 | 0.20058 | 0.1587
Optimized coupler for cavity detuned | 0.010444 | 0.010342 | 0.012764 | 0.022034 | 0.070342 | 0.094099 | 0.064286 | 0.036335 | 0.02087 | 0.015839
Optimized coupler for cavity resonance | 0.0055901 | 0.0058696 | 0.0068012 | 0.0075 | 0.0082919 | 0.0095031 | 0.010016 | 0.0096894 | 0.011646 | 0.01677
With beam, operating power=2.5kW(standing wave)+2.5kW(traveling wave). It is 3.125kW equivalent standing wave power.
Without beam, operating power=2.5kW standing wave.
MPF coupler should be MP free in the operating power range!
Simulated by CST.
Notes: Multipacting comparison between baseline coupler and optimized one. These four curves are from CST simulations, number of primary electrons are set the same. Multipacting intensity stands for the total number of secondary electrons in 8 RF cycles. Peak value is normalized to 1.

## Slide 9: Further Upgrade of the New MPF FPC Prototype
To further improve its performance, we decided to remove the choke and optimized the structure to keep the RF window away from electron impact.

## Slide 10: Automatic Conditioning System
Since multipacting conditioning is time consuming, an automatic conditioning system based on PI algorithm was developed to improve the conditioning efficiency and save effort. Several interlocks were applied in order to keep the system safe when running 24 hours without people onsite.

## Slide 11: Original FPCs Room Temperature Conditioning
40 hours RF condition to reach 20kW 20% duty cycle.
Heat Load ≈ 80W!
The Evidence for MP.
RF power = 8kW

## Slide 12: MPF FPCs Room Temperature Conditioning
Toshiba MP-free FPC-001
Toshiba MP-free FPC-002
Even though we had a spark inside the resonator during the conditioning, it took only 18 hours to achieve 20 kW 20% duty cycle. Multipacting-free design saved 22 hours conditioning time compared to original design couplers.
More importantly, there was no heating problem on multipacting-free couplers which was an evidence for multipacting absence.

## Slide 13: Following Tests
Another 8 original FPCs were tested after the comparison test. As a summary for the original design of the couplers, the average conditioning time for one run was about 60 hours, only three of ten couplers had no heating problem after RF conditioning.
In addition, one of the multipacting-free prototypes was tested with HWR53 cavity at 2K in a vertical Dewar as a final integrated validation test, which was a success.

## Slide 14: Summary
Comparison tests proved that MPF coupler significantly reduces the conditioning time compared with original-design coupler.
After comparison tests, we did conditioning for the rest of original-design couplers, only 3 of 10 has no heating problem.
As a result, FRIB decided to use MPF-FPC design as the fundamental power couplers for more than 200 HWR cavities.

## Slide 15
Thank You !

## Slide 16: Backup Slides
Simplified model to get an multipacting principle
  If we assume E(r) is constant along the radius to get an estimation, thus
    Integrating twice and imposing the condition that s(0) =0 and . The electron’s position at time t:
    Condition for two point MP occurs:
    Since ; Then we get the RF power at which coupler has MP:
      =0.5 (For TW, A=1; for SW, A=0.25;)
      (Z: impedance; f: frequency)
      Since ;
      So impact energy at

## Slide 17: Backup Slides
Figure 12: Comparison of the Eq. (1) results (orange line) and E. Soersalo’s scaling law (green line) for two-point 1st order multipacting in the FRIB coupler, as we change the impedance. Outer radius is 21mm.
E. Somersalo’s scaling law:
Self-derived principle:
(1)
(2)
Chart: Threshold power vs. coupler impedance
| 182.67134626340538 | 141.08251542980867 | 116.7546089433188 | 102.57128225946497 | 99.493684596211949 | 86.105071517359363 | 78.243375772975099 | 75.165778109722083 | 65.916737320086582 | 57.904853762615225 | 52.871964723773104 | 50.837871623232218 | 44.516240683762639 | 38.797629895503142 | 33.57694727612536 | 28.774384815713177 | 24.327906486489862 | 20.188334197272773 | 16.316022929018505 | 12.678545620032418 | 9.2490407896355009
Eq. (1) | 0.78081 | 0.8039 | 0.79217 | 0.76944 | 0.76236 | 0.71981 | 0.68368 | 0.6667 | 0.60387 | 0.53142 | 0.47475 | 0.44889 | 0.35541 | 0.24955 | 0.12929 | -0.0082892 | -0.16736 | -0.35414 | -0.57838 | -0.85647 | -1.2193 | -1.736
scaling law | 1.4664 | 1.242 | 1.0776 | 0.9651 | 0.93864 | 0.81311 | 0.72995 | 0.69509 | 0.58104 | 0.46848 | 0.3895 | 0.35543 | 0.24009 | 0.12066 | -0.0048643 | -0.13893 | -0.28474 | -0.44675 | -0.63172 | -0.85081 | -1.1248 | -1.4999
Figure 13. Multipacting bands in coaxial line

## Slide 18: Backup Slides
Increase impedance by enlarging outer radius. Inner radius=9mm.
Chart: Threshold power vs. coupler impedance
| 182.67134626340538 | 141.08251542980867 | 116.7546089433188 | 102.57128225946497 | 99.493684596211949 | 86.105071517359363 | 78.243375772975099 | 75.165778109722083 | 65.916737320086582 | 57.904853762615225 | 52.871964723773104 | 50.837871623232218 | 44.516240683762639 | 38.797629895503142 | 33.57694727612536 | 28.774384815713177 | 24.327906486489862 | 20.188334197272773 | 16.316022929018505 | 12.678545620032418 | 9.2490407896355009
Eq. (1) | -3.3787 | -2.4018 | -1.7986 | -1.3479 | -0.98025 | -0.66482 | -0.38509 | -0.13124 | 0.10307 | 0.32218 | 0.52916 | 0.7263 | 0.91531 | 1.0975 | 1.274 | 1.4457 | 1.6131 | 1.777 | 1.9377 | 2.0957 | 2.2513 | 2.4049 | 2.5566 | 2.7066 | 2.8553 | 3.0027 | 3.1489 | 3.2942 | 3.4385 | 3.5821
scaling law | -3.0476 | -2.3008 | -1.8038 | -1.4092 | -1.0706 | -0.76749 | -0.48883 | -0.22808 | 0.018988 | 0.25527 | 0.48282 | 0.70316 | 0.91745 | 1.1266 | 1.3313 | 1.5321 | 1.7295 | 1.9239 | 2.1157 | 2.305 | 2.4921 | 2.6773 | 2.8607 | 3.0424 | 3.2226 | 3.4015 | 3.579 | 3.7554 | 3.9306 | 4.1048
Figure 14: Comparison of the Eq. (1) results (orange line) and E. Soersalo’s scaling law (green line) for two-point 1st order multipacting in the FRIB coupler, as we change the impedance. Inner radius is 9mm.

## Slide 19: Backup Slides
These three couplers are all 580mm long and simulated in open circuit .They all have multipacting at the same position(L≈0.47m).
Wave length
  λ=c/f=0.93m
  So, λ/2=0.466m ≈L
Conclusion: The FRIB coupler’s MP is caused by its coaxial structure, MP occurs at the peak E-field
(1) Coupler with bellow and taper
(2) Coupler with taper and without bellow
(3) Coupler without bellow and taper
L≈0.47m

## Slide 20: Backup Slides
SEY used for coupler

## Slide 21: Backup Slides
For cavity detuned case, we found that small magnet will increase multipacting. But multipacting disappeared when coil current was around 5A. This phenomenon is also found in CST simulation.
Explanation: small magnetic field will increase impact angle , thus SEY increases. Large magnetic field will change resonance trajectory, thus multipacting is suppressed.
Coil current /A
Normalized multipacting
Figure 16. Multipacting vs. coil current. Each case is simulated in 5 RF cycles. Peak value is normalized to 1.
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 10 | 12
 | 0.71015 | 0.76635 | 0.94976 | 1 | 0.55287 | 0.21619 | 0.13793 | 0.1393 | 0.14764 | 0.13803 | 0.099664
Why small magnetic field increase multipacting for cavity detuned case?
Figure 15. Three mechanism for SEY

## Slide 22: Backup Slides
Model of True Secondary Yield

## Slide 23: Backup Slides
Y
X
θ1 =tan-1(Vy/Vz) =tan-1(0.75/1.7) =24 °; θ2=tan-1(Ly/Lz) =tan-1(3mm/21mm) =8 °; impact angle: θ=θ1-θ2=16°
K2/K1=1 ≤ (L2/L1)^2≤(21.4mm/21mm)^2=1~1.04
K1=0.68keV, K2=0.68~0.71keV (in simulation, K2≈0.8keV, see picture left up)
Without coil, K1=0.68keV, θ=0°: SEY=1.78
Coil current=3A, K2=0.68~0.71keV, θ=16°: SEY=1.82~1.83
MP intensity ratio=(1.78/(1.83~1.82))^10≈0.8 (about 0.7 in simulation, see figure 4)
Small magnetic field increases MP
Simulated by CST.

## Slide 24: Backup Slides

## Slide 25: IC and OC are Beautiful
The inner conductor is very beautiful, no stain marks and no electron bombarding spots.
Tapered area of outer conductor (close ceramic, vacuum side) is also beautiful but found very light electron bombard spots (maybe ten spots), which is not serious.

## Slide 26: One Electron Bombarded on Gasket

## Slide 27: Brown Spots around RF Window and Brazing
It doesn’t look like electron bombarded mark.
Conclusion: we could not find a big sparking mark in the coupler vacuum side. Big spark mark probably is inside conditioning box.

## Slide 28: MPF FPC Conditioning with New Box

## Slide 29: Original FPC Conditioning with New Box

## Slide 30
THANK YOU!