## Slide 1: JLab CM Production
Bob Legg, Ed Daly
For the Jlab Team

## Slide 2: Contents
Cryomodule Assembly at JLab
  Introduction
  Overview
  Features of Cryomodule Assembly at JLab
  Production processes
  Summary

## Slide 3: Introduction
Jefferson lab has a long standing core competency in cryogenics and superconducting radio frequency (SRF) systems.
A partial list of large cryomodule construction projects to date at Jefferson Lab include:
Original CEBAF construction C20 CEBAF 42.25 Cryomodules
  42 Cryomodules plus two Cryo-units, 338 Five (5) cell cavities
    During peak Production 2 Cryomodules per month for 18 months
    C50 refurbishment Program started in 2006 (12 Cryomodules as of 2016)
SNS Cryomodules, fabrication and test of 23 Cryomodules Built at JLAB
  11 Medium Beta , and 12 High Beta
12 GeV , 10 Cryomodules
    using a new 7 Cell Cavity design “Low Loss”, new tuner, HOM couplers and probe feed through, new RF window design
    Using new cavity processing methods
LCLS-II Construction of 19 Cryomodules for SLAC currently in progress

## Slide 4: Overview of Cavity/Cryomodule Process at JLab
Commissioning at SLAC
Install Cryomodules in Accelerator, cool to 2 K
Weld & certify leak tight , pressure test
check Controls,
Gradient & Dynamic Heat Load - Qo
Supplier
Partners
LCLS-II 1.3 GHz Cryomodule
Courtesy Chi-Chang Kao, SLAC
JLAB SRF Facility
Cavity String Assembly & Leak Test
Assemble Cavity String -Class 100 Clean Room
Cavity /Helium Vessel Prep. & Test
VTA RF Test in liquid Helium @ 2 K
Cryomodule Test in “Test Cave”
Cryomodule integrity @ 2 K
Tuners - Range, Hysteresis, & Resolution/ Sensitivity
Cavities for Gradient & Dynamic Heat Load Qo
Cryomodule Assembly
Instrumentation & Wiring
Tuners, MLI– Multi Layer Insulation,
Cryogenic Circuits , magnetic shielding, alignment
Super Insulation Cabling & Shield
Vacuum Vessel & Final Alignment
Install Cryogenic Supply Interfaces
  Horizontal Test Preparation
  Pressure Test & Leak Check (vacuum)
Receiving in SRF Inventory
Mechanical Inspection CMM
Cryomodule shipping to SLAC
JLAB support for installation of first 3 Cryomodule
 | Component | FNAL | JLAB | SLAC
Cavity String | Niobium (Prototype) - existing cavities | NA |  | 
 | Niobium (Production) | X |  | 
 | Cavities (Prototype) - existing cavities | NA |  | 
 | Helium Vessels (Prototype) | X |  | 
 | Cavities w/Helium Vessels -VTS Ready (Production) |  | X | 
 | Cavity Feedthroughs |  | X | 
 | Cavity Flanges & Assoc. Hardware/Seals (VTS & HTS compatible) |  | X | 
 | Fundamental Power Coupler (FPC) |  |  | X
 | Cavity String Interconnecting Bellows |  | X | 
 | Cavity String Assembly Hardware & Seals | X |  | 
 | SC Magnet Assembly | X |  | 
 | Beam Position Monitor (BPM) | X |  | 
 | Gate Valves |  | X | 
 | Beamline Vac. Monitoring Manifold & Gauge | X |  | 
Cryomodule | Two-phase Pipe Bellows | X |  | 
 | Tuner, actuator, piezos (Prototype) | X |  | 
 | Tuner , actuator, piezos (Production) |  | X | 
 | Magnetic Shielding | X |  | 
 | GRHP Sub-assembly | X |  | 
 | Vacuum Vessel | X |  | 
 | Coupler Pumping Lines & Pumps (ion+TSP) + vacuum gauges | X |  | 
 | Instrumentation | X |  | 
 | Liquid Level Probes & JT Valve | X |  | 
 | Beamline Interconnect Parts including Aluminum Heat Shields | X |  | 
 | HOM Absorber |  | X | 
 | Shipping Frames & End Caps + Shock Log Devices |  | X | 
 | X = Lead Lab per SLAC LCLSII-4.1-PM-0229-R0 (June2014) |  |  | 

## Slide 5: Features of the Jlab System
State of the art high pressure rinse (HPR) tool has been incorporated into JLab’s suite of cavity processing equipment. The new HPR tool provides up to 10 gallons per minute of ultrapure water (UPW) at pressures up to 1500 psig. The tool also has the capability of high pressure rinsing with ambient and 80oC UPW.

## Slide 6: Features of the Jlab System
1800 sq. ft Clean room for string assembly
100% ULPA coverage
Laminar flow, 100% perforated RMF, side wall return
Bulk headed HPR and other process tools

## Slide 7: Cavity String Assembly in Clean Room
Component assembly tooling same as FNAL
“Lollipop” supports for each cavity and BPM subassembly
Lollipops mounted to mobile rail system
Use mobile rail system rather than rail-in-floor used at DESY, CEA/Saclay and FNAL
Transfer to CM assembly rails for cold mass assembly
Cold Coupler Assembly on AES033

## Slide 8
“Berry” Bolts restraints that enable the cavity to be pumped down and kept under vacuum throughout assembly and test.
    Minimize bleed-ups (slow bleed-up/pump down procedures developed)
    No nitrogen purge during assemblies
Features of the Jlab System

## Slide 9
Magnetic Hygiene of Cavity String
Substitute materials with lower permeability materials, if possible
Measure magnetic fields on individual parts and demagnetize if needed
Set a maximum field spec for tooling used and follow it.
  Measure tools before use and exchange or demagnetize if needed
Demagnetize finished cryomodule
  Use magnetometer measurements to verify demagnetization procedure
The goal is to maximize the Q0 of each finished cavity.
LCLS-II pCM
C50-13
Features of the Jlab System

## Slide 10: Features of the Jlab System
The mobile rail system allows assembled cavity strings on lollipops to be delivered to different assembly rails outside the clean room for integration into cryomodules.
Different types of cryomodules can be assembled concurrently on different rails or multiple copies to improve schedule.
LCLS-II CM02
C100’s

## Slide 11: JLab Layout for LCLS-II CM Production
Clean Room String Assembly
Phase I CM Assembly (2X)
Phase II CM Assembly (2X)
Vacuum Vessel Installation
Final Assembly / Prep for Testing
CM Testing

## Slide 12: Summary
Jlab has a history of cryomodule production going back more than 25 years
  In continuous production during most of that time.
Numerous upgrades of the facility to improve the performance of finished cryomodules have been implemented.
LCLS-II Production is latest CM program at Jlab and is just beginning to ramp up the production rate.

## Slide 13
Thanks for your attention!
Questions?