## Slide 1: Downtime – System Overview
Chart: System Downtime 7.07% of 782.14 Operational Hours
| Cryo | Inst | Laser | Magnets | RF | Water
Fractional Downtime | 0.028042 | 0.013466 | 0.00068274 | 0.0021096 | 0.019156 | 0.0072877
As Reported in D18 Log
Implemented after Start of Run
Inst Downtime Underreported
  Camera Server Issues
  Faraday Cup / Collimator
  Assuming double?
    Brings total to 8.42%

## Slide 2: Downtime – Instrumentation
Chart: Instrumentation Downtime by Subsystem Accounting for 1.35% in D18
| BPM | Camera | Faraday Cup | MPS | Toroid
 | 0.0010228 | 0.0066267 | 0.0052203 | 0.00010612 | 0.00048968
Again, Camera Issues were a bigger problem than the downtime log suggests.
Other notable problems:
Toroids & BPMs
  Not ready at Start of Run
  Ongoing work into Run

## Slide 3: Downtime – Camera Frontends (NMLDC1-4)
Chart: Percent Up-Time Between 5/15 & 8/3 (From Front End Fit Device DCnFXR, n=1-4)
| DC1 | DC2 | DC3 | DC4
Percent Up | 0.7203 | 0.71111 | 0.71218 | 0.69562
This includes
Power Cycles
DPM_PEND
Other ACNET issues
This does NOT Consider
Run Impact (time of day)
Multi-Process Crashes
Image Tool Problems

## Slide 4: Progress – Instrumentation
Toroids
  Not working well even with initial 50 MeV Beam
    Power cycle resets baseline subtraction bit
  Window still a little odd
    Readback is more realistic with larger numbers of bunches
    New window is available through MPS- needs to be implemented
BPMs
  Not working with initial 50 MeV Beam attempt
  Noise continued to be an issue (CC transport matrix measurement)
  Ongoing work to reduce noise & improve sensitivity in hardware & software
HOMs
  The 50 MeV run was spent getting these established
  Available for use by the end of the run (CC1 & CC2)

## Slide 5: Operations – Progress
Turn-on/off can be done through Sequencer (N43).
  Includes routines to turn on all major elements and walk the operator through standard tune-up.
  Does not yet include a full beamline setup check/restore
    In progress…
  “Turn-key” by means of N:LGXS once beam is established
Routines have been written to assist with collection of pulse-to-pulse information from a number of sources while coordinating complex measurements.
  Data sources include ACNET devices (BPMs, toroids, etc) and the camera system.
  Test devices include goniometer, iris, waveplate, TPMs, & trims.

## Slide 6: Operations – Moving Forward
What we need…
  Add 300 MeV to the turn-on sequence
    CM should be the most challenging part but there is nothing new
      Klystron turn-on will behave like the Gun (5MW)
      Cavity Autogradient will behave like CC1/2
    300 MeV Trims/Quads/Bends may be integrated into existing routines for 50 MeV beamline or replicated.
  Get the AD/Operations (MCR) involved more
    Turn-On / Off and basic tuning could be handled easily
    Extra resource for studiers to interface with
    FAST beamline experts freed up for tool development