## Slide 1: Summary of Run
Late start:
  Documentation approval by safety panel
  Leaking valves delaying a successful leak check during installation
  Need to warm to 200 K trying to release contamination plugging lines.
During run
  Few issues caused delay of running to have system come back to steady state. (discussed in the next slide)
  Steady state achieved while running CC1 and CC2 only without the need to cool down the Cryo Module

## Slide 2: Cryo Issues seen during running
Contamination
    Introduction of CC1 introduced a contamination which plugged up pressure transducers.
Kinney Booster failure
  Cause is still currently unknown. Possibly due to booster bearing failure. AD/Cryo is currently working with Tuthill for replacement and search for cause of failure.
Valve 88
  Miscommunication with FESS on water tie in caused an accidental disruption in the ICW resulting in vacuum pump trip.

## Slide 3: Upgrades to system
Kinney Booster
  Upgrades to vacuum PLC software for more efficient protection
  Swap Kinney booster for properly working system
Pressure transducer connection lines
  Contamination leak believed to come from these lines. Search for leak to begin soon.
  Addition of purge ports to major pressure transducer lines.
  Upgrades to vacuum PLC software for more efficient protection
  Swap Kinney booster for properly working system.
Frick compressor remote feature
  Install remote feature on Frick system
ODH ventilation system
  Extension of the test cave requires upgrade to ensure safe operations
  Rick Bossert and Liujin Pei to work on the electronic and controls.
  ODH Engineering note being upgraded currently.