## Slide 1: FAST lattice adjustments summary
Aleksandr Romanov
FAST meeting
18 July 2016

## Slide 2: Trajectory steering
Goal is to align beam with magnetic axes of elements for better emittance and minimal movement of trajectory from lattice adjustments
  Results of alignment through CCs are controversial, need to confirm with HOM detectors or bunch-by-bunch movement mitigation.
  Aligning through quads is possible to within +-0.5 mm
If everything ready and smooth it took 20-25 minutes/iteration
  15 minutes measurements for all quads with magnetization and 9+9 measurements
  5-10 minutes for processing (data analysis and file copying)
  3-4 iterations needed, resulting in 2 hours without major time losses.
Can be speed up to 10 minutes/iteration with proper improvements in correction software
  Get rid of external scripts file editing/copying
  Use optimized magnetization management
Due to quads crosstalk, different quad settings, especially with different polarities, may require adjustments of trajectory

## Slide 3: Lattice correction
Maintain zero field at cathode
Initial conditions determination: 1 hour
  Geometrical method or quad scan
Gradients and other parameters adjustments: 3 x 60 minutes
  Can be speed up to 30 minutes with proper software additions, by eliminating external scripts and files copying.
    15 minutes for experimental data measurements
    10 minutes for processing and correction implementation in control room, but some home work must be done
    5 minutes to save all data for possible future analysis

## Slide 4: Problems
Image acquisition tools are problematic.
  Online processing is erratic and can’t be used.
  Slow and nontrivial operation (impossible to save arbitrary amount of raw frames)
  Crushes quickly if cameras are switched frequently and arbitrarily
  Even if operated as expected by design, crashes every couple hours of continuous operation in “save frames for offline processing” mode. Memory leak?
Absence of usable high level control software.
  ACNET terminals, probably, may be used for these purposes, but they are overloaded with functional and too many ways to do something wrong.
  Needed simple and clear way to save, restore and compare regimes of operation
    For linear lattice parameters: solenoids, quads, trims, RF gradiends and phases, laser spot parameters
    For arbitrary list, but should be only limited amount of lists, to keep it simple.
Looks like gun RF turn-on is too long, because of not perfect parameters of PID algorithm, also model dependent methods may be considered.
  Takes ~30 minutes
Lattice and trajectory correction routines are not fully automated and take at least 2 times more time and require to much “know-how” (same as ACNET terminals for regimes).
  Magnetization is not optimal
  Laser’s shutter is not turned off while magnetizing
  Manual files copying and editing
  Several external scripts are necessary

## Slide 5: Conclusion
Make Sixdsimulation routine to be able to work with control system with minimal manual operations (also important for IOTA).
Prepare bug list and feature request for image tools.
Develop save/restore/compare tool fro linear lattice settings.