## Slide 1: Short Baseline Neutrino Program
Anne Schukraft (FNAL)
for the SBND, MicroBooNE and ICARUS collaborations
Fermilab Users Meeting 2017

## Slide 2: One program – three detectors
SBN Far Detector
Booster Neutrino Beam (BNB)
Detector | Distance from BNB target | Active LAr mass
SBND (near) | 110 m | 112 ton
MicroBooNE | 470 m | 87 ton
ICARUS (far) | 600 m | 476 ton
SBN Near Detector
MicroBooNE
NuMI neutrino beam
All detectors are liquid-argon time projection chambers (LArTPC)
Sitting on-axis in the BNB
Receiving off-axis NuMI beam

## Slide 3: Physics motivation: Oscillations beyond the three flavor mixing model?
“solar mixing”
KAMLAND
Super-K
Daya Bay
Standard model three-flavor oscillations are observed on the scale of L/E km / MeV
“atmospheric mixing”

## Slide 4: Physics motivation: The reactor neutrino anomaly
arXiv:1204.5379 [hep-ph]
Deficit in neutrino flux at the detector observed
Normalization problem?
Oscillations on the scale of L/E m / MeV?
Reactor disappearance experiments
Typical energies: few MeV
Typical baselines: 10 – 1000m
3 flavor neutrino mixing
3 + 1 mixing scenario

## Slide 5: Physics motivation: Radioactive source experiments
Phys. Rev. C73, 045805 (2006)
Radiochemical solar neutrino experiments GALLEX and SAGE with intense (MCi) calibration sources ( disappearance experiments)
below the MeV scale
Baselines on the scale of meters
Deficit in rate observed
Normalization problem?
Oscillations on the scale of L/E m / MeV?

## Slide 6: Physics motivation: The MiniBooNE and LSND results
Anomalies observed in appearance experiments
LSND
Eν = 20 – 55 MeV
Baseline L = 30m
e+
p
n
See also talk by A. Fava yesterday
MiniBooNE
Eν ~ 800 MeV
Baseline L = 540 m
e+
p
n
e-
p
n
Intrinsic background
Other background
signal?

## Slide 7: Physics motivation: The MiniBooNE and LSND results
LSND
See also talk by A. Fava yesterday
MiniBooNE
Excess of electromagnetic events on a scale of L / E ~ m / MeV
Intrinsic background
Other background
signal?
Oscillation signal from additional sterile neutrinos?
Unknown background?
Oscillation signal from additional sterile neutrinos?
Background from induced showers?
Unknown background?

## Slide 8: Status of sterile neutrino global fits
S. Gariazzo, C. Giunti, M. Laveder, Y.F. Li, arXiv:1703.00860
and
( disappearance)
and
( disappearance)
and
( appearance)

## Slide 9: Mission of the SBN program: Resolving the low-energy excess question
The strengths of the SBN program:
MicroBooNE?
Same beamline as MiniBooNE but measurements at different baselines
LArTPC technology:
Excellent spatial resolution and calorimetry  e/ separation
appearance and disappearance measurements with the same experiments
1.
2.
3.
The mission of the SBN program:
Observe or rule out length dependence of oscillations
cover the entire LSND allowed region at 5 .
Resolve the nature of the low-energy EM event excess
Phase A
MicroBooNE only
Phase B
SBND+MicroBooNE+ICARUS

## Slide 10: Principle of LArTPC
Cathode
Anode
Large volume filled with liquid-argon
Strong electric field
E

## Slide 11: Principle of LArTPC
E
ν
Neutrinos interact within the liquid argon volume
Scintillation light production

## Slide 12: Principle of LArTPC
ν
Production of ionization electrons
Ionization e-

## Slide 13: Principle of LArTPC
Anode
ν
Drift
Electrons drift towards anode plane
E

## Slide 14: Principle of LArTPC
E
Anode
ν
Readout on wire planes
Scintillation light captured by PMTs
Anode
U
V
Y

## Slide 15: e / separation in LArTPCs
Technique well demonstrated by ArgoNeuT:
ArgoNeuT collaboration; Phys. Rev. D 95, 072005 (2017)
ArgoNeuT electron candidate
ArgoNeuT candidate
mm resolution allows you to “see” neutral as a gap after the vertex
Calorimetric capabilities can distinguish e from at the shower start
el. shower
e-
el. shower
e+
e-

## Slide 16: Sensitivities of the SBN program
SBN is sensitive to the entire range of interest.
appearance
disappearance
arXiv:1503.01520
Appearance and disappearance measurements with the same detectors!

## Slide 17: SBN schedule
2Q 2019
4Q 2018
3Q 2018
2Q 2018
4Q 2017
1Q 2018
3Q 2017
2Q 2017
1Q 2017
4Q 2016
3Q 2016
1Q 2019
Building Construction
Warm Vessel
Cryogenics
Warm Vessel Design & Fabric.
ICARUS TPC 1 & Cold Vessel
Cold Vessel
TPC 2
Cryogenics Design, Fabrication, Delivery
Lar Fill Commission
Operate
Readout Electronics
Not all activities shown
Operate
Building Construction
Cryostat and Cryogenics Design, Fabrication, Delivery
TPC Design and Fabrication / PMT Procurement
Detector Installation
TPC Assembly
Cryo Installation
TPC Electronics Design, Fabrication, Delivery
Cryo install.
LAr Filling & Commissioning
ICARUS
SBND
MicroBooNE
2Q 2016

## Slide 18: SBND construction
Cathode
Anode & wires
HV system
Cosmic ray tagger
Cold electronics
SBND Building

## Slide 19: ICARUS installation
Warm vessel assembled in May 2017
TPC refurbishment @ CERN
Both TPCs are ready for shipment from CERN to FNAL. Shipping date: June 12!
Watch this space to follow ICARUS:
http://icarustrip.fnal.gov
Cold vessel preparations @ CERN
See also talk by A. Fava yesterday

## Slide 20: MicroBooNE – installation completed in 2015
PMT system installation: Dec 2013
MicroBooNE’s home in the beam line: The LAr Test Facility
Electronics installed
TPC insertion: Dec 23rd, 2013

## Slide 21: The first neutrinos in MicroBooNE
First neutrinos seen and automatically identified a few days after receiving first beam in Oct 2015.
(stat. uncertainties only)
Successful automated reconstruction and event selection chain.
First kinematic event distributions presented at NEUTRINO2016.
MicroBooNE public notes:
http://www-microboone.fnal.gov/publications/publicnotes/
MICROBOONE-NOTE-1002-PUB
MICROBOONE-NOTE-1010-PUB

## Slide 22: MicroBooNE operations
BNB
NuMI
Thanks to the lab’s accelerator and operations team!
Oct 2015 May 2017
BNB
Oct 2015 May 2017
In other words:
  ~ 140 000 CC interactions
  ~ 55 000 NC interactions
  ~ 90 000 CC 0interactions
  ~ 10 000 NC interactions
  ~ 60 000 CC and ~ 12 000 CC interactions
  ~ 25 000 NC and ~ 8 000 NC interactions
Switch to antineutrino-mode running on 02/20/17
~ 5.5e20 POT BNB collected.
MicroBooNE uptime ~97% during stable operations.
~7.6e20 POT NuMI collected.

## Slide 23: MicroBooNE physics goals: Low-energy electromagnetic event excess
What MicroBooNE can do without SBND and ICARUS:
Definitively answer the question if the MiniBooNE excess is electron- or photon-like
γ1
γ2
Electrons?
Or photons?
MiniBooNE collaboration; Phys. Rev. Lett. 110, 161801 (2013)
MiniBooNE
Spectrum of electron-like events
Spectrum of electron-like events
OR
?
MicroBooNE simulation

## Slide 24
MicroBooNE physics goals: Neutrino-Argon cross section measurements
Excellent for
Tracking
Reconstruction of hadronic contribution
Calorimetry
Angular phase space coverage
High statistics
osmic
osmic
Proton/track multiplicity measurements
Quasi-elastic-like:
Muon and proton kinematics
Single and double differential cross sections
NC elastic
CC 0 production
… and much more!
MicroBooNE simulation
Kaon production and ID
MICROBOONE-NOTE-1010-PUB
MICROBOONE-NOTE-1025-PUB
MICROBOONE-NOTE-1006-PUB
MICROBOONE-NOTE-1010-PUB

## Slide 25: How do we get there?
Data
Results

## Slide 26: Roadmap
Data
Results
LAr/e propagation properties
Detector response calibration & simulation
2D & 3D event reconstruction
Noise filtering & signal processing
Cosmic removal
Particle & event ID
Momentum reconstruction
Energy reconstruction and energy scale calibration

## Slide 27: Publications
Data
Results
LAr/e propagation properties
Detector response calibration & simulation
2D & 3D event reconstruction
Noise filtering & signal processing
Cosmic removal
Particle & event ID
Momentum reconstruction
Energy reconstruction and energy scale calibration
Noise Characterization and Filtering in the MicroBooNE Liquid Argon TPC; arXiv:1705.07341
Michel Electron Reconstruction Using Cosmic-Ray Data from the MicroBooNE LArTPC; arXiv:1704.02927
Determination of muon momentum in the MicroBooNE LArTPC using an improved model of multiple Coulomb scattering; arXiv:1703.06187
Design and Construction of the MicroBooNE Detector; arXiv:1612.05824
Convolutional Neural Networks Applied to Neutrino Events in a Liquid Argon Time Projection Chamber; arXiv:1611.05531
The Pandora multi-algorithm approach to automated pattern recognition of cosmic-ray muon and neutrino events in the MicroBooNE detector; coming soon
Measurement of cosmic-ray reconstruction efficiencies in MicroBooNE using a small external cosmic-ray counter; coming soon

## Slide 28: Public notes
Data
Results
LAr/e propagation properties
Detector response calibration & simulation
2D & 3D event reconstruction
Noise filtering & signal processing
Cosmic removal
Particle & event ID
Momentum reconstruction
Energy reconstruction and energy scale calibration
Noise Characterization and Filtering in the MicroBooNE Liquid Argon TPC; arXiv:1705.07341
Michel Electron Reconstruction Using Cosmic-Ray Data from the MicroBooNE LArTPC; arXiv:1704.02927
Determination of muon momentum in the MicroBooNE LArTPC using an improved model of multiple Coulomb scattering; arXiv:1703.06187
Design and Construction of the MicroBooNE Detector; arXiv:1612.05824
Convolutional Neural Networks Applied to Neutrino Events in a Liquid Argon Time Projection Chamber; arXiv:1611.05531
The Pandora multi-algorithm approach to automated pattern recognition of cosmic-ray muon and neutrino events in the MicroBooNE detector; coming soon
Measurement of cosmic-ray reconstruction efficiencies in MicroBooNE using a small external cosmic-ray counter; coming soon
http://www-microboone.fnal.gov/publications/publicnotes/
Space charge studies
Detector stability studies
Data/MC agreement
Cosmic shielding studies
3D shower reco
CC muon kinematics
Charge extraction
Proton ID
Track multiplicities
[~ since last year’s User’s meeting]

## Slide 29: Cosmic removal in MicroBooNE
A typical recorded event in MicroBooNE:
Cosmic removal = Challenge.
Ionization electrons: SLOW! 2.3 ms from cathode to anode)
Scintillation light: FAST!
Cosmic removal strategy:
Require scintillation light at the time of the beam spill arrival (width 1.6us)
Additional topological cuts
First attempt of CC selection (NEUTRINO2016)
Most challenging: Cosmics & neutrinos in the same event
Sufficient for some physics analyses but not for all

## Slide 30: Successful installation of a cosmic ray tagger
73 Modules and readout designed and built at University of Bern
Scintillator bars with two fibers & SiPMs per strip.
X-Y layout for position resolution
Details: arXiv:1612.04614
Completed in March 2017
~85% coverage
Will be used for cosmic removal and detector physics studies using cosmics

## Slide 31: Muon momentum estimation with Multiple Coulomb Scattering
Multiple scattering for momentum estimation of contained and exiting muons
Tuning of the Highland formula for application in LArTPCs
Demonstration on MC and data.
Details: arXiv:1703.06187
Analyze scattering deflection angles in x and y direction
Expect Gaussian with RMS .
= (p) Fit for momentum p.
contained
exiting
< 15% momentum res.
< 10% momentum res.

## Slide 32: Michel electron reconstruction
Michel events are useful for:
Energy calibration
Muon tagging
Stopping muon identification
Energy reco:
Collect all charge from the reco electron track
Collect all charge from radiative phtons
Calibration factor from ADC founts to charge
Recombination correction
Lifetime correction
Details: arXiv:1704.02927

## Slide 33: Cross section physics: From MicroBooNE to SBND
Once SBND is up and running, the MicroBooNE cross section program will be continued with SBND and unprecedented statistics!
Study of nuclear effects in neutrino-nucleus scattering
ArgoNeuT
High-statistics sample will greatly benefit oscillation analyses in SBN and DUNE
High precision & high statistics allow search for rare interaction processes

## Slide 34: Conclusions
SBN is designed to study the baseline dependence of the low-energy event excess and cover the full LSND allowed parameter space with .
While waiting for SBND and ICARUS to come online, MicroBooNE is going to investigate the nature of the low-energy excess.
MicroBooNE is doing groundwork for LArTPC calibration, simulation, reconstruction and analysis for future detectors.
An extensive neutrino-Argon cross section program is being setup by MicroBooNE, and will be followed by SBND with much larger statistics.
MicroBooNE is up an running and working on its first standalone physics results. SBND and ICARUS will follow in 2018 and 2019.
SBND
MicroBooNE
ICARUS
I am coming soon!
Follow my travels on http://icarustrip.fnal.gov/
Working hard on first results. Stay tuned!
Under construction.

## Slide 35: Backup

## Slide 36: Noise characterization and filtering
Main sources of noise identified and characterized
  Low-voltage regulator for cold ASICS
  HV power supply
  900 kHz burst noise.
Hardware upgrades improved (1) and (2).
Residual noise level is low and stable.
Noise filtering is successfully applied in the signal processing chain.
Valuable input for the design of SBND and DUNE.
Details: arXiv:1705.07341

## Slide 37: Convolutional neural nets for particle and event ID
Successfully demonstrated that the technique can be applied to LArTPC images
Details: arXiv:1611.05531
Single particle identification (simulation)
(stat. uncertainties only)
Neutrino event identification
Work on-going to apply these techniques to neutrino analyses.