## Slide 1
Brian Chase
DOE Independent Project Review of PIP-II
15 November 2016
Low Level RF Control System

## Slide 2: Brian Chase - Fermilab
SPM – Low Level RF and RF Integration
Started at Fermilab in 1982 and have work experience in cryogenics, power supplies, D0 detector electronics and beam Instrumentation
LLRF – Linac, Main Injector, Tevatron, Recycler Ring
SRF LLRF – Proton Driver, ILC, ILCTA, DESY (9mA Tests)
LCLS-II, CMTS, PIP-II
LLRF Team
  AD LLRF - E. Cullerton, P. Varghese, J. Edelen, J. Einstein-Curtis, D. Klepec
  IIFC - G. Joshi, S. Khole, D. Sharma, & many others
  CSU – A. Edelen
Charge #1

## Slide 3: Outline
Project Status
System overview
Simulation and Results

## Slide 4: Project Status

## Slide 5: LLRF Systems needed to meet R&D Goals
325 MHz Horizontal test stand
  Support for CW and pulsed mode (Operational)
650 MHz Horizontal test stands
  Support for CW and pulsed mode operation(To be supplied by India)
PIP2-IT
  Master Oscillator and Phase Reference distribution line
    162.5 MHz & 325 MHz (Operational)
  RFQ – 162.5 MHz (Q4FY15)
    2 RF amplifier system (Operational in pulsed and CW modes)
  Buncher - 3 cavities - 162.5 MHz (1st buncher operational)
  Half Wave Resonators - 8 cavities @162.5 MHz
  SSR1 - 8 cavities @ 325 MHz
  Kicker waveform generator

## Slide 6: Synergy Between LLRF DOE Projects at FNAL
 | RF Converters | Digital controller | Algorithms FW/SW | Phase Reference Line | Resonance Control
NML-ILC | FNAL v1,v2 | FNAL MFC | FNAL v1 | FNAL v1 | Development
PIP2 IT HTS | v3 | SOC-MFC | FNAL ongoing | in development | 
CMTS-1 | v3 | SOC-MFC | FNAL ongoing | simplified | 
LCLS-II 1.3 GHz | FNAL v4 | LBNL | LBNL | SLAC | JLAB/FNAL
PIP2 IIFC HTS1, HTS2 | v5 | leveraged from LCLS-II | Leveraged | Leveraged | Leveraged
Mu2e G-2 |  | SOC-MFC |  |  | 
Lots of good project cross pollination going on

## Slide 7: IIFC Deliverable Schedule
A prototype RF protection and interlock has been delivered and tested at Fermilab
LLRF is on a reasonable pace for 2018 delivery
RFPI boards

## Slide 8: IIFC LLRF Status
Seven joints FRSs Approved (two more near approval)
  TRSs in process
8-Channel Down-Converters
  BARC version is in manufacturing process
4-Channel Up-Converters
  FNAL version tested
  BARC version is in manufacturing process
FPGA Board
  In schematic review process
ADC-DAC FMC Module
  Ready for manufacturing
Resonance Control Chassis
  Leverage from FNAL LCLS-II design and is in progress

## Slide 9: LLRF System Overview

## Slide 10: PIP2-IT Low Level RF
40 m, ~25 MeV
30 keV
RFQ
MEBT
HWR
SSR1
HEBT
LEBT
2.1 MeV
10 MeV
25 MeV
- Drive 20 accelerating structures
3 RF frequencies
Master Oscillator and phase reference lines
0.01% amplitude and 0.01 deg. Phase regulation goal
Cavity RF operating parameters

## Slide 11: Primary Technical Risks
Resonance and Field Control for 5 new cavity designs
  Lorentz Force Detuning compensation for narrow bandwidth cavities operated in pulsed mode
  New cavity designs with new mechanical properties
  ~20 Hz half BW with expected 420 Hz Lorentz Force Detuning in SSR1
  See resonance control talk
10-4 beam energy regulation with pulsed system
    Sensitivity analysis in progress
RMS phase along LINAC from 10 deg cavity phase change in first HWR

## Slide 12: RF Power budget and Ql
Total cavity detuning budget including LFD
Measured LFD is 22 times
larger than the entire
resonance error budget
Ongoing cavity design efforts
to lower these numbers
May need real-time feedback during pulse

## Slide 13: Example of Microphonic Detuning at CMTS-1
Main source is believed to be pressure fluctuation from a check valve in the helium return line and will be fixed in current shutdown. Resonance control is every system’s responsibility.

## Slide 14: PIP2-IT RF Stations Diagram

## Slide 15: PIP2IT LLRF rack layout - front and rear view
RFQ
HWR
SSR1

## Slide 16: Phase Reference Lines (162.5, 325, 650 ,1300 MHz)
Multi-frequency Phase References and Local Oscillators

## Slide 17: Basic LLRF Station Diagram for 4 cavities

## Slide 18: System on Chip Multi-channel Field Controller
(16) 14 bit ADCs
(8)14 bit DACs
System on Module
Dual core Arm processor
with FPGA eliminates
the need for a backplane and CPU card

## Slide 19: 4-Channel Up-converter
20 MHz IF input -2 dBm max
162.5, 325, and 650 MHz Output, +11 dBm max
13 dB IF to RF Conversion Gain typ.
Channel to Channel Isolation > 88 dB
Spurious Signal Suppression > 80 dB
High isolation (>68 dB) TTL RF switch
Power Supply 6V, 1.8 Amp
Chart: RF Output vs IF Input
| -15.0 | -14.0 | -13.0 | -12.0 | -11.0 | -10.0 | -9.0 | -8.0 | -7.0 | -6.0 | -5.0 | -4.0 | -3.0 | -2.0 | -1.0 | 0.0 | 1.0 | 2.0
162.5 MHz | -0.58 | 0.44 | 1.48 | 2.46 | 3.42 | 4.44 | 5.42 | 6.44 | 7.42 | 8.43 | 9.43 | 10.42 | 11.41 | 12.38 | 13.36 | 14.29 | 15.12 | 15.72
325 MHz | -1.17 | -0.15 | 0.89 | 1.88 | 2.85 | 3.86 | 4.85 | 5.87 | 6.85 | 7.87 | 8.87 | 9.86 | 10.86 | 11.83 | 12.82 | 13.74 | 14.54 | 15.16
650 MHz | -1.5 | -0.48 | 0.57 | 1.54 | 2.53 | 3.54 | 4.53 | 5.55 | 6.53 | 7.54 | 8.55 | 9.53 | 10.51 | 11.48 | 12.47 | 13.39 | 14.19 | 14.84
Chart: RF Output Linearity
| -15.0 | -14.0 | -13.0 | -12.0 | -11.0 | -10.0 | -9.0 | -8.0 | -7.0 | -6.0 | -5.0 | -4.0 | -3.0 | -2.0 | -1.0 | 0.0 | 1.0 | 2.0
162.5 MHz | 0 | 0.22999 | 0.6884 | 0.45946 | 0 | 0.22999 | 0 | 0.22999 | 0 | 0.11506 | 0.11506 | 0 | -0.1152 | -0.46158 | -0.69317 | -1.5079 | -3.5142 | -8.3927
325 MHz | 0 | 0.22999 | 0.6884 | 0.57399 | 0.22999 | 0.34479 | 0.22999 | 0.45946 | 0.22999 | 0.45946 | 0.45946 | 0.34479 | 0.34479 | 0 | -0.1152 | -1.0416 | -3.3951 | -8.019
650 MHz | 0 | 0.22999 | 0.80267 | 0.45946 | 0.34479 | 0.45946 | 0.34479 | 0.57399 | 0.34479 | 0.45946 | 0.57399 | 0.34479 | 0.11506 | -0.23052 | -0.34598 | -1.2745 | -3.6335 | -7.8947

## Slide 20: PIP-II LLRF 8-Channel Downconverter Prototype
RF input 162.5 MHz – 650 MHz
Less than 1% non-linearity up to 10 dBm RF input
1.8, 2.1, 2 dB conversion loss @ 162.5, 325, 650 MHz respectively
Better than 82 dB Channel to Channel Isolation
RF, LO, IF monitor ports
Absorptive IF output low pass filter
Noise output floor of -161 dBc/sqrt(Hz)
Integrated output 1/f noise < 1.84 fsec, (0.02 to 20 Hz)
LO Input power of 3.1, 3.8, and 5.7 dBm @ 162.5, 325, 650 MHz respectively
Power Supply 6V, 2.25 Amps
Chart: IF Output vs RF Input
| -10.02 | -9.02 | -8.02 | -7.04 | -6.03 | -5.05 | -4.03 | -3.0 | -2.03 | -1.02 | -0.02 | 0.96 | 1.97 | 2.97 | 3.96 | 4.96 | 6.37 | 7.31 | 8.32 | 9.27 | 10.28 | 11.26 | 12.24 | 13.23 | 14.22 | 15.24
162.5 MHz | -11.77 | -10.76 | -9.77 | -8.77 | -7.77 | -6.78 | -5.78 | -4.76 | -3.79 | -2.78 | -1.78 | -0.8 | 0.22 | 1.21 | 2.21 | 3.21 | 4.61 | 5.56 | 6.56 | 7.49 | 8.45 | 9.28 | 9.83 | 9.73 | 9.36 | 9.08
325 MHz | -12.03 | -11.04 | -10.05 | -9.05 | -8.06 | -7.07 | -5.97 | -4.98 | -3.98 | -3.01 | -2.02 | -1 | 0 | 0.99 | 1.98 | 2.99 | 4.35 | 5.34 | 6.33 | 7.33 | 8.37 | 9.55 | 10.58 | 11.42 | 12.02 | 12.48
650 MHz | -11.99 | -11.01 | -10.03 | -9.04 | -8.03 | -7.05 | -5.96 | -4.96 | -3.97 | -2.97 | -1.98 | -0.99 | -0.01 | 0.98 | 1.95 | 2.95 | 4.26 | 5.25 | 6.22 | 7.21 | 8.24 | 9.39 | 10.43 | 11.27 | 11.93 | 12.41
Chart: Output Linearity vs RF Input
| -10.02 | -9.02 | -8.02 | -7.04 | -6.03 | -5.05 | -4.03 | -3.0 | -2.03 | -1.02 | -0.02 | 0.96 | 1.97 | 2.97 | 3.96 | 4.96 | 6.37 | 7.31 | 8.32 | 9.27 | 10.28 | 11.26 | 12.24 | 13.23 | 14.22 | 15.24
162.5 MHz | 0.11506 | 0.22999 | 0.11506 | 0.34479 | 0.22999 | 0.34479 | 0.11506 | 0 | 0 | 0 | 0 | 0 | 0.11506 | -2.2204e-14 | 0.11506 | 0.11506 | 0 | 0.11506 | -2.2204e-14 | -0.23052 | -0.80916 | -2.5652 | -7.7705 | -22.18 | -42.8894 | -65.9587
325 MHz | -0.23052 | -0.1152 | -0.23052 | -0.1152 | 0 | 0.22999 | 0 | 0 | -2.2204e-14 | 0.11506 | 0 | 0.34479 | 0.45946 | 0.34479 | 0.34479 | 0.45946 | 0.91681 | 0.91681 | 1.1447 | 1.2584 | 1.8252 | 3.9494 | 4.7204 | 3.0607 | -1.1579 | -7.6465
650 MHz | -0.46158 | -0.34598 | -0.46158 | -0.34598 | -0.34598 | -0.23052 | -0.23052 | -0.23052 | -4.4409e-14 | 0 | 0 | -0.1152 | -0.1152 | -0.1152 | -0.34598 | -0.1152 | 0 | 0 | -0.1152 | -2.2204e-14 | 0.45946 | 2.3887 | 3.0607 | 1.4855 | -2.0939 | -7.7705

## Slide 21: Simulation and Results

## Slide 22: RF system control diagram

## Slide 23: Baseband cavity and controller model

## Slide 24: Open loop transfer function of cavity and controller
Magnitude
Phase
Closed-loop bandwidth: ~50 kHz
Control system zero: 15 kHz
Proportional gain: 1500
Integral gain: 1.44e+08
Max gain
Nominal gain
Closed-loop bandwidth: ~25 kHz
Proportional gain: 750
Integral gain: 7e+07

## Slide 25: RFQ and Buncher pulsed response
RFQ Pulse measured vs. simulated (Proportional and integral gains were 9.0 and 8.0e5 respectively)
Buncher simulated vs. measured (kp 3.5, ki 6.0e5, Ql ~5000)

## Slide 26: RFQ Resonance control status
Currently meeting specification
  Specification was to recover the RFQ in less than 10 times the RF recovery time
  Goal of less than twice the RF recovery time
  We anticipate meeting our goal requirement after the next round of improvements
The controller interfaces with the water instrumentation, ACNET, and LLRF
The controller framework is modular and can easily be improved or adapted to new systems
Plans to improve performance will decrease the initial start time and decrease the trip recovery time
Vane voltage: Red
Frequency error: Blue
Grey: RFQ ramp, resonance control is idle, LLRF is in SEL
Orange: Resonance control bringing RFQ to frequency, LLRF is in SEL
Green: RFQ is in GDR and LLRF feedback is active

## Slide 27: Conclusions
PIP2IT LLRF is operational with the RFQ and first buncher and are on schedule for the next stages.
IIFC joint designs are are making good progress
PIP-II LLRF detailed level requirements are still being refined with simulation and PIP2-IT experience

## Slide 28: Thank you for your attention!

## Slide 29: Backup slides

## Slide 30: Piezo Resonance Control Requirements
Minimize microphonics to <10 Hz
1 Hz or better resolution
+- 1kHz tuning range
2 drive amplifiers for 2 piezo stack groups per cavity
  (1 module per cavity)
  4 drive modules per chassis

## Slide 31: Piezo Amplifier – PDu150

## Slide 32: Total phase noise to SSA from controller and oscillator
Cavity: 0.00078° rms
SSA: 1.04°
SSA from ADC noise 0.96°
Closed loop response
Cumulative SSA phase noise voltage
Careful attention to noise terms will allow high controller gains
Code developed for LCLS-II
Larry Doolittle LBNL and FNAL

## Slide 33: Feedback gain studies
Percentage error in the cavity field amplitude at 20 microseconds after a disturbance
The disturbance was 10% of full scale
For cases with large integral gain and low proportional gain, the feedback loop is unstable

## Slide 34: 5 min ramp. Mostly automated (operator tuning at 14 minutes to speed things up a little)
Testing faster start, not fully automated. Kink in resonance frequency at 14 minutes was due to operator tuning not automatic tuning.
Vane voltage: Red
Frequency error: Blue
Grey: RFQ ramp, resonance control is idle, LLRF is in SEL
Orange: Resonance control bringing RFQ to frequency, LLRF is in SEL
Green: RFQ is in GDR and LLRF feedback is active

## Slide 35: RFQ vane system step response
Transient response of the RFQ resonant frequency due to change in the vane flow control valve. Prior to changing the flow valve, the intermediate skid was cooled to approximately 25C. The control valve was stepped from 0% open to 50% open.
Notes: \begin{tabular}{c|c|c|c}
& initial & transient & steady state \\ \hline
Time & 0 & 7.2 min & 115.4 min \\
$\Delta f_{res}$& 0 & 46.13 kHz& 21.15 kHz \\
$TT_{101}$ &22.280 $^o$C&25.796 $^o$C& 25.649 $^o$C \\
$TT_{102}$ &31.489 $^o$C& 28.126 $^o$C& 26.141 $^o$C\\
$TT_{103}$& 30.941 $^o$C& 27.639 $^o$C& 26.284 $^o$C\\
\end{tabular}
\begin{tabular}{c|c}
flow path & time delay [s] \\ \hline
$TT_{101} \rightarrow TT_{103} $& 1.0 \\
$TT_{103} \rightarrow TT_{102} $& 17.0 \\
\end{tabular}

## Slide 36: Feedback requirements and analysis
Expecting large disturbances from LFD, want fast response from beam loading transient
  get 15 dB from feedforward beamloading compensation
Approach - find highest stable loop gain and determine system noise requirements
Determine best gain settings from operational experience and needs of beam-based feedback
  It is easy to turn down the gain on a well designed system, impossible to turn up gain on a poorly designed one
Assume a low noise oscillator
  Wenzel VHF ULN 100 MHz 13.7 dBm
  % http://www.wenzel.com/model/vhf-uln/
System loop delay of 2.1 msec
Cavity bandwidth 30 Hz

## Slide 37: Details of First 162.5 MHz RF Section
Phase stability across
harmonics (400 fs)
Temperature controlled racks and component plates
We have this experience and see a path forward

## Slide 38: SOC Data Acquisition Software / Firmware Model
800 Mbit/s data transmission has been demonstrated

## Slide 39: System on Module Multi-cavity Field Controller (SOM-MFC)
SOM is socketed
and upgradable