## Slide 1: The H2 VLE Beam Status report
N.Charitonidis and Y.Karyotakis
October 5th 2016

## Slide 2: Simulation studies
GEANT4 based package (G4BeamLine)
  Full simulation of H2 beam line transport + sec. target + VLE extension
  All material included until the cryo membrane
  We request a particle to cross all our detectors
  Target W for 0.4 to 3. GeV/c and Cu for p > 3 GeV/c
We generate 6M events per energy
CERN-ACC-NOTE-2016-0052

## Slide 3: Beam Composition and rates

## Slide 4: Beam Instrumentation

## Slide 5
Beam size and momentum @ LAr center

## Slide 6: Beam Detectors
Trigger
  3 scintillator tiles 10x10 cm2, S1,2,3
Tracking devices
  4 fiber layers ( 3 in vacuum and the 4th in front of LAr entrance) BPROF1,2,3,4
    1mm diameter one layer per coordinate, ~92% acceptance
Cherenkovs
  Two, 2m long threshold Cherenkovs
TOF
  Two layers of fibers, distant of 32m
  All detectors in vacuum, but BPROF4, and S3.

## Slide 7: CERN Fiber Beam Profile Monitors and trigger tiles, TOF  Integrated in both beam lines
Courtesy: S. Girod, W.Devauchelle, I. Ortega-Ruiz [CERN]
Tilt Flexibility: ~3 degrees from the nominal position
Support Flexibility: ~3 degrees from the nominal position
1mm fibers pitch
Trigger tile of 2mm scintillator
Final design and production for H2 under way by BE/BI group @ CERN

## Slide 8: H2: Integration
All vacuum elements and instrumentation (Cherenkovs, BPROF’s…) integrated.
Courtesy: S. Girod & V. Clerc

## Slide 9: Beam profile monitors, tracker, scintillator tiles
Couresy: S. Girod, V. Clerc

## Slide 10: Momentum reconstruction 3 Fiber monitors around the last bend (both lines)
H2
Beam lines include a momentum selection collimator to be used in redundancy if necessary.

## Slide 11: Particle ID
C1
C2

## Slide 12
For 3.0 to 4.5 GeV/c
  Beam ++ : We identify pions and (K+[0.64% - 1.64%]+p[7.6%]), therefore we call them all p contaminated by K [8%-18%]
  Beam +- : We identify pions and (anti-p[0.3%-0.65%]+K-[0.36%-0.65%])

## Slide 13: Freon 12
This gas may be available at CERN but needs a lot of effort
Replaced by R134a
  The refractive index is ‘unknown’. However for the R134 (n – 1) = 3200 10-6 ( J. Phys. Chem., 1990, 94 (25), pp 8840–8845 ) which would be perfect. Many weeks to get R134 !
  Use parasitically a beam at PS (1-5 GeV, e, p, p) and make pressure scans. Experiment to be done next week in principle.

## Slide 14: DAQ
CERN is responsible for the beam data DAQ
  VME crate and dedicated standard modules
Beam Data
  x,y from the 4 beam profile monitors
  Two Cherenkov counters firing
  Time stamp
  TOF (?)
Beam Data buffer available between bursts
Time Stamp via White Rabbit
  Extra VME module to be added

## Slide 15: Muon Shielding Studies

## Slide 16
v. 1 : No Shielding

## Slide 17
No Shielding Results
Number of muons in cryostat LAr 12GeV 229881
Number of muons in FC 12GeV 105162
Number of hadrons in FC 12GeV 63779
Number of electrons in FC 12GeV 41518

## Slide 18
Shielding v1

## Slide 19
Number of muons in cryostat LAr 12GeV 67523
Number of muons in FC 12GeV 39996
Number of hadrons in FC 12GeV 9685
Number of electrons in FC 12GeV 21171
Shielding v1

## Slide 20
Shielding v2

## Slide 21
Number of muons in cryostat LAr 12GeV 42824
Number of muons in FC 12GeV 33471
Number of hadrons in FC 12GeV 5537
Number of electrons in FC 12GeV 11367
Shielding v2

## Slide 23
More shielding

## Slide 24
No shielding

## Slide 25
1250
Passage 1250
XCET
XCET
Shielding upstream NP02 top view
H 3.9m
H 3.9m

## Slide 26
1600 mm
XCET
1200 mm
23168
1688
1688

## Slide 27
800mm Concrete; Fe; Al; feta?

## Slide 28: Summary
Extensive simulations finished for H2, data available on eos
  Physics list study
  Target optimization
  Background (muons) in progress
  Momentum measurement
Material budget optimization
Detailed technical note submitted end of july 2016
Measure R134a refractive index
Detector production in progress
  Build 1/10th of TOF and test it on SPS this autumn