## Slide 1: Booster operation and beam studies
Kiyomi Seiya
10 November 2016

## Slide 2: 700kW operation at Fermilab
Booster
Proton Improvement Plan (PIP):
Booster upgrade for 15Hz operation
Numi 400kW  700kW (4.3E12 ppp at 9Hz)
Booster repetition rate: 7.5Hz  15Hz

## Slide 3: Outline
Booster at Fermilab
PIP goals and requirements for the 15Hz Booster operation
Beam studies in the Booster
Summary and Plan

## Slide 4: 15 Hz Resonant Circuit Synchrotron
F-Magnet
D-Magnet
Resonant Capacitor
Choke
Proton Kinetic Energy
@ Injection  @ Extraction
400MeV 8GeV in 33.33msec

## Slide 5: Beam to Neutrino experiments
Numi (120GeV)
Recycler(RR)
Main Injector (MI)
(h=588)
Booster (h=84)
LINAC
Booster send beam to Booster neutrino experiment and MI/RR
BNB (8GeV)

## Slide 6: Booster 15Hz operation on Fri Apr 08 2016
11Hz
15Hz
BOOSTER EVENTS
D: BNB
5: Numi
3: SWITCHYARD
7: BSTR DUMP
2: PRE PULSE
1: NO PULSE PS

## Slide 7: Status of Beam Power loss
Chart: 
Delivering protons per hour
Beam Power Loss [W]
2.3E17
4.3E12 ppp with 81 bunches to Recycler
  FULL 15Hz operation for entire Fermilab exp. program.
  Delivering 2.3E17 protons/hour (at 15 Hz) in FY2017
15 Hz and 4.3e12/cycle is 232e15/hour
625 W
Administrative Limit
allows workers to work on components without being exposed to excessive radiation

## Slide 8: Intensity and beam loss in November 2016
Int. at Injection: 4.8E12 ppp
Int. at Extraction: 4.4E12 ppp
Efficiency: 92%
Beam energy loss/cycle = 0.055 kJ  825W@15Hz
(625 W Administrative Limit)
Slow loss
Slow loss
Intensity
Notch creation
Transition
Extraction
Beam Energy Loss

## Slide 9: Current beam studies
Collimator
Optics correction
Absorber
Laser notch
Injection capture and timing
Transition

## Slide 10: Booster FDOODF lattice
Combined function magnets: F, D
FDOODF x 24 periods
Corrector packages at short and long
Corrector package (12 poles) includes
H & V dipoles, quad, skew quad, sextupole, skew sextupole
and H & V BPMs.
F Magnet
D Magnet
Corrector Package

## Slide 11: Booster Lattice and H/V beam size at short and long straight sections
bx @short = 33.7
bx @long = 6.1
by @short = 5.3
by @long = 20.4
H_emittance(95%) = 14p mm-mrad
V_emittance(95%) = 16 p mm-mrad
+/-21.5 mm
+/-17.9mm
+/-9.12 mm
+/-9.15mm
@ SHORT straight
@ LONG straight
beam size
SHORT straight
LONG straight

## Slide 12: Components at long straight section in the Booster
Energy | 400 MeV – 8GeV
RF frequency | 37.9 – 52.8MHz
Harmonic number | 84
Radius | 75.75 m
Cycle Rate | 15Hz

## Slide 13: Booster collimation studies - V. Kapin Single stage collimation to two stage collimation
The phase advance is not optimal for the secondary collimators.
There are aperture restrictions at bending magnets and RF cavities.
1SC (operation)
2SC
H
V
L6
L7
S5

## Slide 14: Simulation and beam studies for collimators
Simulation:
Under optimal conditions the 2SC system could be more effective than the 1SC system by 5%.
Beam study in the vertical plane:
Two stage collimator is less effective by a factor of ~2.
Simulation with 1SC
Simulation with 2SC
Eff. after 10 turns
Eff. after 100 turns
Foil thickness

## Slide 15: Optics correction - C. Y. Tan with LOCO (Linear Optics from Closed Orbit)
Beta beating with extraction bump
corrected lattice
Beta beating can be corrected by using a few quads around the ring.
Extraction bump at Long3

## Slide 16: Beam optics measurement at DC magnetic field
LOCO:
Uses measurements all of the BPM positions at each location and calculate dx/dq.
Calculates quad and skew quad strengths for the beta beating correction using the error between measurements and the model including the rolls and calibrations of every BPM and dipole corrector.
Dipole measurement:
)
= /
Comparison of LOCO and dipole measurements.
B:DOGL3 = 150A
B:DOGL3 = 350A

## Slide 17: Tune scans at DC studies
B:DOGL3 = 150A
B:DOGL3 = 350A
This clearly shows that higher dogleg current increases the width of the Qx = 0.5 resonance.
Currently debugging the code for the correction.

## Slide 18: Notch and beam at injection
Gap
for the extraction kicker
h=588
h=84
Notch(extraction kicker gap) – Booster extraction kicker –MI/RR injection kicker
Notch has to be created at LOW energy
Main Injector / Recycler
81 bunches + 3 empty buckets
Notch
81 bunches
+ 3 empty bkts
capture with
37MHz RF
 84 bunches
1 Booster revolution
Injection
200MHz
Longitudinal profile monitor
@ Booster injection
Time

## Slide 19: Notch creation at 400MeV –S. Chaurize
Notcher at L12
Absorber at L13
Top view of vacuum chambers
L12
L13

## Slide 20: Voltage on the Notcher
Voltage, pulse length and absorber length have to be optimized to reduce losses
at notch creation
(400MeV)
at extraction
(8GeV)
RWM signal
Notcher voltage
X’
X
Absorber edge: 19.93 mm (set to 590 mils)

## Slide 21: LINAC Notch –D. Johnson
No more beam energy loss from Notch creation in the Booster.
Laser notching cavity installed on the downstream RFQ flange.

## Slide 22: Beam sent to the Booster with Laser Notch in July 2016
Commissioning will start at the end of November 2016.
WCM signal at LINAC
WCM signal in Booster
32 msec
70 nsec

## Slide 23: Injection rf capture – C. Bhat
260s
rf capture
150s
60s
debunching
Bmin
New Scheme
Start End
New Scheme:
Booster B-curve
Original Scheme:
40s
injection
360s
rf capture
[time]
RF feedback on
(adjusted)
Booster bending field
We can put more beam to the Booster and reduce momentum spread.

## Slide 24: Longitudinal emittance blowup after transition – C. Bhat
Possible source of the oscillation
Beam current dependence (space charge)
Bucket mismatch (timing, voltage and phase)
Measured ratio of the first quadrupole peak to the transition peak.

## Slide 25: Comparison of 8 BT and 16 BT
Simulation and measurements showed that the quad peak ratio did not change at different intensity after the timing for the transition jump was optimized.
No blowup due to the space charge effect at the intensity of 5E12 ppp.
 Need to improve timing and phases control

## Slide 26: Plan and Summary
Plan
Add two more cavities – reliability and losses
Collimator and absorber upgrade – control beam loss location.
Laser notch – no more notch loss in Booster
Harmonic cavity – increase injection capture efficiency by flatting bucket
Tune and lattice studies – fix beta beating and reduce losses at injection
Summary
The goal is to achieve a Booster operation cycle rate of 15 Hz and an average of 4.3E12 protons per pulse for 2017, as users come on line.
A successful completion of the PIP effort is a laboratory priority and essential for reaching the HEP proton delivery goals.