## Slide 1: RF upgrade for MW beam
Chihiro Ohmori
KEK/J-PARC

## Slide 2: Contents
Status of RF upgrade
FT3L Cavities for Acceleration
Beam Loading Issues
2nd Harmonic Cavities
Mid-Term Plan
Very Long Term Plan for Multi-MW

## Slide 3: Status of RF upgrade
In 2014-2016, all (9) cavities were replaced.
Available voltage : 280 kV => 504 kV for 1.28 sec. cycle (540 kV for 1.16 s cycle).
  For 2.48 sec cycle,
    5 cavities for acceleration
    2 cavities for 2nd H
    2 reserved
123 4 567 8 9

## Slide 4: Status (Reuse of old cavities)
4 cavities/Long Straight, 27 cells
3 cavities/ long straight, 43 cells
Space between Kickers
Ins C
Ins C
2014 Before Replacement
2016 After Replacement
Old cavities are stored in tunnel for 2nd H cavity use in another straight section (INS-A)
Installation in 2018

## Slide 5
Kinsho@IPAC16
Reuse of Old Cav.
Air-cooled Cav.
Old Cav.
2 new Cav.
=====Consolidation of power supplies=

## Slide 6: New FT3L Cavity
Development takes 10 yrs. 9 cavities were replaced to new FT3L cavities.
FT3L ring cores were loaded in the new cavities.
“Finemet® FT3L” is the name of nano-crystalline material which was annealed under transverse magnetic field. It has two times higher impedance than ordinary nano-crystalline material-Finemet® FT3M.
FT3L and FT3M cores were made of thin ribbons. Especially, 13mm-thick ribbon is used FT3L for accelerator uses.

## Slide 7: Magnetic Annealing
Nano-Crystalline is formed during annealing from amorphous.
Crystalline has “easy-magnetized axis”. It affects magnetic domain.
Magnetic annealing controls directions of magnetism of crystalline. It is perpendicular in FT3L.
Major RF loss in magnetic alloy is “domain wall” displacement. FT3L has less displacement motion than others.
FT3L has a half power loss than FT3M which was used in old MR cavities.
Magnetic annealing oven was tested in NU1 building of J-PARC
FT3M
Annealing
FT3L
Mag. Annealing
Direction of easy-mag. axis
RF RF RF
OFF ON ON

## Slide 8: Higher Field Gradient
By the FT3L cavities, available voltage and field gradient are improved !
First FT3L cavity in FY2014
=> 5 FT3L cavities in FY15
=> 9 FT3L cavities in FY16.
Comparison of Field Gradient
Characteristics of materials.
Because of high saturation field, characteristics are stable.

## Slide 9: Assembly of FT3L cavity
Cutting & Polishing
Installation into water tank
FT3L core
Cavity assembling
Molding with low viscosity resin
Water-proof coating
KEK-made
oven

## Slide 10: Beam Loading on FT3L cavity
Anode current during acc.
More RF power & Inductive tuning of cavity
Inductive cavity tuning fits high intensity operation.
No beam
2E14 protons
Original FT3L cavity design: 5 gaps for 70 kV/cav for 1Hz.
Modified: 4 gaps operation for higher intensity with 56-60kV/cav for 1.16 s cycle.
Inductive
tuning
Less power

## Slide 11
RFG山本さんによる計算結果
Calculation by Yamamoto
1.16 sec cycle
Estimation of Anode Current
Max. Anode Current
Res. Freq. w/0 Beam with Beam
Adding 4 Inverter units to APS, max current
becomes
Required Anode Current from a simle model
=> 1.32MW can be handled!

## Slide 12: Compensation scheme
If IB ~ I0 or larger,
Feed Forward
  ISIS
  J-PARC
Fast Feedback
  CERN PS
  AGS
No work in Tunnel.
Need fine tuning for different conditions
Fast Feedback AMP in Tunnel.

## Slide 13: Feed Forward
Feed Forward Compensation for Wideband cavity
  J-PARC adopts wide band cavities. Q=2 for RCS and Q>20 for MR.
  J-PARC adopts feed forward beam loading compensation because
    RCS system may not have enough gain (~20dB) by fast feedback.
    Feed forward does not need extra work in tunnel.
  J-PARC Feed Forward system works properly up to 1 MW-eq. for RCS and 380 kW for MR
Feedforward module can handle 3 harmonics.
RCS: 2,4,6 (or 1-6 for single bunch)
MR:8,9,10
F. Tamura, J-PARC

## Slide 14: Feedback AMP from LIU Collaboration
KEK contributes LIU (LHC Injector Upgrade)-PS&PSB RF.
FT3L cavities will be used to replace all PSB cavities and damper cavities in PS.
These cavities are driven by Solid State AMP. The solid state AMP may fit to FB AMP at J-PARC.
Advantage: More beam & shorter tuning time
PSB
PS

## Slide 15: Recent Progress for Damper
Damper works remarkably!
H. Damerau@Finemet Review
H. Damerau@Finemet Review
2 !

## Slide 16: Feedback amplifier from LIU collaboration
Feedback amplifier for PSB back-up scenario
SSA for PSB FT3L system
J-PARC RF Cavity & AMP
A half size of SSA
A full size of SSA
AMP

## Slide 17: 2 nd Haromonic RF Pattern
RF pattern :
  Injection : 120 kV (fundamental), 70 kV (2nd harmmonic)
  Acceleration : 280 kV → 256 kV (fundamental)
Beam loading compensation effectively works to damp the synchrotron oscillation.
Bunching factor was measured to be 0.3 during injection.
Longitudinal wave forms during injection
with wall current monitor
K1
K2
K3
K4
160 kV 85 kV

## Slide 18: Longitudinal Profiles with High Intensity Beam of 500 kW equivalent
(100 kV, 0 kV)
Bunching factor
0.2 ~ 0.3
Bunch length
~200 ns
(100 kV, 70 kV)
Bunching factor
0.3 ~ 0.4
Bunch length
~400 ns
Simulation
(100 kV, 0 kV)
Simulation
(100 kV, 70 kV)
Tamura

## Slide 19: Mid Term Plan Voltage Requirements
 | Present |  | Upgrade 1 |  | Upgrade 2 | 
Cycle Time (s) | 2.48 |  | 1.28 |  | 1.16 | 
# of protons | 2.2E+14 |  | 2.00E+14 |  | 3.20E+14 | 
Beam Power (kW) | 425 |  | 756 |  | 1334 | 
Acc. Time (s) | 1.4 |  | 0.62 |  | 0.57 | 
Smoothing (s) | 0.1 |  | 0.1 |  | 0.1 | 
RF Voltage (kV) | 280 |  | 504 |  | 540 | 
Max/Extraction | 280 | 255.92 | 504 | 453.6 | 540 | 486
Synch. Phase | 21.85 | 24.03 | 31.13 | 35.06 | 32.27 | 36.38
Ratio of RF bucket | 1 | 1 | 1.10 | 1.03 | 1.11 | 1.03
Upgrade １：504kV = 14 kV/cell X 36 cells
Upgrade 2：540kV = 15kV/cell X 36 cells *Bench test with 16 kV/cell&60%Duty
Two issues;
1) 2nd H RF system (PS, AMP, DAMP, LLRF) when 1.28 s cycle starts.
2) Consolidation of Anode PS for MW beam & #10 Cavity system
Duty 58％ 48% 49％

## Slide 20
Simulation Results for 1.32 MW with 1.16 s cycle M. Yamamoto
100% emittance
Acceleration by 540 kV 1st RF + 75 kV 2nd RF!
0.57s acceleration
Loading compensation on more
Harmonics is needed.
3.19 E14 ppp
B
V
f
Bf
eL
pf
Bunching factor, emittance, filling factor
Beam parameters &
RF parameters
Beam Loading compensations
Injection
Extraction

## Slide 21: An idea for long term: Multi-MW by Batch Compression
RCS achieved 1MW. RCS study suggests 1.6 MW (133 TP) is reasonable.
  FT3L cavities & consolidation of power supplies
  But,3GeV injection seems difficult to inject to MR.
One of future (Long-Term) plans of J-PARC is 6-8 GeV Booster to reduce the space charge effects.
  More beam can be accepted.
Bunch Manipulation by batch compression was studied to achieved Multi-MW beam for T2K with reasonable (achievable) technologies.
  w/o “super-fast” kicker magnets, w/o faster cycling than 1 sec.

## Slide 22: Bunch Manipulation
Slip Stacking at FNAL
Batch compression at CERN
Merging and splitting at CERN
“Handbook of Accelerator Physics and Engineering” World Scientific
K. Seiya, PAC07
H. Damerau, HB2014
No manipulation at J-PARC!

## Slide 23
3.2 GeV Inj: Ave Inj loss 1.5%
(Total loss ~ Inj loss x1.5: 3 kW
for MR 1.2 MW @1.2 s cycle)
Simulation of beam survival in the injection period of the MR
for the RCS 1MW eq. beam (4e13 ppb)
MR Injection Energy and Beam Loss
3.4 GeV
3.6 GeV
6.0 GeV
Time [s]
0 0.04 0.08 0.12
0.94
1.0
0.96
0.98
3.4 GeV Inj: Ave Inj loss 0.75%
(Total loss ~ Inj loss x1.5: 1.7 kW
for MR 1.2 MW @1.2 s cycle)
3.6 GeV Inj: Ave Inj loss 0.38%
(Total loss ~ Inj loss x1.5: 0.92 kW
for MR 1.2 MW @1.2 s cycle)
3.2 GeV
Survival ratio
3.0 GeV
3-50BT: 60π cut 2.4% loss (3.2 kW loss for 3GeV injection MR 1.2 MW @1.2 s cycle)
3.0 GeV Inj: Ave Inj loss 3.2%
(Total loss ~ Inj loss x1.5: 6 kW
for MR 1.2 MW @1.2 s cycle)
Y. Sato

## Slide 24
BR
MR
K1
K2
K3
K4
K5
K6
K7
K8
H=9
H=9
H=9
H=9
H=11
H=13
H=13
H=13
2 empty buckets -> 1ms for Extraction Kicker
Narrow injection bunch w/o 2nd H
->200 ns for injection kicker
Batch Compression at J-PARC MR using 6-8 GeV Booster

## Slide 25: Batch Compression at J-PARC
K4-K5:80 ms for H=9 to H=13
H=9: V=60 kV
H=13: V=87 kV
Total Injection time 120 ms to 280 ms
Increasing injection energy, MR can store more beam.
Recent simulation suggests RCS has a capability to handle 1.6 MW beam.
Batch Compression fits 6 (8) GeV booster scenario to achieve ~3 MW beam power.
Need cavities for compression & consolidation of RF power supplies
H=13
H=12
H=11
H=10
H=9
0V VH

## Slide 26: Summary
All cavities are replaced by new FT3L cavities.
504 (540) kV is available for 1.28 (1.16) sec. cycle.
Before 2018, need new RF AMP and APS for 2nd H
For MW beam, need consolidation of APS.
Batch Compression fits to 6 GeV booster scenario for 3 MW beam.