## Slide 1
Katsuya Yonehara
US-Japan Workshop on Accelerators and Beam Equipment for High-Intensity Neutrino Beams
11/09/2016
Review of LBNF Hadron Monitor Design Options

## Slide 2: Beam Profile Monitor in Neutrino Beam Line
Beam profile monitor in a front end of a neutrino beam
  Combination of hadron and muon monitors
  Monitor beam centroid
Hadron monitor is exposed to severe radiation
  It locates at the end of a decay pipe without shielding
  Radiation hardness is a potential issue for multi-MW beam
  Unexplored beam power!! What kind of device can survive?
NuMI Front end

## Slide 3: Current System Design [1] lots of ion chambers
Hadron Monitor
  7x7 grid  1x1 m2
    1 mm gap chambers
  Radiation Hard design
    ~ 10 Grad exposure
  Mass minimized for residual activation
    57 Rem/hr
Muon Monitors
  9 tubes of 9 chambers each  2.2x2.2 m2
    3 mm gap chambers
  Tube design allows repair
High Voltage (100-500 V) applied over He gas
  Signal acquired with charge-integrating amplifiers

## Slide 4
Vertical Position (inches)
Vertical Position (inches)
Vertical Position (inches)
Muon Alcove 1
Muon Alcove 2
Muon Alcove 3
p+
m+
um
p
m+
m+
Target in - Horns on
Target out -Horns off
Vertical Position (inches)
Hadron Monitor

## Slide 5: NuMI Target Alignment
Proton beam scanned horizontally across target and protection baffle
  Also used to locate horns
Hadron Monitor and the Muon Monitors used to find the edges
Measured small (~1.2 mm) offset of target relative to primary beam instrumentation.
Pulse Height in Chamber (arb.)
target
baffle
baffle
target
baffle
baffle
Graphite protection baffle
Graphite target
Water cooling line
21.4 mm
15.0 mm
11.0 mm
6.4 mm
Horizontal Fin
Target
Horn
Baffle
p
p
Notes: Harp on implementation

## Slide 6: Degrade Beam Sensitivity by Radiation Damage
Sent the same amount of beam for each pixel but the response is not the same

## Slide 7: Possible issues on Ion Chamber for LBNF
Lifetime
  Degradation of the hadron monitor observed almost from the start for the NuMI application
    Certain number of damaged pixels at start
    Gradual increase in leakage voltage on HV
    Gains become variable
    Lifetime is 2-4 years in recent operations
Linearity of output signal
  Found non-linear response at > 2 1011 protons/5 cm2/1.56 ms
    Space charge effect activates recombination
LBNF/DUNE situation will be a factor of 10-20 worse
  Questions of temperature, robustness, and signal response
Courtesy of R. Zwaska, “NuMI Hadron Monitor” [1]
& “Beam Tests of Ionization Chambers for the NuMI Neutrino Beam”

## Slide 8: Proposed Radiation Hard RF Gas Monitor
RF cavity/waveguide made of Aluminum
No other material used in beam enclosure
(Optional: Diagnose the cavity)
DAQ & Analyzer
• Beam induces plasma via interacting
with gas in the cavity
• Plasma changes gas permittivity
• Permittivity change is measured
by observing frequency shift and
Q factor change

## Slide 9: Concept of RF Gas Monitor
Gas permittivity is measured in a microwave-resonant cavity
  Permittivity change modulates the resonant frequency and the quality factor
Permittivity change is proportional to the number of ion pairs in the RF cavity
  Measure the number of ion pairs to reconstruct the number of incident charged particles in the cavity
Degree of permittivity change is dependent on the species of plasma particles
  Electrons contribute the most for RF modulations because of their light mass
  Control the plasma population in cavities is essential
  The change is also influenced by the RF amplitude and gas pressure

## Slide 10: Simulated Secondary Beam Profile in LBNF
1-meter-long-C target
RMS size 7.2 cm
2-meter-long-C target
RMS size 14.4 cm
Fraction of secondary protons per single proton on target
at the end of a 200-m decay pipe (by using G4Beamline[2])
Bin size
3 × 3 cm2, which is the required pixel size in the
monitor for LBNF
Primary proton beam for LBNF
• 120 GeV protons; 1.5E14 ppp for 2.4 MW; 20 ns bunch gap
• 10 msec pulse length; 1.2 s cycle time
• Highest secondary proton intensity 5E10 ppp/cm2 in this bin size

## Slide 11: Simulated RF signal with 1 m carbon target
• Raw x-y beam profile at monitor
• Unit is mm
• Signal from gas-filled RF monitor
- RF amplitude E0 = 0.1 MV/m
- N2 gas pressure pgas = 1 atm
• Vertical shows the plasma
loading
• RF cavity size 30 mm x 30 mm
• 12 x 12 RF cavity cells

## Slide 12: Simulated Beam Alignment with RF gas monitor
Estimated beam center
dy = 1.6 ± 0.5 mm
Estimated beam center
dy = 4.1 ± 1.1 mm
• Add beam position offset
• y-offset is reconstructed
with the absolute error
less than 0.5 mm
• Swept beam position in
x plane that is the same
procedure as for NuMI
beam alignment
• Find transvers profile of
baffle and target
Target
Baffle
Baffle

## Slide 13: Required RF power for single RF cavity
Required peak power for single RF cavity
0.3 or 3 W for 9.3 or 2.45 GHz @ E0 = 0.1 MV/m

## Slide 14: R&D Test and Goal
Verify the concept of RF gas monitor in experiment
Study plasma dynamics in the range of RF gas monitor
  Demonstrate how to control plasma population, i.e. electron-ion recombination, ion-ion recombination, electron capture, etc
Demonstrate feasibility of the system
Propose beam test
DoE SBIR/STTR funded $1M in FY17 & FY18
Looking for beam test facilities & collaborators

## Slide 15: Possible Beam Test Facilities at Fermilab
 | SY dump [4] | M01
Proton energy | 120 GeV | 120 GeV
Beam pulse length | 10 msec (fast kicker) | 4 sec (slow ext.)
Integrated beam intensity per pulse | 1E13 | 4E12
Availability | Limited | Unlimited
Purpose | Close to NuMI/LBNF beam profile: Verify the concept: Study plasma physics | Pretest the RF test equipment including with gas filled cavities and RF sources

## Slide 16: Summary for RF gas monitor
It seems to work for multi-MW beams
Required demonstration
  Verify plasma dynamics
  Demonstrate feasibility of apparatus
Funded for a two-year R&D project
  Preparing beam test
  Looking for collaborators

## Slide 17: Other Possible Method
Fluorescence screen
SEM
Interferometer/Faraday Shift
Thermal scan
Acoustic scan
Nuclide transformation rate
R&D required to evaluate
Radiation robustness/Lifetime
Accuracy/Reliability/Time response
Cost/Complication

## Slide 18: Citations
[1] R. Zwaska, “NuMI Hadron Monitor”, http://docs.dunescience.org/cgi-bin/RetrieveFile?docid=1403&filename=zwaska_hadmon_final_v1_shortened.pdf&version=1
[2] G4Beamline, http://www.muonsinternal.com/muons3/G4beamline
[3] B. Freemire et al, “Pressurized rf Cavities in Ionizing Beams”, PRAB 19, 062004, 2016,
[4] A. Watts, “Magnetic Control of Fermilab Switchyard Beam Splits”, http://beamdocs.fnal.gov/AD/DocDB/0050/005040/002/magnetic-control-fermilab%20%281%29.pdf
[5] K. Yonehara et al., IPAC2015, 1189 (2015), IPAC2016, 2733 (2016),
[6] M. Chung et al., PRL 111, 184802 (2013).
Q. Liu, “Future Prospects of RF Hadron Beam Profile Monitors for Intense Neutrino Beam”, TUPOA44
  Discuss about temperature increment of RF cavities and possible cavity shapes

## Slide 19: Backup

## Slide 20: Plasma Population
Simplified time domain rate equation
: Ion pair production rate [cm-3 s-1]
ne: Number density of electrons [cm-3]
n+: Number density of positive ions [cm-3]
n-: Number density of positive ions [cm-3]
b: Effective electron-ion recombination rate [cm3/s]
t: Effective electron capture time [s]
h: Effective ion-ion recombination rate [cm3/s]
No dissociation
No distinguish of ion cluster
nor ion polymer
Ion pair production rate has been studied and tested its validation in experiment
Need b, t, h to complete
the rate equation

## Slide 21: Effective Electron-Ion Recombination[3]
Electron-Ion recombination time = (Positive ion density × b)-1
≈ (1013 × 10-7)-1 = 10-6 sec < Beam pulse length @ LBNF (10 ms)
X0 = E/p
E = RF amplitude
p = gas pressure
Great amount of ion pairs disappear at the end of beam pulse!!
It induces a systematic uncertainty to reproduce plasma population

## Slide 22: Remove Electrons by Electronegative[3]
Doping electronegative in gas to remove electrons
  Produce positive-negative ion pairs instead of electron-ion one
  Ion-ion recombination time is order of magnitude longer than electron-ion recombination time
  Contribution of electrons is negligible when t ≤ a half RF period
  t ≤ 1 ns is probably acceptable to have a practical system
Plasma loading is ~100 times less with dopant
  Save stored RF energy from RF power consumption by plasma
Require t measurement in the range of RF gas monitor
Shortest time resolution
in this measurement

## Slide 23: Drude model with RF field [5]
Displacement of electron
Polarization
Permittivity
n: Electron collision frequency with gas
m: Electron mass
wrf: Frequency of driving RF
Equation of motion of electron
Energy gain term
Drag force term

## Slide 24: Permittivity change [5]
Resonant frequency shift
Plasma loading
RF power consumed by plasma
Formulae tell us:
Permittivity change is proportional to ne
Real part is enhanced at a low n → Low RF gradient & Low pressure
Imaginary part is enhanced at a high n → High RF gradient & High pressure
ne and n are functions of a gas pressure and a RF gradient

## Slide 25: Study beam induced plasma in gas-filled RF cavity
Tested a gas-filled RF cavity with intense proton beams
400 MeV
H- Beam
Gas-Filled 800 MHz RF cell
Multi-Tesla
solenoid
RF responses with proton beams [6]
Proton beam test at MTA
Extract plasma population from RF signal
Emax = 50 MV/m
Gas pressure = 100 atm
DA: Dry Air
Proton beam energy → 400 MeV
Protons per bunch → O(109/2 mm diameter beam)
Bunch gap/length → 5 nsec/10 msec

## Slide 26: Interpret RF signal [6]
RF amplitude with a plasma loading
Emax = 50 MV/m
Gas pressure = 100 atm
DA: Dry Air
Ion pair production rate
Plasma loading
Recombination process
Electron capture process
Time constant b-1ri → O(msec)
Time constant t → O(nsec)
dN/dt → O(10 pairs/cm) @ pgas= 1 atm
meE02 → O(10-17) Joules/RF cycle
m-iE02 ≈ m+iE02 → O(10-19) Joules/RF
RF source term
Power consumption term