## Slide 1: PIP-II Conceptual Design
Valeri Lebedev
DOE Independent Project Review of PIP-II
15 November 2016

## Slide 2: Outline
PIP-II Performance Goals
Major changes since previous review
  Linac
  Transfer line
  Booster
  Recycler and MI
Summary

## Slide 3: PIP-II Performance Goals
Increase MI power from 700 kW (NOvA) to >1 MW (LBNF) in the energy range 60 – 120 GeV
Increase Booster power from 80 to 160 kW
  8 GeV program: SBNE, …
Future upgrades
  Mu2e at 0.8 GeV and ~100 kW
  Beam power to LBNF to >2 MW
  Provide a platform supporting a high duty factor/CW operation for future intensity frontier experiments

## Slide 4: PIP/PIP-II Performance Goals
Performance Parameter | PIP | PIP-II | 
Linac Beam Energy | 400 | 800 | MeV
Linac Beam Current | 25 | 2 | mA
Linac Beam Pulse Length | 0.03 | 0.5 | ms
Linac Pulse Repetition Rate | 15 | 20 | Hz
Linac Beam Power to Booster | 4 | 18 | kW
Linac Beam Power Capability (@>10% Duty Factor) | 4 | ~200 | kW
Mu2e Upgrade Potential (800 MeV) | NA | >100 | kW
Booster Protons per Pulse | 4.2×1012 | 6.5×1012 | 
Booster Pulse Repetition Rate | 15 | 20 | Hz
Booster Beam Power @ 8 GeV | 80 | 160 | kW
Beam Power to 8 GeV Program (max) | 32 | 80 | kW
Main Injector Protons per Pulse | 4.9×1013 | 7.6×1013 | 
Main Injector Cycle Time @ 60-120 GeV | 1.33* | 0.7-1.2 | s
LBNF Beam Power @ 60-120 GeV | 0.7* | 1.0-1.2 | MW
LBNF Upgrade Potential @ 60-120 GeV | NA | >2 | MW
*NOvA operates exclusively at 120 GeV

## Slide 5: Major Changes since Previous Review (June 2015)
RDR -> CDR
  Draft is ready - Major problems are resolved
Beam Optics
  Stable optics in the SC linac
    Advances in design may result in minor (insignificant) changes in locations of elements
  Beam transport to the Beam dump, Booster and Mu2e upgrade is finalized
    Crossing of Tevatron tunnel is addressed
    Tunnel and service buildings are swapped
      Great progress with civil construction
    Different location of the beam dump
      BPMs in the first arc will be used for energy stabilization feedback
        instead of the time-of-flight measurements at the linac end
      Consistent with eventual delivery of 800-MeV beam to Muon Campus
    Fast switch between beam dump, Booster and Mu2e

## Slide 6: Major Changes since Previous Review (continue)
Progress with PXIE
  LEBT-> RFQ -> Short MEBT->Full MEBT
Progress in construction of HWR and SSR1
Progress in design of SSR2, LB650 & HB650
A requirement to operate in a pulsed regime greatly helped to make better cryo-modules
  Reduced sensitivity to LFD; better reliability of fast tuners
Transition crossing in Booster understood and looks realistic
Indian collaborators will supply a cryo-plant supporting CW operation at Day-0
  High Q0 studies support reduction of Q0 for LB and HB
    LB: (1.5->2.15)1010 ; HB: (2->3)1010

## Slide 7: Approach to the PIP-II Accelerator Physics Design
New SC Linac (800 MeV)
  Design compatible with CW operation => 2 mA beam current
  MEBT bunch-by-bunch chopper chops out bunches at boundaries of Booster RF buckets and from the extraction gap
  Emittance less than 0.3 mm mrad (rms, norm)
    to minimize injection loss and support of tailless transverse painting
  Energy stability of ~10-4 to support longitudinal painting
Booster upgrade
  Rep. rate: 15 -> 20 Hz (leaves more power at 8 GeV)
  Injection energy: 400 -> 800 MeV => intensity1.5, reduction DQSC
  Transverse and longitudinal painting: small Ibeam helps
    Reduces tails and, consequently, DQSC (KV-like distribution)
    Improved energy stability at injection (required for long. painting)
Recycler (intensity 1.5 times)
  Booster repetition rate increase
  => larger momentum separation in slip-stacking => smaller loss
MI (tcycle: 1.33 -> 1.2 s, Ibeam & RF power 1.5 times, P>1 MW @ 60 GeV)

## Slide 8: Major PIP-II Components
New 0.8 GeV linac
  L≈210 m
    Includes 4 empty slots at the linac end, L≈40 m
      Possible energy upgrade
  ~200 m linac extension is anticipated
New Linac-to-Booster transfer line
  L≈300 m
  Better understanding of civil construction
  New location of beam dump
Upgraded Booster
  20 Hz, 800 MeV injection
    New injection girder
    More RF cavities (18 -> 22) (almost there)
Upgraded Recycler & MI
  RF and collimation

## Slide 9: Linac Major Components
H- ion source: 30 kV, 10 mA
LEBT – differential pumping, optics match, beam switch for MPS
RFQ – 2.1 MeV, CW
MEBT – bunch-by-bunch chopper with 20 kW beam dump, optics match, differential pumping, prevent micro-particle migration
SC linac – 800 MeV, 2 mA, CW compatible operation

## Slide 10: SC part of PIP-II linac
Transition points are chosen to minimize number of cavities/ cryomodules (i.e. cost)
Altogether - 25 cryomodules
Type | N CM | Cav/CM
HWR | 1 | 8
SSR1 | 2 | 8
SSR2 | 7 | 5
LB650 | 11 | 3
HB650 | 4 | 6

## Slide 11: Beam Loss and Emittance Growth in SC Part
Simulations do not show dangerous halo growth
  Verified by SNS experience at ~twice larger value of Nb/e
  Ratio of beam size to aperture stays approximately the same downstream of HWR
Intrabeam stripping is expected to be the major loss mechanism

## Slide 12: High Q0 program
LCLS-II: from discovery to technology
New requirements for Q0 for PIP-II (@ 2K)
LB 650 HB 650
RDR 1.50e10 2.0e10
CDR 2.15e10 3.0e10
Single-cell B=0.90 and B=0.61 test results. Five-cell B=0.90 test results.
The results are very promising, but statistics is still insufficient

## Slide 13: Cryogenic Requirements
Dynamic and static loads are about equal in pulsed regime
  Solenoids and couplers are included in the static load
Cryo-plant power has sufficient operating margins at all temp.
  T[K] Cryo-plant(W) Cryomodules(W)
  70 13,000 2,830
  5 1,900 715
  2 2,000 1,676(315)
Rms pressure fluctuations have to be <0.1 mbar
  Passive microphonics suppression
CM Type | Static cryo-load (W) | Dynamic cryo-load (W) | Total cryo- load (W)
HWR | 14 | 23.3 | 37.3
SSR1 | 12 | 23.1 | 35.1
SSR2 | 8.8 | 52.3 | 61.1
LB650 | 2.5 | 52.4 | 54.9
HB650 | 4.7 | 130 | 134.7
Total | 146 | 1532 | 1676
Cryo-loads
per CM at 2K in CW

## Slide 14: Microphonics and LFD
High Eacc & small Ibeam => small cavity bandwidth => high sensitivity to microphonics and LFD
Major sources of cavity detuning:
  Variations in He pressure
  Mechanical vibrations driven by external sources
  Lorentz Force Detuning (LFD)
    Pulsed operation greatly complicates LFD compensation
Passive means
  Reduction of sensitivity to He pressure and LFD
  Engineering aimed at noise reduction in the tunnel
Active means
  Piezo tuners
  Adaptive feedback (Tests of SSR1 yield result close to specs, 20 Hz)

## Slide 15: SC Linac-to-Booster Transfer Line
Major design features
  Bending radius is chosen to prevent Lorentz stripping
  Simple FODO optics, minimum number of power supplies
  2 arcs, zero dispersion straight between them with beam switch
  Beam based energy stabilization based on the 1st arc BPMs
  Fast switching (~20 ms) from beam dump to Booster and Mu2e
The line is lifted to cross Tevatron tunnel (free pass to BSY)
  Tevatron tunnel is used for beam delivery to the test area

## Slide 16: Acceleration in Booster
Beam aperture in the Booster is formed by poles of laminated combined function dipoles
  That greatly amplifies Booster impedance
Impedance was benchmarked by wire measurements (J. Crisp, 2001) and beam based measurements (2016)
Simulations were benchmarked by beam measurements
Simulations ignore multi-bunch modes
  Aimed to study transition-crossing
  Good coincidence between simulations and measurements

## Slide 17: Acceleration in Booster (continue)
Injected beam is painted longitudinally for 300 turns
Large voltage is required to suppress L-emittance growth
Values of 2nd order slip-factor and delay of transition crossing phase jump were adjusted to minimize emittance growth

## Slide 18: Emittance Growth due to Transition Crossing
Simulations show that the target value of 97% particles in 0.1 eV·s is achievable in the Booster
Q-jump with present trim quads helps to reduce De|| ; DQ=0.047
Timing for sextupole sign flip controls 2nd order slip-factor
max(Vbeam) ~ 250 kV

## Slide 19: Recycler and Main Injector
Recycler: Slip stacking with 50% more beam
  It requires an increase of slip stacking efficiency: 95%  97%
    Increased rep. rate (1520 Hz) increases bucket separation  helps
    But there are still severe limit on the tails of Booster beam L. distr.
  Scrubbing is used to suppress ep-instability at present intensity
More powerful RF system in MI
  Present system can accelerate up to 6.2•1013
  PIP-II requires 7.5•1013
A conceptual design of gt jump system exists for long time
  Simulations confirmed, gt jump is needed for loss-free X-crossing
Electron cloud simulations indicate that a SEY smaller than 1.4 is sufficient to suppress the e-cloud in both MI and Recycler.
We have a capability to coat both MI & Recycler beam pipes.
  The MI beam coating has to be done in situ.
  The Recycler beam pipe can be replaced.

## Slide 20: Summary
PIP-II RDR -> PIP-II CDR
The concept is solid and did not get significant changes during last year
During last year a considerable progress has been achieved in
  Design of SRF cavities
  Microphonics and LFD suppression
  Understanding of transition crossing in Booster
Before we have the SC linac we plan
  Work on Booster optics improvements and transition crossing
   Gradual Booster intensity increase toward to PIP-II intensities

## Slide 21
Backup Slides

## Slide 22: Beam Loss
Intrabeam stripping is the main source of particle loss in the SC linac
  The loss value (<0.1 W/m) for CW beam (2 mA, with 5 mA RFQ) is well within requirements
    Not an issue for PIP-II operating at ~1% duty factor

## Slide 23: General Approaches to Design of Cryomodules
All the CMs are based on SSR1-type concept
  They should contain as much identical parts as possible
SSR1 and SSR2 should be as much similar as possible
  The same concept of the He vessel with small df/dP
  The same high power couplers
  Similar tuners. The goal is to use identical tuners
  Similar designs of solenoids
LB650 and HB650 should be as much similar as possible
  The same concept of He vessel
    small df/dP & no magnets inside
    Similar magnetic screens
  The same HP coupler as HB 650
  Similar tuners as HB 650. The goal is to use identical tuners

## Slide 24: SC Linac Design Choices
  Separate SC cryomodules
    Collimators between cryomodules to minimize beam loss inside them
    Solenoidal focusing for HWR, SSR1&2
      SC solenoids inside cryomodules (with attached BPMs and built-in trims)
  Doublet focusing between cryo-modules for LB650 and HB650
    Warm correctors and BPMs
  Energy stability of ≈10-4 is supported by the beam based feedback
    Cavities of the last cryo-module are used for correction
    4 empty slots at the linac end are used for time-of-flight energy measurements
  All beam instrumentation with exception of BPMs in HWR and SSR1&2 cryo-modules is located between cryomodules

## Slide 25: Warm Sections of SC linac
LB&HB650 sections of SC linac include 2 warm quads (Q), 1 dipole corrector (D) (X&Y), and strip-line BPM
Configurations are:
  Low Beta : (QDQ) (CCC) (QDQ) ………. : 11 CM
  High Beta :(QDQ) (CCCCCC) (QDQ) ….. : 4 CM

## Slide 26: Magnets & BPMs
Quads
GdL (T) | 3
G (T/m) | 13.5
2*a [mm] | 48
Dipoles
BdL (mT m) | 10
2*a [mm] | >48
BPMs
Strip-line
4 electrodes
Located between quads

## Slide 27: RF Power Requirements
RF power requirements include
  Up to 20 Hz microphonics driven detuning
  1 dB allowance for regulation
  Power transfer inefficiency:
    0.5dB - HWR&SSR (coaxial);
    0.25 dB – LB&HB (wave guide)
CM type | Power trans-ferred to beam per cav. (kW) | Cavity half-bandwidth, f / 2QL, (Hz) | Peak RF power per cavity (kW) | Power of RF Amplifier (kW)
HWR | 4 | 33 | 6.5 | 7
SSR1 | 4.1 | 43 | 6.1 | 7
SSR2 | 10 | 28 | 17 | 20
LB 650 | 23.8 | 29 | 38 | 40
HB 650 | 39.8 | 29 | 64 | 70

## Slide 28: Transverse Painting
H- strip injection
  Linac beam comes to the foil corner
    Like in the SNS
  Reduced beta-functions for linac beam to reduce secondary heats of stripping foil
Zero dispersion of linac beam
Non-zero Booster dispersion and non-zero momentum offset reduce secondary hits

## Slide 29: Booster Injection
No significant changes since last MAC
More work is required and planned in support of CDR
  Final choice of the scheme
    New short dipoles adjacent to injection straight versus tightly located elements of the injection straight
  Conceptual design of injection straight magnets and, possibly, short Booster dipoles

## Slide 30: Acceleration in Booster
Transition from 15 to 20 Hz rep. rate would not require additional RF voltage if beam current is not changed
  Due to smaller slip factor at injection
Increase of beam current (planned for PIP-II) requires additional voltage
  Deceleration due to RW impedance
  Suppression of quadrupole oscillations after transition
15 Hz 20 Hz

## Slide 31: Results of Booster Transition Crossing Studies (3)
Measured shift of accelerating phase with beam intensity yielded a calibration of ZL
The peak deceleration voltage expected at PIP-II design intensity of 6.5•1012 is ~300 kV
Decent coincidence of simulations and measurements is achieved
Studies of transition crossing at PIP-II intensity will follow shortly

## Slide 32: Booster Transition Crossing Studies
Present transition-X is quiet sophisticated and very well tuned. It effectively suppresses quad-oscillations introduced by X.
Optimization of transition-X at PIP-II intensity requires good modeling of Booster acceleration and its L. impedance
4 sets of measurements (Jan,July&Nov/2015, & Jan/2016)
  Usefulness of data was improved with time
Data are taken at injection and transition (few ms each)
  RF sum + RWM + Rpos (0.2 0.8 ns sampling time, 6•106 points)

## Slide 33: Development of Software for Simulations of Longitudinal Dynamics (F. Ostiguy)
To assure the simulation results the Booster simulations are done with a code specially developed for Booster acceleration
  No GUI, minimally required numerical engine
  ESME was not used
However for over 3 decades, the code ESME has been used to simulate long. dynamics, both at Fermilab and elsewhere.
  While ESME remains in use, the main author is retired and the code is minimally maintained.
  Details of its inner workings and of underlying approximations are not well documented. Code structure and organization reflect limitations of late 1980s software technology.
    Even minor modifications are hard to implement and debugging is often a non-trivial endeavor.
To address this deficiency as well as to model the Booster and other machines we initiated development of a new code based on a code developed for Booster simulations.

## Slide 34: Slip Stacking in Recycler
Twelve Booster batches are slip-stacked in Recycler
An increase of Booster rep. rate from 15 to 20 Hz requires faster slipping => larger momentum separation => larger RF bucket size => smaller loss at slip stacking

## Slide 35: Beam Acceleration in MI
The accelerating rate in MI is determined by maximum slue rate of magnetic field and RF voltage
  That determines the dependences of (1) cycle time duration and (2) beam power on the final beam energy
MI RF power upgrade is required to support the beam intensity increase

## Slide 36: MI Transition Crossing
Increased beam intensity and larger longitudinal emittance complicate transition crossing
gt jump is preferred method for transition crossing in MI
ESME simulations do not show significant increase of L. emittance and longitudinal tails
Additional hardware for fast tune change is required
Phase space distribution after transition in MI. The hole in the center is a result of slip stacking