## Slide 1: DAQ Architecture
Giovanna Lehmann Miotto
DAQ Design Review
3 Nov 2016

## Slide 2: Introduction
From DUNE DAQ to ProtoDUNE DAQ
External interfaces and constraints
DAQ logical architecture
Main DAQ components and their interaction
Risks & timescales
Summary

## Slide 3: DUNE Trigger and DAQ Requirements
Very high up-time (>99%)
Collect beam+atmospheric neutrinos as well as proton decay candidates (Etot>100 MeV) with high resolution and no dead-time
Collect interactions with Etot<100 MeV with a limited zero-suppression loss
Be able to trigger on beam pulses irrespective of the deposited energy
Collect data with the most favorable zero-suppression possible over >10 s periods (supernova trigger)
+ all DAQ ancillaries (event building, calibration, control, …)
Difficult to satisfy so varied requirements!

## Slide 4: Main Trigger & DAQ Features
The DUNE DAQ is designed combining ideas of
  Continuous readout systems
  Triggered systems
No dead time achieved by streaming the data summaries into a trigger farm and keeping raw data in ring buffers on readout system during decision making
  HE events:
    trigger request sent to readout system and data fully readout, built, processed, stored
  LE events:
    Trigger stream of hits are useful for SNB analysis and will be buffered/stored as long as possible (ring buffer of disk files)
    When a SNB is noticed in the trigger farm, it directs to also extract data from ring buffers

## Slide 5: Sketch of the DUNE DAQ
Detectors’ Electronics
Off detector readout systems
Data summaries
Ring Buffer
Trigger Farm
Data Processing
Farm

## Slide 6: Sketch of the DUNE DAQ
Detectors’ Electronics
Off detector readout systems
Data summaries
Ring Buffer
Trigger Farm
Data Processing
Farm

## Slide 7: Sketch of the DUNE DAQ
Detectors’ Electronics
Off detector readout systems
Data summaries
Ring Buffer
Trigger Farm
Data Processing
Farm

## Slide 8: Sketch of the DUNE DAQ
Detectors’ Electronics
Off detector readout systems
Data summaries
Ring Buffer
Trigger Farm
Data Processing
Farm
Zero suppression and compression occurring at different stages of the DAQ, depending on trigger type.

## Slide 9: From DUNE to ProtoDUNE SP
Smaller
  0.77 kt vs 10 kt LAr per DUNE module; only 1 module
  Less components but each component is full-scale pre-production module; only 6 APA
On surface
  Higher flux of cosmic ray particles
On SPS beam line
  charged particles 0.5 – 7 Gev/c
The rate and volume of data produced by these detectors will be substantial (O(Tb/s))

## Slide 10: The ProtoDUNE DAQ Environment
6 Anode Plane Assemblies (APA)
  TPC ~ 430 Gb/s (15kCh @ 2 MHz)
  Photon Detectors ~ 1 Gb/s (288 SiPM, headers only)
Beam instrumentation (BI) & Cosmic Rays Tagger (CRT) detectors
  Negligible throughput
SPS super cycle structure: 2 x 4.8 s bursts in 48 s
  Full readout -> ~85 Gb/s
  Too much for DAQ as well as for storage!
Introduction of a simple trigger to mitigate data flow
  Retain full readout off detector
Use of lossless data reduction techniques

## Slide 11: From DUNE to ProtoDUNE DAQ
TPC
Off detector readout systems
Data summaries
Ring Buffer
Trigger Farm
Data Processing
Farm
✗
✗
✗
Beam Instrumentation, cosmic μtagger
Trigger
Photon Detectors
Off detector readout system
Data summaries

## Slide 12: The 35 t prototype DAQ
HERE SLIDE FROM GILES

## Slide 13: Scope of the ProtoDUNE DAQ
Provide service to the detector/electronics validation
  Take and store data safely and efficiently
  Reuse existing components, experience, …
Evaluate DAQ solutions and technologies that may be suitable for DUNE
  TPC readout system
  Data storage
  Dataflow software (hardware fully COTs servers + switches)
  Control and monitoring software

## Slide 14: Interfaces
DAQ
Photon Detectors (SSP)
TPC (WiB)
Beam Instrumentation
CRT
SPS
Offline Computing
Spill Signal
Trg In
Trg In
Timing + Trg out
Data
Data files + metadata

## Slide 15: Constraints
Decoupling
  The DAQ needs to ensure a proper decoupling between the “online” and the “offline” worlds
    Sufficient storage space for raw data files on the DAQ side should be available to store up to 3 days worth of data taking.
Grounding
  Try to keep all DAQ equipment on building ground
  Any link connecting the detector must be isolated -> optical
    Direct impact on readout, timing, trigger

## Slide 16: Grounding Isolation
Detector
Building
Timing
Trigger Board
Other DAQ equipment
Beam Instrumentation
CRT
SSP
WIB
Ethernet switch

## Slide 17: The ProtoDUNE DAQ
TPC
Off detector readout systems
Ring Buffer
Event Building
Farm
Temporary Storage
Beam Instrumentation, cosmic ray tagger
Trg+Timing
Photon Detectors
Off detector readout system
Summary Info
Data Compression
430 Gb/s
24 Gb/s
25 Hz in burst
EOS
20 Gb/s
Event size ~ 60 MB (5ms window, x4 compression)
DB

## Slide 18: ProtoDUNE Software
Dataflow software is based on artDAQ developed at FNAL
  Customizable “Board Reader” application
  Event building
  Dispatching to monitoring apps
  Aggregation
  Storage
Control, operational monitoring, graphical UIs
  Joint COntrols Project (JCOP) toolkit developed originally for LHC experiments
  Uniform interface also for detector control and safety systems
Software approach
  Minimize the risks by relying on existing frameworks
  Focus effort only on experiment specific needs

## Slide 19: Readout of External Systems
PDS
  On detector electronics already does data reduction and sends data over TCP/IP (-> DAQ starts at Board Reader)
TPC (point-to-point optical links from WiB)
  2 solutions being implemented
    Baseline: ATCA platform from SLAC
    Prototype alternative: ATLAS FELIX + network connected PCs
  5 APAs will be readout via ATCA boards (12800 ch), 1 APA (2560 ch) via FELIXs
    2 firmware variants in electronics (WiB)
    API for transparently treating data at software level
    Provision to read out all system with ATCA
From a software point of view the interface towards the event builder is the Board Reader application for all readout systems

## Slide 20: ProtoDUNE Data Flow
Board Reader
Event Builder
Event Builder
Board Reader
Board Reader
DataFlow Orchestrator
Trg/Timing
1
2
3
4
5
10 Gbps Ethernet
(Brocade ICX7750)
Aggregator/Storage

## Slide 21: DAQ Temporary Storage
I/O requirements similar to ATLAS/CMS now
Hardware solution similar to ATLAS data loggers (modular!)
Transfer to EOS using F-FTS and XRootD
Courtesy W. Vandelli, CERN

## Slide 22: ProtoDUNE Trigger Throttling
Board Reader
Event Builder
Event Builder
Board Reader
Board Reader
DataFlow Orchestrator
Trg/Timing
Aggregator/Storage
No storage space or slowed down disk writing
-> EB cannot clear events
EB cannot get rid of events
-> DFO cannot assign new events
DFO full/free
-> BUSY/NBUSY
Readout full/free
-> BUSY/NBUSY
Due to the low trigger rates and the “continuous” readout mode of on-detector electronics, software throttling seems sufficient
-> hardware throttling still possible as an option

## Slide 23: A Word on Partitioning
Partitioning = the mechanism by which multiple copies of the DAQ can run on a same installation
The DAQ has a few elements that cannot be split
  (Virtual) duplication to allow for parallel running
Partitioning is normally extremely useful during commissioning & testing
  Even if it wasn’t a requirement from the experiment point of view it is a requirement from the DAQ side
Proposal to be able to partition the system into vertical slices, i.e. by APA
  Only one partition will make use of the central trigger board, while others will use random or constant rate triggers

## Slide 24: ProtoDUNE Timeline
Nov‘16
End’18 LS2
Jun’17
Jul‘18
Test 1st APA
Installation complete
Data Taking
TDR
DAQ ~functional
DAQ complete
DAQ design review
Continue data taking and R&D
in 2019, possibly….

## Slide 25: Risks
External Interfaces
  Detailed specs (physical links, connectors, protocols, information content)
  Continuous interaction between sub-system leaders AND detailed work sessions with sub-system specialists
Internal Interfaces
  New timing system to be integrated with trigger and many endpoints
  Detailed specs and regular meetings
  Continuous integration testing!
Resources
  We are confident that the people and institutions that committed to the DAQ will deliver on their components
  Sufficient effort will be needed @CERN to ensure smooth integration, commissioning, tuning, operation

## Slide 26: Summary
A complete design of the DAQ system exists
  Interfaces
  Components model, Interactions and data flow
All hardware components required for the DAQ identified
  COTs servers, switches, interconnects (not a large system!), storage solution
  ATCA based SLAC solution
  FELIX PCIe cards
  Timing units
  Central Trigger board
Main risks have been identified at the external interfaces level
  Mitigation through direct discussions at different levels
We are confident that the proposed DAQ design can be implemented on the timescales required by ProtoDUNE, that it satisfies the requirements that have been put forward by the experiment and that it has sufficient modularity to allow for flexibility, in case of additional performance needs.