## Slide 1
Muon Campus Timing Meeting
10/24/2016
ACNET Infrastructure Around The Muon Campus

## Slide 2
ACNET Networking
  Gigabit & 100 Megabit Ethernet
TCLK
  High level machine timing (microsecond level) and co-ordination
RRBS
  Beam synchronous timing (20 nanosecond level)
  Fiber-RRBS: 7.5MHz events encoded, 53MHz RR-RF
  Cu-RRBS: 7.5MHz events encoded
MDAT
  Machine data including Machine State Information
Abort Links
  P1, P2, Muon
ACNET Infrastructure

## Slide 3
Muon Campus ACNET Infrastructure
MI-52
  Gigabit Ethernet, TCLK, MDAT, fiber-RRBS, RR & P1 Abort Links
F0
  Gigabit Ethernet, TCLK, MDAT, fiber-RRBS, P1 & P2 Abort Links
F1
  100 Megabit Ethernet, TCLK, MDAT, fiber-RRBS, Muon & P2 Abort Links
F23, F27
  Gigabit Ethernet, TCLK, Cu-RRBS, Muon Abort Link
AP-0
  Gigabit Ethernet, TCLK, Cu-RRBS, Muon Abort Link
AP-10, AP-30, AP-50
  Gigabit Ethernet, TCLK, Cu-RRBS, fiber-RRBS, Muon Abort Link,
  MDAT@AP-30
MC-1, Mu2e (planned)
  Gigabit Ethernet, TCLK, fiber-RRBS, Muon Abort Link

## Slide 4
TCLK $1C – Booster reset for beam to Muon Campus
TCLK $93 – Muon reset for beam to Muon target via RR
TCLK $94 – Muon reset for beam to Muon around target via RR
TCLK $E9 – RR reset for beam to Muon Campus
TCLK $9A – RR to Muon Campus Transfer #1
TCLK $9B – RR to Muon Campus Transfer #2
TCLK $9C – RR to Muon Campus Transfer #3
TCLK $9D – RR to Muon Campus Transfer #4
TCLK $9E – RR to Muon Campus Transfer #5
TCLK $96 – RR to Muon Campus Transfer #6
TCLK $97 – RR to Muon Campus Transfer #7
TCLK $98 – RR to Muon Campus Transfer #8
RRBS $A6 – RR to Muon Campus transfer event (fires kickers)
TCLK $F6 – TCLK reflection of RRBS $A6
TCLK $EF – RR Abort Cleanup
TCLK $E6 – RR End of Beam Operations
TCLK $89 – Muon Abort Cleanup
TCLK $86 – Muon End of Beam Operations
Some Muon Campus Important Clock Events

## Slide 6
R:ACUPE9 264.9mS ref $E9 - triggers TCLK $EF, RR Abort Cleanup
R:EOBE9 265.9mS ref $E9 - triggers TCLK $E6, RR End of Beam Ops.
T:TD9A ~200mS ref $93 - triggers TCLK $9A, 1st RR xfer to Muon
T:TD9B 10mS ref $9A - triggers TCLK $9B, 2nd RR xfer to Muon
T:TD9C 20mS ref $9A - triggers TCLK $9C, 3rd RR xfer to Muon
T:TD9D 30mS ref $9A - triggers TCLK $9D, 4th RR xfer to Muon
T:TD9E 40mS ref $9A - triggers TCLK $9E, 5th RR xfer to Muon
T:TD96 50mS ref $9A - triggers TCLK $96, 6th RR xfer to Muon
T:TD97 60mS ref $9A - triggers TCLK $97, 7th RR xfer to Muon
T:TD98 70mS ref $9A - triggers TCLK $98, 8th RR xfer to Muon
R:RRMNX 9mS ref $9A,$9B,$9C,$9D,$9E,$96,$97,$98 - RRBS $A6 trigger
Muon g-2 Timeline Important Timers

## Slide 8
Modifications to Timeline Generator (TLG) to allow moving RR reset(s) closer to Booster reset(s).
Set TLG delay timer T:RSTDL2 to approximately 14.5mS
Set TLG delay timer T:RSTDL1 to approximately 14.5mS
Note: This moves the timing of all MI & RR reset events to within 2mS of the first booster reset of the cycle. This will shorten the time between the MI/RR reset event and the first injection from booster from approximately 52mS to approximately 37mS.
Among timers that will have to be adjusted:
  I:ACUPnn, R:ACUPnn
  I:EOBnn, R:EOBnn
  I:RPSTnn
  I:FTSTnn

## Slide 9
Issues:
RRLLRF setup time (must be less than 36mS)
RR&MI Abort Kicker charge time (must be less than 36mS)
Instrumentation setup time (must be less than 36mS)
Only 1 mS between last transfer to Muon and Abort/CleanUp (TCLK $EF)
Only 1 mS between Abort/CleanUp (TCLK $EF) and End of Beam (TCLK $E6)
“Only” 800 uSec. between “End of Beam” and next Recycler Cycle Reset
  May be shorter due to line breathing (200uS?)
  LLRF?
  Instrumentation readout: BPMs, BLMs, etc.
  Pulsed devices?
Delay of $E9 event to within 2mS of booster reset via TLG moves ALL MI & RR resets relative to first booster injection. This shortens front porch of all booster=> MI/RR cycles by approximately 14.5mS.