## Slide 1: Study of Fast Instability in Recycler
Sergey Antipov, The University of Chicago
Advisors: Young-Kee Kim (U.Chicago) and Sergei Nagaitsev (FNAL/U.Chicago)

## Slide 2: Outline
What we know about the fast instability?
Electron cloud trapping in Recycler combined function magnets
Model of the instability
Microwave measurement of electron cloud
Stabilization with a clearing bunch

## Slide 3: Acknowledgements
Phillip Adamson, Ming-Jen Yang, Victor Grzelak, AD Operations for help with conducting the experiments
Alexey Burov, Yuri Alexakhin, Jeff Eldred, and all e-cloud group for numerous useful discussions of the results

## Slide 4: Fermilab’s Recycler
Proton momentum | 8.9 GeV/c
Circumference | 3.3 km
Max protons per batch | 4*1012
Number of batches | 6
Bunch spacing | 19 ns
Revolution period | 11 μs
Betatron frequencies (x, y) | 25.425, 24.415
The Recycler (top) and the Main Injector (bottom) rings installed in a common tunnel.
Dipole
Quadrupole
Gradient Dipole
8*1012 after upgrade
Based on gradient dipoles
SPS (CERN) – similar issues

## Slide 5: Fast instability in Recycler
Develops in 20-30 turns
Leads to increase of transverse emit.
Might be a challenge for PIP-II intensities
~ 20 turns
Beam center hor. position (mm)
Revolution #

## Slide 6
Horizontal Position
Number of Revolutions
6
Fast instability affects the first batch above the threshold intensity
Threshold intensity
Pictures provided by J. Eldred
Notes: 6
6

## Slide 7
7
Electron cloud build-up
Pictures provided by J. Eldred
Notes: 7
7
7
7
7

## Slide 8: Electron cloud can lead to an instability
Ideal case
With electron cloud
Solution – oscillations around the reference orbit
‘Driven oscillator’
Can have unstable modes
Focusing strength
Kick by electron cloud

## Slide 9: Direct measurement showed evidence of EC
Phase modulation at beam revolution freq., 90 kHz
Pictures provided by J. Eldred
2 GHz
Propagate a microwave signal through the beampipe
Phase-delay:
Not enough temporal resolution to observe the evolution
50 m

## Slide 10: Why do we see an instability in Recycler but nothing in Main Injector?
Same energy
Same beam
Same beampipe
Dipole
Quadrupole
Gradient Dipole

## Slide 11: Trapping in combined function dipoles
Escape cone:
Quadrupole component
Dipole component

## Slide 12: Trapping in combined function dipoles
Escape cone:
Quadrupole component
Dipole component
Magnet | Central Field, kG | Bdl, kG-m | Quad, kG/m
RGF | 1.3752 | 6.182 | 3.355
RGD | 1.3752 | 6.183 | -3.238
SGF | 1.330 | 4.121 | 6.682
SGD | 1.330 | 4.121 | -6.824

## Slide 13: Up to 1% of the particles can be trapped by magnetic field
Chart: Bunch population
| 100000000 | 300000000 | 500000000 | 1000000000 | 2000000000 | 2200000000 | 2300000000 | 2400000000 | 2500000000 | 3000000000 | 4000000000 | 5000000000 | 10000000000 | 20000000000 | 30000000000 | 40000000000 | 60000000000 | 80000000000 | 100000000000
Trapped | 0.00025 | 5e-05 | 3e-05 | 0 | 0 | 0.00035 | 0.0016 | 0.005 | 0.014 | 0.022 | 0.017 | 0.017 | 0.014 | 0.02 | 0.0041 | 0.0046 | 0.009 | 0.007 | 0.0019
Current
intensity
Lifetime due to scattering: ~ 1 ms
All trapped particles survive until the next turn

## Slide 14: Presence of trapping changes the build-up
Linear particle density (m-1)

## Slide 15: Electron cloud forms a vertical stripe inside the vacuum chamber; its horizontal position - beam center
2σ

## Slide 16: When bunches compress longitudinally, the electron density reaches the beam density
Linear particle density (m-1)
beam
time (μs)
0
1
2
3
4

## Slide 17: Fast instability happens when the cloud reaches the saturation
Beam center position (white) and electron cloud distribution every 4 bunches or 80 ns Intensity - 5*1010 ppb, 80 bunches, σz = 40 cm
2 cm

## Slide 18: The instability only affects the horizontal motion
Growth rate ~ 4 revolutions (after the cloud has reached the saturation density)

## Slide 19: Clearing prevents the multi-turn accumulation of the electron cloud
Linear particle density (m-1)

## Slide 20: Stabilization by Single Low-Intensity Bunch
1.5e10 p
1e10 p
5e9 p
Increase clearing bunch intensity:
3.6e12 p
3.6e12 p

## Slide 21: Electron cloud creates a shift in betatron frequencies between the head and the tail of the bunch train
Focusing horizontally (higher Q)
  Electron cloud is the only effect that can increase the frequency
Defocusing vertically (lower Q)

## Slide 22: Electron cloud creates a shift in betatron frequencies between the head and the tail of the bunch train
Use the data from 600 turns to evaluate the betatron frequencies (tunes)
Positive tune shift is a signature of electron cloud
Chart: Horizontal tune shift
No clearing
With clearing

## Slide 23: Can we estimate the rate of the electron cloud instability?

## Slide 24: Analytical model of the instability: coasting beam
Solving the coupled e-p motion
Searching for solutions in the form
Im(Δω) – Growth rate Re(Δω) – Frequency shift
Damping
Focusing
Linear coupling
Mobility of the cloud

## Slide 25: Analytical model of the instability: bunched beam
Impedance
The most unstable mode
Instability growth rate
Betatron frequency shift
One can estimate the unknowns from the measurement of the betatron frequency shift or from the simulation of the build-up
Unknown

## Slide 26: Tune measurement agrees with the simulation
Chart: Horizontal tune shift
Witnesses: 8e9 p
Main batch: 5e10 ppb
Simulation
ne = 6*1011 m-3
λ = 2.7*106 s-1

## Slide 27: Growth rate and mode frequency are consistent with the observations
The most unstable mode is nmax = 30
The frequency of this mode is 0.4 MHz
Stripline measurement shows a horizontal instability with a period of slightly less than the length of a batch and a frequency < 1 MHz

## Slide 28: Instability goes Up and then down with intensity
4.2e10 ppb
4.6e10 ppb
5.0e10 ppb
5.4e10 ppb
5.8e10 ppb
6.3e10 ppb
6.6e10 ppb
7.0e10 ppb

## Slide 29: Peak of instability rate is consistent with electron cloud simulations
Experiment
Simulation

## Slide 30: Direct measurement of electron cloud

## Slide 31: Microwave measurement procedure
Isolate 1 gradient dipole
Shoot an RF wave, measure phase delay
Get an estimate of e-cloud density as a function of time:
  Density at saturation
  Rate of build-up
  Amount of trapped electrons
2 GHz
5.6 m
Dipole
Source
Receiver

## Slide 32: First Data: Seems that what matters is the peak intensity, not the total charge in the beam
ECloud density is consistent with the simulation
Problems:
  High noise
  Unable to make a fast measurement
Chart: Beam Intensity (E12)
| 6.3 | 17 | 41.2
phase delay | 0 | 0.2 | 0.3
Electron cloud | 0 | 7.2 | 10.9
Beam | p per batch | Cloud density (m-3)
41.2x1012: 4+6 batches | 4.12x1012 | 17.9±4.9 x1011
17.0x1012: 4 batches | 4.25x1012 | 20.3±5.8 x1011

## Slide 33: Broadband Schottky noise
90.9 kHz
At 2 GHz
At 200 MHz
Betatron sideband
45 kHz
~ 250 Hz
Synchrotron sidebands

## Slide 34: Improving signal/noise
Addition amplifier in the tunnel
Measure when no beam
Recommissioned old amps from Recycler Schottky detectors
  +30 dB at 2.0 GHz
Put it in the tunnel
Replace the amps if they burn
Triggering hardware to arm the scope already in place, need to reconfigure after shutdown
Need to add fast gating from RF

## Slide 35: Amplifier in the tunnel
Source BPM
15 V DC
1 W Amplifier
Circulator
50 Ω
+ 30 dB @ 2 GHz
1.9 GHz
2.1 GHz

## Slide 36: Can we do anything to reduce the instability?

## Slide 37: Conditioning helps
Chart: Instability threshold increases during the run
| 42309 | 42461 | 42552
Series 1 | 10 | 12 | 0
Series 2 | 0 | 0 | 14
SEY of the beampipe drops down as it conditions
Yi-Chen Ji, ECloud test set up in MI
ξx,y = -6,-8
ξx,y = -2,-2; no inst. below 17 turns at ξx,y = -6,-8
ξx,y = -6,-8

## Slide 38: Stabilization with a clearing bunch
No clearing bunch – the first batch is unstable
Beam: 3 batches of 5.8*1010 ppb
time
long. position (ns)
time
long. position (ns)
4.2*1010
Add a clearing bunch – all bathes stable
Beam: 3 batches of 5.8*1010 ppb
time
long. position (ns)
4.2*1010
At least 5-7 buckets apart

## Slide 39: Summary
The fast instability in Recycler is caused by electron cloud
Combined function magnets trap the electron cloud
  Trapping of the order 10-3 – 10-2 leads to multi-turn accumulation of the cloud
  The cloud reaches much higher densities than in a dipole
An analytical model of the instability has been created
Trapped electron cloud can be cleared out with a clearing bunch
  Need a gap of 5-7 RF buckets

## Slide 40: Current progress
Yes
E-cloud density estimated from the frequency shifts
No
Yes
Complete?

## Slide 41: Time line
Done
Done
Right after the shutdown
Ongoing

## Slide 42: Thank you for your attention
Questions?

## Slide 43: Back-up slides

## Slide 45: Courant-Snyder Parameterization
Consider a ring with a one-turn transfer matrix M
det M = 1
α, β, γ – Twiss parameters
Emittance:
Φ – betatron phase advance
Φ/2π = Q – frequency of betatron oscillations (tune)

## Slide 46: History
1965 INP, Novosibirsk: coherent oscillations and beam losses above a threshold proton intensity of 1-1.5e10 | 1972 CERN ISR, 1988 Los Alamos PSR 1989 KEK: multibunch instability after switching from e to e+
ZGS, Argonne: vertical instability, threshold 2-8e11 proton | CERN SPS: instability different in two transverse planes
Beam intensity (top) and position (bottom)

## Slide 47: Longitudinal Mismatch Leads to an Instability
Injecting a high-intensity batch
  4.5e10 p per bunch
Observe rapid increase of beam center oscillations when bunches shrink longitudinally
  In x-plane only
Damper helps

## Slide 48
Microwave Measurement Schematic
~ 2 GHz carrier signal propagated in beampipe.
The presence of ecloud causes a phase-delay.
Phase modulation at beam revolution freq., 90 kHz.
Ecloud measured in the 90 kHz sidebands of the carrier frequency.
48
Notes: 48
48

## Slide 49
EC in Dipoles Matches Instability
First Batch
Configuration
Second Batch
Configuration
49
Notes: 49
49
49
49

## Slide 50: SEY Measurements at MI (Y. Ji, J. Eldred et al.)
Measurements performed over the course of first 4 months in 2015 (uncoated SS316L shown) demonstrate gradual conditioning due to exposure to the beam
SEY of SS316L with TiN coating is a few % lower (no big effect)
With large grazing angle in B-field SEY can be much higher
Special “scrubbing run” can reduce SEY if necessary
Incident electron energy (eV)
SEY of uncoated SS316L

## Slide 51: SEY depends on the angle
Most particles hit the vacuum chamber at small angles
chamber at small angles
Mean incident angle ~ 15 deg
Effective SEY about 5% higher
1 M. Furman, M. Pivi, Phys. Rev. ST Accel. Beams, Vol. 5, 124404 (2002)
1

## Slide 52: Electron trapping: For some initial velocities final speed close to 0
Equation of motion:
Initial condition: A – phys. aperture, dt – time between bunches
Aperture limitation:
y(t) for different initial vy

## Slide 53: Lifetime is limited by scattering
Residual gas
Coulomb scattering within the cloud
Pressure: p ~ 10-8 torr
Cross-section:
Cloud density2: n < 107 cm-3
Energy ~ 5 eV or less
Energy distribution of secondaries G. Lladarola PhD thesis, dE = 1eV
Overall, τ ~ 1 ms
Scattering cross-section1
1 MacDonald, A. D. Microwave Breakdown in Gases. New York: Wiley, 1966 2 Elded, J. et al, Fast Transverse Instability and Electron Cloud Measurements in Fermilab Recycler, HB’14, 2014
E, eV
E, eV
σc, 10-16 cm2
σc, 10-18 cm2
Pc, cm-1-torr-1
Pc, cm-1-torr-1

## Slide 54: Microwave measurement procedure
Isolate 1 gradient dipole
Shoot an RF wave, measure phase delay
Get an estimate of e-cloud density as a function of time:
  Density at saturation
  Amount of trapped electrons
Use BPMs as antennas
  Signal attenuation < 10 dB
  2 for source – to kill reflections
  1 for receiver
  All BPMs already installed
Elements between source and receiver | 1 gradient dipole
Frequency, polarization | 2 GHz, vertical
Phase velocity in beampipe | 0.37 c
Path length | 560 cm
Number of data points per rev. period | 200
Estimated phase delay, trapped e | 10 mrad

## Slide 55: Parameters of the build-up simulation

## Slide 56: Stripline measurements
Goal: To get some information on the dynamics of fast instability in the Recycler
Can be used as input data to build a model of e-cloud instability
Procedure:
  Turn the damper OFF
  Create conditions for fast instability
  Observe dynamics with and without cleaning bunch

## Slide 57: Stripline measurements: What we did?
Measured:
  Averaged beam position
  Beam intensity
  WCM
  Stripline
Controlled:
  Charge
  Number of bunches
  Bunch rotation (long. mismatch)
  Tune chromaticity
Beyond control:
  Quality of Booster beam
Major source of uncertainty

## Slide 58: Stripline measurements: Looking inside a bunch
Full batch
Close view
Temporal resolution: 0.2 ns
Both horizontal and vertical
Do 1 ns smoothing to remove HF noise
signal
reflection
Stripline
Quaterwave for 53 MHz
Length: 140 cm
Hor. & vert. plates
Sensitivity of log(A/B): 2 mm/dB
Digitizer: 5 points/ns
12 data points
80 bunches

## Slide 59: Analytical model of the instability: coasting beam
Solving the coupled e-p motion
Searching for solutions in the form
Growth rate:
Frequency shift:

## Slide 60: Analytical model of the instability: Input parameters
Parameter | Symbol | Value
Cyclotron frequency |  | 0.57e6 s-1
Betatron tune, frequency | Qx, | 25.45, 14.54e6 s-1
Relativistic factor | γ | 10
Protons per bunch | Nb | 5e10
RF period |  | 18.87 ns
Electron cloud density | ne | 6.1e11 m-3
Coupling frequency |  | 0.23e6 s-1
Build-up rate | λ | 2.65e6 s-1
Landau damping rate | Γ | 0