## Slide 1: Can we use R134a as Cherenkov radiator ?
Yannis & Nikos
16 Nov 2016

## Slide 2: What is the index of R134a ?
Small experiment at PS on T9 beam
Hadron or electron enriched target
Two threshold Cherenkovs A and B
A can be filled with CO2
B can be filled with CO2 or R134a
Beam at + 7GeV/c, -2GeV/c, -3GeV/c
Pressure scan
Fit (n-1), Constant A, muon/e content

## Slide 3
Used positive beam at 7 GeV/c @PS Zone T9
Collimator ± 5mm
Two scintillator counters = Trigger
Two Cherenkovs filled with CO2
Composition collimator wide open:
40%
p 47%
K 5%
e < 1%

## Slide 4
At full efficiency both Cherenkov see 50% of the beam
Pions (hadron enhanced target) and muons from p decays and elsewhere
Very few electrons
Momentum = +7GeV/c

## Slide 5: PM overall efficiency is critical for the index determination

## Slide 6
Cherenkov A filled with CO2 and Cherenkov B filled with CO2 @ 1.2bars
We scan the pressure of Cherenkov A
We measure the (Index-1) CO2 > 418 10-6
and 11% muons in the beam
m content fixed to 0
Momentum = +7GeV/c
F=Sipiexp(-KNphel)
Where Nphel= A L (n-1) (Pressure – Pressure Threshold )
and Pressure Threshold = mi^2 / (2(n-1)p^2)

## Slide 7
Cherenkov B filled with CO2 and Cherenkov A filled with CO2 @ 1.2bars
From literature n-1 = 418 10-6
We scan the pressure of Cherenkov B
We measure (Index-1) CO2 > 414 10-6
and 13% muons in the beam
Momentum = +7GeV/c

## Slide 8
Cherenkov B filled with R134a and Cherenkov A filled with CO2 @ 1.2bars
(Index-1) R134a > 700 10-6
and 11% muons in the beam
Momentum = +7GeV/c

## Slide 9
Cherenkov B filled with R134a and Cherenkov A filled with CO2
Momentum = -3 GeV/c electrons enhanced target
We tuned the Ch-A pressure below the m threshold and we measure :
Nb of e = Ch-A / Trigger = 10.9% in agreement with the fit for Ch-B
Momentum = -2 GeV/c electrons enhanced target
We do not see pions
Ch-A shows 21.7% electrons

## Slide 10
Taking for R134a (Index-1) = 700×10-6
A=32 and Cherenkov length = 200cm

## Slide 11: Conclusion
For the H4 beam we need
A high pressure (pmax=15 bars) Cherenkov to be filled with CO2
A low pressure (pmax=3 bars) Cherenkov to be filled with CO2 or R134a
Below 3GeV/c, only a moderate TOF will save us !