## Slide 1: Microphonics study at FNAL (pCM)
T.Arkan, B. Chase, J.Einstein-Curtis, B.Hansen, J.Holzbauer, E. Harms, J.Kaluzny, A. Klebaner, M. Mcgee, Yu. Pischalnikov, W. Schappert, R.Stanek, J. Theilacker, R.Wang.
January 11, 2017

## Slide 2: Outline
Introduction
System description (Jay Theilacker)
Measurement results
Planned tests
Planned mitigations

## Slide 3: Introduction
Level of microphonics that measured during first cool-down cycle was in 10-20 time large than LCLS II specs (10Hz peak)
FNAL management put together strong multidisciplinary team (LLRF, mech. engineers, cryo-engineers, resonance control experts, etc.) to address problems with microphonics with FNAL pCM.
External source studies were conducted through period of cryoplant shutdown, upgrade and cryoplant turning back on
Microphonics studies on pCM are in progress
Our short list of warm tests on CM2 to help (maybe) reduce the microphonics

## Slide 4: System Description

## Slide 5
The CMTF Cryogenic system has two methods to achieve 2K operation in the cryomodule test stand
  Cryoplant Cold Compressors and Warm Vacuum Compressor
  (2K Refrigeration Mode, 500W capacity)
  Advantages: JT heat exchanger in plant
  Disadvantages: Min. CC flow, Less forgiving, Learning curve
  Cryoplant in Liquefier Mode with Kinney Vacuum Pump
  (Liquefaction Mode)
  Advantages: More forgiving/flexible, Better turndown
  Disadvantages: No JT HX
Fermilab CMTF

## Slide 6: Fermilab CMTF Operating Modes
Kinney Pump
2K
Load

## Slide 7: CMTF Layout
VB
SCP
CMTS
Kinney Header
Cryo Transferline
DB

## Slide 8: pCM Cryogenic Operating History
  2K Plant
    Long recovery from CC trips (learning curve)
    Anxious for data for CM PRR
  4.5K Plant and Kinney Vacuum Pumping
    Could only achieve 2.1K due to pressure drop and high flows resulting from the lack of a JT HX
    Single cavity tests were performed in this mode
  2K Plant
    Single cavity tests at 1.93K
  Shutdown
    Addressed Kinney header ΔP, added LN2 shield cooling to DB, changed CC drives, changed one control valve, added thermal intercept to CM JT valve, added flow meter to Kinney discharge
  4.5K Plant and Kinney Vacuum Pumping
    Current mode at 2K

## Slide 9: Operational Experiences
  Apparent thermoacoustic oscillation (TAO) in CM JT valve
    Added thermal intercept, investigating valve stem wiper
  High flow rates due to high JT valve inlet temperature (no JT HX and TAO)
    Addressing TAO, investigating JT HX possibilities
  Liquid level stability in CM was challenging
    Four contributors:
      Incline
        Design requirement
      high total flow rate
        See previous
      JT flow injection into two-phase pipe disrupting liquid surface
        Adding baffle, increasing JT line size
      apparent flow regime throughout two-phase pipe not as expected
        Researching

## Slide 10: Cryomodule Pipings
Courtesy of T. Arkan

## Slide 11: Measurements and Preliminary Results

## Slide 12: External sources investigation did not find significant contribution sources. Starting from December, 2016 concentration of the efforts shifted from analysis of just vibration measurements from geophones mounted on the different components of CM (with goals to find external source(s) of vibration penetrated inside CM) to studies the correlation between cavity microphonics & cryo-system operational parameters.

## Slide 13: Microphonics tests completed with pCM (during December/ January, 2016/17)
Measurements of the cavities transfer functions (Piezo-to-RF). Objective was to confirm that cavity/tuner system has no low frequency (below 100Hz) resonances. Cavity/tuner TF did not change from HTS studies.
One shift (8 hours) test at T=2K (recorded microphonics on one cavity at a time)/ during 2 hour test JT valve was fully closed for 5 min...
1⁄2 shift ( 4 hours) test at T=2K (recorded microphonics on all 8 cavities simultaneously)
One shift (8 hours) test at T=4K (when cryo-system recovering after Kinney pump trip) – Microphonics at 4K was so large/ data has no value. At the same shift done some efforts to mitigate large (near cavity #1) bellow vibration (analyzing data from geophones)
One shift (8 hours) test at 2K. Stable operation with JT control by AD cryo-control system (2 hours)/fixed position of JT valve/ closed flow to 5K shield / supply He through CD valve...
One shift (8 hours) test at 2K... Regulate Liquid Level into 2-phase pipe through 300mm pipe (Valve PV8AB the AB turn around)

## Slide 14: FNAL pCM Vibration Levels

## Slide 15: FNAL pCM Vibration Levels

## Slide 16: FNAL pCM Vibration Levels

## Slide 17: FNAL pCM Vibration Levels

## Slide 18: Vibration Measurement by Geophone
2-Phase Liquid Level Study
Wed 28 Dec 2016 12:00 to 13:00
JT Observations:
Change in Mass Flow (C:8FTA2) correlation to change in longitudinal (z) JT mid 30 Hz & ~70 Hz response
Geophone Spectrogram
Mass Flow
Mass Flow
M. McGee, et al.

## Slide 19: Vibration Measurement by Geophone
2-Phase Liquid Level Study
Wed 28 Dec 2016 13:00 to 15:15
Mass Flow
Mass Flow
CLL301 – Liquid Level
Longitudinal
Transverse
Cavity Observations:
Longitudinal Response of Cavity 3, 19 Hz signal diminishes with operation of CLL301 beneath 62% Full
Cavity operation directly affected by mass flow with very little transmission to large feed bellows
Bellows
Bellows
M. McGee, et al.

## Slide 20: 2K JT fully closed
Courtsey of Y. Pischanikov

## Slide 21: Upstream Cryomodule Bellows Modification
Rubber
Rubber
Cork
J. Holzbauer, etc

## Slide 22: Upstream Cryomodule Bellows Modification
Spectrum while bellows unconstrained
Spectrum while bellows constrained with rubber padding on collar and in convolutions.
19 MHz line eliminated

## Slide 23: Intermediary Summary
Contribution from cryo-flow is dominant.
Cryogenic mass flow induced vibration happens inside the cryomodule. JLAB pCM results may give us some indication of the differentiation of cryo system effects vs. cryomodule effects
External (outside CM) sources of vibration are less of concern compared to cryogenic vibration sources, but cannot be fully excluded yet. Once cryogenic vibration source is mitigated, external sources may become significant ( below LCLS II spec (10Hz)... )

## Slide 24: Path forward

## Slide 25: Planned pCM Microphonics Studies (1)
Cavities transfer functions (Piezo-to-RF). No low frequency (below 100Hz) resonances. Cavity/tuner TF did not change from HTS studies.
2K with JT valve fully closed for 5 min. Data shown
4K Microphonics was so large/ data has no value.
Mitigate large (near cavity #1) bellow vibration (analyzing data from geophones). 19 Hz line removed.
2K (recorded microphonics on all 8 cavities simultaneously). Analysis in progress
2K. Stable operation with JT control. Analysis in progress
2K. Fixed position of JT valve. Analysis in progress
2K. Close the flow to 5K shield. To be tested.
2K. Supply He through CD valve. To be tested
2K. Regulate Liquid Level into 2-phase pipe through 300mm pipe (Valve PV8AB the AB turn around). Analysis in progress
CM02. Warm. Vibration measurement using Piezos. To be tested

## Slide 26: Planned Cryogenic Studies
2K. Stable operation with cold compressor. To be tested
  Lower temperature of 2-phase supply line
  2-phase supply line vibration
JT valve thermo-acoustic-oscillation. Mitigation to be implemented
Liquid level oscillation

## Slide 27: Proposed plan for passive microphonics mitigation at CM2 (FNAL)
Support the capillary line from upstream end liquid level probe to cavity#1 & #8
Measure with Tuner (piezo-as a sensor) vibration of the 2-phase pipe invar rods clamps. If we will find it important to G-10 supports around the 2-phase for these long invar rods.
Evaluate (measure) transfer function of the cavity #1 (Cavity 1 attached rigidly to heavy gate valve)
Repeat warm/ impulse response of the cavities on the string (using piezo-as-a-sensors) ... review results
Larger diameter JT fill line
1-2 weeks to allow microphonics studies and vibration mitigations

## Slide 28: Summary
More tests are planned.
Mitigations on cryomodule mechanical improvement are considered.
Current focus is on
  Vibrations of 2-phase supply line (Jay Theilacker)
  Helium gas supply temperature at JT valve input (Jay Theilacker)
  TAO in JT valve (ice on the top & correlation of JT valve vibration with cavity detuning)
  Gate valve rigidly attached to Cavity 1
  End cap bellows vibrations
Suppressing microphonics to required levels will need a concerted effort on the part of EVERY group involved in the design and operation of the machine
  Too early to draw any firm conclusions
  Important that FNAL put together strong team with expertise in all aspects (cryo; mech; control; tuners; analysis)
  We collected significant amount of the data/ have detail program for studies/ analyzing data & modifying test plan as we go..
Based on results from microphonics level at FNAL’s pCM assumption that resonance control of SRF cavities in LCLS II linac can be done without active piezo-control looks quite questionable.