## Slide 1
N.Solyak,
SRF workshop, FNAL, Feb. 9-10, 2017
ILC cost reduction (question #4)

## Slide 2: ILC cost distribution
The cost is dominated by the SCRF components and related systems, together with the conventional facilities. These two elements account for 73% of the total.
The main linac itself corresponds to 67% of the total project. Thus investing in a carefully selected main linac R&D should be most efficient in bringing the ILC cost down.

## Slide 3
Distribution of the ILC value estimate by system and common infrastructure, in ILC Units. The numbers give the TDR estimate for each system in MILCU
72%
54%

## Slide 4
Cryogenic heat load and system
Distribution
(ILC TDR)

## Slide 5
Linac systems scales with gradient (length) for fixed Energy
Cavities and CM (incl. materials) = 35.4%
Cryogenic (~90% of total) = 8 % cryo-power G
CFS (x55% of total) = 9%
HLRF (x10% of total -PDS ?) = 1.1 %
LLRF (50%) = 2.3%
Other (instr, vacuum, install, ~50%) ~2.2%
--------------------------------------------------------------
Total ~ 58% = 50 % + 8 %
(possible saving on PDS)
 | Other+ML+cryo | Total %
Gx1; Q0x1,nom | 42 + 50 + 8 | 100 %
Gx1; Q0x2, Q | 42 + 50 + 4 | 96 %
Gx2; Q0x1, grad | 42 + 25 + 16 | 83 %
Gx2; Q0x2, | 42 + 25 + 8 | 75 %
Gx2; Q0x4, | 42 + 25 + 4 | 73 %
Gx2; Q0:2, | 42 + 25+ 32 | 99 %
Assumption:
HLRF –same req. (not true – need modification  cost~2-5% up)

## Slide 6: ILC cost reduction – cost model developed
A simplified cost model has been developed based on the ILC TDR and new progress in the SRF technology on cavity achievable efficiency (Q0) and acceleration (Eacc), showing potential cost reduction estimated to be in the range from 10% (35 MV/m) to 20% (45 MV/m) in ILC operation (with 20% spread).
This recent progress in raising Q of SRF cavities has been driven by large R&D efforts at FNAL and other US labs, and further boosted by the LCLS-II project.
Assumptions:
ML tunnel length and number of CM’s scales as 1/Eacc
Part of cryogenic ~ Eaccα =(0.6-1)
HLRF – same cost (possible saving on distr. system ?)
Other systems – same cost
Q0/2
2xQ0
Q0
Hi-G Q-slope

## Slide 7
C.Adolphsen

## Slide 8: Required modifications of RF components Cost
Longer RF pulse: QL ~Eacc; Tfill~1/QL
  1.65 µs  2.58 µs for 2xEacc
  New reqs for klystron and modulator
FPC power requirements
  P (pulse)~ Eacc; P (avrg)~Eacc*Pulse
Cost increase ???
Strategy: increase beam current ~Eacc