## Slide 1
Sam Posen
GARD-SRF Worksbop
Fermilab
9-10 February 2017
High Gradient Nb3Sn (Long Term)

## Slide 2: High Energy Collider with Gradients >50 MV/m?
If Nb3Sn was developed to withstand fields up to Hsh~0.4 T (transformative), this would correspond to over 80 MV/m
Predicted cost reduction ~30% possible, but requires high Q0 to maintained out to maximum fields
Will be important to keep Rres small – RBCS negligible for Nb3Sn at 2 K

## Slide 3: High Energy Collider with Gradients >50 MV/m?
If Nb3Sn coatings were developed to withstand fields up to Hsh~0.4 T, this would correspond to over 80 MV/m
Predicted cost reduction ~30% possible, but requires high Q0 to maintained out to maximum fields
Will be important to keep Rres small – RBCS negligible for Nb3Sn at 2 K

## Slide 4: 4.2 K ILC?
Other advantages (Tom Peterson):
  Increased reliability of the cryogenic plant, since cold compressors are not used
  Reduced risk of air leaks causing contamination of the helium (no subatmospheric volumes)
  Relatively easy and fast capacity adjustment to load changes; good turn-down capability
  Less expensive infrastructure (no 2 K cold box, no cold compressors)
  No superfluid leaks
Primary advantage: 3-4x higher efficiency  Smaller infrastructure costs and reduced power consumption

## Slide 5: Calculation of Cost Reduction for 4.5 K ILC
Based on analysis by Tom Peterson
Assumptions:
  Same ILC spacing, distances, and layout
  No changes in heat load estimates other than the one small change eliminating 2.0 K support post heat
  Remove all 2.0 K features including the 2.0 K cold box - 33% of original cryoplant cost (agrees with LHC design report)
  Required capacity for each cryogenic unit is calculated assuming 4.2 K operation and given Eacc and Q0
  Scale the cost of that 4.5 K cryogenic system by heat load to the 0.6th power

## Slide 6: 4.5 K ILC?
2.0 K
4.5 K
4.5 K system helps reduce cryogenic costs (analysis by Tom Peterson).
Analysis is specific to ILC, but representative of significant cost savings for machines large and small that would benefit from high gradients.
Need to understand impact to thermal stability at 4.5 K