## Slide 1: Transformational SRF routes – intro thoughts
Alexander Romanenko
GARD-SRF Workshop
9 Feb 2017

## Slide 2: Goal – how to probe and push the limits of gradient and Q?
Gradient
  Conventional wisdom is that superheating field (~55 MV/m for clean Nb) is the “hard” limit
    What is meant by “limit”?
    Is the ”limit” directly confirmed by any experiments?
      We need to explore it
    What if we remove a CW constraint?
    Can we slow down/make penetrating flux not to lead to quench?
      Need to probe/explore the relevant timescales (<1 nsec)
      Can we take advantage of layered structures from this point of view?
  If we can sustain RF fields up to Hc2 -> 100 MV/m
  Up to Hc3 -> 300 MV/m (EP+120C bake)
  Above Hc3?

## Slide 3: Up to what fields does superconductivity exist in the walls?
EP+120C
300 MV/m
200 MV/m
T=2K

## Slide 4: One established way to probe gradient limits
N. Valles, PhD thesis

## Slide 5: Q factor
Quality factor
  For 2-1.8K operation, we discussed in previous session how to dramatically abate BCS resistance (doping, Nb3Sn)
  The highest Q factor (at T->0)we can achieve is limited by residual resistance
    If we understand/control the origin of the remaining Rres after flux, hydrides etc are removed – can Q be infinite at low enough T?
      NB: DC conductivity is infinite in SC
      This is unique for SRF
    Would it be useful for accelerators?
    Certainly will be for non-accelerating applications
  How to address it?
      One example: STM, PCT - is density of state different from the “ideal” BCS?