## Slide 1
Martina Martinello
GARD SRF Workshop 2017
What are the state of the art and the new ideas to pursue abatement of field emission in vertical test and cryomodules?

## Slide 2: State of the Art: Plasma Processing at SNS
In-situ removal of hydro-carbons via Ne-O2 plasma processing
  <> increases ~ 21%
  Ex:CM00012
  <> = 12.3 MV/m before PP
  <> = 15.3 MV/m after PP
  Significant reduction of radiation level
  Increasing the work-function
3 cryomodules successfully processed at SNS
20-30% increase in

## Slide 3: State of the Art: Plasma Processing at SNS
In-situ removal of hydro-carbons via Ne-O2 plasma processing
  <> increases ~ 21%
  Ex:CM00012
  <> = 12.3 MV/m before PP
  <> = 15.3 MV/m after PP
  Significant reduction of radiation level
  Increasing the work-function
3 cryomodules successfully processed at SNS
20-30% increase in
Successful technology to mitigate field emission and increase the maximum accelerating gradient without disassembly and re-assembly the cryomodule at prohibitive cost

## Slide 4: Mid-Term Goals: Plasma processing for LCLS-II
Present
Applicability of SNS plasma processing to LCLS-II
Design of RF and vacuum system
Goals
Plasma processing of 1.3 GHz single-cell cavity
RF test in VTS
Goals
Plasma ignition in 9-cells cavity
Plasma processing and RF test of 9-cell cavities in VTS
Improve maximum of field emitting cavities
Goals
Plasma ignition in 9-cells cavity
Plasma processing and RF test of 9-cell cavities in VTS
Goals
Plasma processing in-situ in a cryomodule-like environment (HTS)
Monitor of plasma ignition based on resonance shift
Goals
Plasma processing in-situ in LCLS-II cryomodules
Improve maximum of ~ 15-20 %
Goals
Plasma processing in-situ in LCLS-II cryomodules
2017
2018
2019
2020

## Slide 5: Long-Term Goals: Extension to other accelerators
2017
2018
2019
2020
PLASMA PROCESSING FOR LCLS-II
Single-cell
9-cells VTS
9-cells HTS
LCLS-II cryomodules
PLASMA PROCESSING FOR HIGH GRADIENT MACHINES
2018
2019
2020
Studying more aggressive plasma mixtures
  Eliminate/Smooth metallic contaminants
  Improve effectiveness of the process to all kind of field emitters
Processing of cavities with different frequencies/shapes
Defining guidelines to develop plasma-processing friendly cryomodule
2021
2022