## Slide 1
Learning from Samples
C. Reece
Objective: Rs(T,f,H) sample measurements
  The biggest impediment to rapid progress in material/performance understanding and process feedback
  JLab – “SIC” system – 7.5 GHz
    Convenient sample size, two tests/week
    Good for high Tc material development
    Not useful for residual resistance studies
  CERN QPR -1 – 400, 800, 1200 MHz in use,
    few samples per year – nice precision
    Difficult/expensive samples
  HZB QPR – in use, student project, not fully commissioned
  CERN QPR -2 – redesigned, anticipate commissioning 2018
  JLab + ODU partnership would like one
    325, 650, 975, 1300 MHz - would adapt CERN new design
    Easy cryogenic and rf support at JLab
    Many uses – fundamental, detailed materials study
      Doping, Nb3Sn, peak fields, multi-layers, other A15, MgB2…
    Need funding: ~$250k