## Slide 1
P. Piot*
IOTA/FAST 5th Users’ meeting
June 6, 2017
* Joint appointee with Northern Illinois University
Other linac-based experiments downstream of the cryomodule

## Slide 2: Research opportunities at the FAST e-injector
FAST/IOTA supports collaborative research opportunities with Universities, National labs, and Industries
e-injector can support research relevant to other (than HEP) programs within DOE:
  NP: electron-cooling, phase space manipulations, magnetized beam in IOTA
  BES: formation and diagnosis of bright e- beams, phase-space manipulations, electron-laser interactions
  NNSA: tests of subsystems for MARIE (LANL)
e-injector has been (and is being) leveraged to secure funding outside of DOE: e.g. NSF, DOD, DHS.

## Slide 3: The IOTA/FAST Overview
Key Components of FAST e-injector:
  Photoinjector electron source:
    50 MeV beams
    Flexible beam parameter
  SRF linac:
    Up to 300-MeV
    Stabilized bunches
  Extensive suite of diagnostics
  Real-estate for experiments
SRF linac
SRF cavities
~300-MeV e- injector section
RF gun
2.5 MeV p source
test beamlines
beam
dumps
IOTA
Bunch
compressor
laser

## Slide 4: Experiments
Acceleration to 300 MeV!
  Beam characterization
IOTA-related tests:
  Beam diagnostics
  Preparatory tests of subsystems for OSC
Multi-bunch wakefield (B. Carlsten’s talk)
Gamma-ray source via ICS
Longer term
  Radiation/laser-based beam manipulations,
  Interaction with crystals
  Application of flat beams
  Advanced acceleration/manipulations

## Slide 5: Acceleration to <300 MeV
The 50-MeV beam is accelerated in a cryomodule (8 SRF cavities)
Produced stable beams with energies up to 300 MeV arranged as macropulses.
IOTA requires ~150-MeV e-beams
[E. Harms, et al. SRF2015 (2015)]
ILC goal
Adapted from Elvin Harms

## Slide 6: Acceleration to <300 MeV: beam optics
Extensive models of the beamline.
Nominal lattices available in ELEGANT (D. Broemmelsiek)
ELEGANT used for single-particle optics.
ASTRA & IMPACT-T used for the injector.
IMPACT-T & IMPACT-Z used for the entire beamline.
Start2End simulations and optimization performed with py-based GlueTrack (initiated at DESY).
all ELEGANT lattices available at https://github.com/NIUaard/FAST
200 pC
BC1 off

## Slide 7: IOTA-related tests using D600 dipole magnet
Imaging of SR for beam profile monitor for IOTA (Romanov, et al.)
Single-photo detection using PMT (Stancari, et al.)
Spectral measurement at 2 mm + amplification (Andorf, et al.)
Energy (MeV) | Critical wavelength (nm) | photons in BW (%) | Energy flux per e- (J)
100 | 2734 | 15.8 | 2.66e-22
150 | 810 | 7.2 | 1.21e-22
200 | 342 | 3.0 | 5.0e-23

## Slide 8: Test of OSC-experiment subsystem
OSC will operate in the [2200,2900] nm spectral range
Amplifier medium is a Cr:ZnSe pumped by a Thulium laser.
Recently procured all the components necessary to assemble the amplifier.
We are trying to get ready to perform an experiment in the summer demonstrating amplification of synchrotron radiation around ~2500 nm.
M. Andorf, et al., CLEO’17 https://doi.org/10.1364/CLEO_AT.2017.JW2A.90

## Slide 9: Inverse-Compton Scattering for high-flux gamma-ray production (funded by DHS DNDO-ARI)
Use a conventional superconducting radiofrequency (SRF) linear accelerator which readily produce electron bunches at high frequencies.
Develop a recirculation optical cavity to collide the e-bunches and laser pulses at high rep. rates
  upgrade the laser currently available,
  design and install a suitable interaction region.
Combine SRF linac with optimized optical cavity to produce high-flux g rays (we anticipate Watt level average power)
FAST 3000 bunches
FAST 1 bunch
[F. Hartemann et al. PRSTAB 8, 100702 (2005)]

## Slide 10: Overview of the proposed experiment
highlighted yellow boxes indicate the subsystems to be developed in support to the ICS g-ray experiment
IR
IR transport
UV

## Slide 11: g-ray brightness optimization
Brightness in phot./sec/mm/mrd/0.1% BW
# of g photons
# of collision per sec
1 to 15,000 at FAST
# of g photons
# e-
# colliding photon
sizes of colliding laser (L) and electron(e) beams
suppression factor <1
D. Mihalcea et al., to appear in NIMB http://dx.doi.org/10.1016/j.nimb.2017.03.140

## Slide 12: Anticipated performances
g-ray parameters
e- & laser beams parameters

## Slide 13: Beam dynamics Considerations
ELEGANT matching + Impact-T tracking over the ~120 m (space- charge included only)
Final focus needs to be compact and use PM quadrupole magnets
Vibration is an issue

## Slide 14: Possible interaction area
Interaction region foreseen downstream of D600
  Small-aperture permanent quadrupole
  Decoupled from transport to HE dump /injection to IOTA
Vibration measurement to be incorporated in design
e-beam
IR laser
e-
beam
[Design by A. Khizhanok, MS thesis in Dept. of Mechanical Eng., NIU
Adviser: J.-T. Gau]
to
dump

## Slide 15: Progress on laser upgrade
Current laser system was optimized (J. Ruan, et al.)
1st amplifier received from Northrop-Grumman to be tested (part of M. Urfer MS thesis)

## Slide 16: ICS timeline (still in discussion)
1st interaction planned in 2019
Summer 2017:
  Characterize beam downstream the cryomodule (especially transverse emittance & energy spread)
  Commission the laser amplifier and demonstrate E>0.5 mJ
  Finalize design of the optical cavity
Fall 2017
  Manufacture PMQ
  Build optical transport line?
Beyond
  Finalize and construct interaction area with associated diagnostics, test some diagnostics when beam time available

## Slide 17: Possible longer-term experiments: laser/radiation-based manipulations
Capitalize on the infrastructure available from the ICS
  High-energy laser pulse
Optical- or self-manipulation of e beams
  OSC R&D (UR interference)
  Energy/density modulation (optical-replica diagnostics, …)
  Controlled chromatic aberrations aka beam conditioning (Zholents PRSAB 2005)
  Radiation sources
  Longitudinal-space-charge amplifier
[P. Piot, NAPAC16]

## Slide 18: Possible longer-term experiments: LSCA
Cascaded longitudinal space-charge amplifier was investigated in FAST using start-to-end simulations (simplified model)
[H. Halavanau, 10.1016/j.nima.2016.03.002

## Slide 19: Final comments: other opportunities being explored
Compatibility of high-repetition-rate beam driven acceleration concept (e.g. DWFA)
Resuming the channeling radiation experiment in collaboration with MEPHI, IPN Lyon, U. Ferrara.
Applications of ultra-relativistic flat beams (see Halavanau’s talk):
  Acceleration in DLAs (ACHIP collaborations)
  Diving wakes in planar structures
  Micro-undulator tests
Summer16 CR experiments
1 bunch
200 bunches
energy
Wakefield due to a bunch train in a DLW
[F. Lemeny, P. Piot @PITZ]