## Slide 1: JT Valve Outlet Line
Jay Theilacker
pCM Testing Review Workshop
January 11, 2017

## Slide 2: JT Valve Addition to Cryomodule
  Heat load of CW operation required a JT valve per cryomodule
  Tunnel incline required the two-phase pipe to be increased to the largest practical size that would fit in the cryomodule without a 5K shield
    A flat liquid surface takes up 60% of the two-phase pipe cross section
    This leaves less than ±20% for operational regulation
  Based on LHC R&D, it was thought that the liquid surface would be “still” under design conditions
  The outlet of the JT valve was routed upstream before injection into the top of the two-phase pipe in order to avoid possible entrained liquid from leaving through the Line B riser

## Slide 3: JT Valve Line and Two-Phase Line Observations
  Top of JT valve ices up
    Thought to be thermoacoustic oscillations
    The pCM JT valve did not have a thermal intercept
  pCM operation at CMTS has lower liquid quality due to the lack of a JT heat exchanger
    Higher vapor flow in the JT valve line
    Higher vapor flow in the two-phase pipe between JT valve injection and the Line B riser
  Vapor velocity in 0.5” JT line
    LCLS-II - 19 m/s (25% of the speed of sound)
    CMTS - >57 m/s (>70% of the speed of sound)
  JT injection into two-phase pipe may be disrupting the liquid surface
  Vapor flow appears to be dragging liquid surface down stream on its way to the Line B riser

## Slide 4: Line A, B and G Configuration

## Slide 5: Apparent Liquid Sloshing

## Slide 6: Possible Improvements
  Apparent thermoacoustic oscillation (TAO) in CM JT valve
    Added thermal intercept (didn’t help)
    Investigating valve stem wiper with valve vendor
    Turn valve around
  Liquid level stability in cryomodule
    JT flow injection into two-phase pipe impeding liquid surface
        Adding baffle
          Prevents injection flow from impinging the liquid surface
          CFD analysis has been performed
        Increase JT line size
          Reduces velocity in tube and injection point
          Should reduce potential for vibration in JT line
          Space constraints make it difficult to increase line beyond 1”
            LCLS-II conditions – 4% of the speed of sound
    Need to further investigate flow regime throughout two-phase pipe
        Revisit LHC research

## Slide 7: Baffle at JT Injection

## Slide 8: Design for Increased JT Line Size

## Slide 9: Possible Problems
  Increasing JT line size
    Will lower velocities result in liquid/vapor separation in the tube?
      Separation in the tube could be a problem since the tube is going uphill
  Duplicating LCLS-II vapor velocity in two-phase pipe
    Verify that “lifting” liquid surface does not occur at LCLS-II conditions
      Need data from Jlab with JT heat exchanger
      Consider adding JT HX to CMTS

## Slide 10: Backup

## Slide 11: Operational Experiences

## Slide 12: Liquid Level Instability