## Slide 1: Coupler Performance at FNAL pCM
LCLS-II pCM Test Review Workshop
JLAB, January 11-13, 2017
Nikolay Solyak (on behalf LCLS-II team)
Nikolay Solyak (on behalf of LCLS-II team)

## Slide 2: Outline
Power requirements
Coupler diagnostics in pCM
Coupler tests results at 3.5 and 3.2 kW
FPC static and dynamic heat load
Lessons learned
Changes in production CMs

## Slide 3: LCLS-II Power requirements for main coupler
RF Power vs. Beam current: 16MV/m; QL=4e7; ΔFpk=10 Hz
Forward
Total
Reflected
 | (peak / avrg) | 
 | 0.1 mA | 0.3 mA
16MV/m | 4.6 | 6.4 / 5.7
 | 0.1 mA | 0.3 mA
16MV/m | 4.6 | 6.4 / 5.7
QL=4.e7; detuning ΔF=10Hz
E= 16 MV/m; 0.3mA; QL=4e7
Average =5.7kW
=6.4kW
Dissipation in coupler ~ Ptot. Max Temp depends on reflection phase.
In pCM coupler power increased to Pt =7 kW and 6.4kW (2·Pf) by tuning QL ~1.e7
In HTS coupler tested up to Pt = 8kW
Total Power in coupler (QL=4e7, ΔFpk=10 Hz)

## Slide 4
Coupler and cavity end-group diagnostics
(2,4,6,8)

## Slide 5
Location of T-sensors
Cernox on FPC 5K tube
Cernox on cavity beampipe
PT100 on CF100 flange (50K)
RTD stycasted to the HOM.

## Slide 6
Main coupler tests in pCM
Room temp. power processing (couplers #1 thru #7): 2.5 to 4 kW
Coupler #8 was processed at 4kW with cavity OFF-resonance (2.1K)
All couplers are tested at cold, P= 3.5 kW & 3.2 kW (~12-20 hrs)
      QL =1.e7 (tuned to low Qext for low cavity gradient )
      Cavity gradient 10-12 MV/m
      All couplers in pCM are TTF3 modified (different from production)
Coupler #4 was retested at 2K (13hrs). From other couplers data are taken from cavity Q0 measurement runs (0.9 kW and 1.6kW)
Test result summary:
Max temperature at 50K/5K intercept ~200K/20K at 3.5 kW.
No overheating of cavity beampipe  small effect on Q0
Improved design will be tested at JLAB pCM (production version)

## Slide 7
High field operation

## Slide 8
Interlock=200K
Interlock=250K

## Slide 9
Coupler #4: Power = 3.5 kW
Interpolation to equilibrium:
Coupler #5: Power = 3.5kW
Tmax=222 K
Tmax=209 K

## Slide 10: Extended tests at 2K
Cavity Gradient
steps = 16/14/12 MV/m
#4; #6; #1; #2; #3; #6; #7
RF power:
1.65 /1.25/0.9 kW
(variation < 10%)
CF100 flange
Tmax = 115-128 K (at ~0.9 kW)
Gradient MV/m
Temp of CF100

## Slide 11
Extended test of the main coupler #4 (2K)
Power 3.2kW
Duration ~13hrs
TCT100 = 208 K
Consistent with 2.1K result
RF power =3.2kW
Gradient=11.510 MV/m
TCT100

## Slide 12
Summary of coupler heating
Different thermal intercept configuration in HTS
Coupler#4
50K
5K

## Slide 14
pCM
pCM
pCM
Waveguide/RT flange cooling condition
  No air cooling in pCM
  Dry nitrogen cooling in HTS

## Slide 15: HOM coupler: static and dynamic heating
Conclusion from pCM measurements and simulation:
Static heat load to 2K < 0.15 W
  FPC ~ 50mW
  HOM+FP cables < 100mW
Dynamic heatload (2K) < 1.2 W
  bellow < 150mW @16MV/m
  FPC @3.5kW < 1W
HOM-can
HOM-can
HOM-feedthru
HOM-feedthru
Acnet name | Location | cavity |  |  |  |  |  |  |  | Note
 |  | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | 
CT116 | Cav BeamTube (coupler) | 2.51 | 2.38 | 2.29 | 2.38 | 2.63 | 2.32 | 2.38 | 2.81 | 
CT121 | HOM can (coupler) | 2.41 | 2.34 | 2.26 | 2.31 | 2.30 | 2.25 | 2.31 | 2.87 | 
CT120 | HOM feedthru (coupler) | 6.43 | 5.35 | 5.02 | 5.29 | 4.97 | 5.28 | 5.90 | 5.30 | Heated by 2.5m cable
CT117 | Cav BeamTube (tuner) | 5.01 | 5.47 | 2.85 | 2.84 | 10.73 | 4.64 | 2.71 | 2.35 | 
CT119 | HOM can (tuner) | 2.68 | 2.24 | 2.31 | 2.24 | 2.83 | 2.38 | 2.20 | 2.22 | 
CT118 | HOM feedthru (Tuner) | 4.30 | 4.59 | 4.43 | 4.05 | 3.96 | 4.04 | 4.26 | 4.35 | Heated by 3m cable
Static temperatures (no RF power)

## Slide 16
FPC&HOM Couplers 2K Heat Load (CTS/COMSOL analysis of pCM)
T-map (QFPC = 1.2 W)
Temperature Profile along the 5K Tube
QFPC = 1.2 W
QFPC = 0.8 W
QFPC = 0.4 W
QFPC = 0.2 W
QFPC = 0.05 W
QFPC = 0.1 W
Static heat load
Dynamic heat load
P=55 mW @10MV/m
A.Lunin
Total 2K Heat Loads from FPC & HOM Couplers in the LCLS-II pCM (based on T-meas: FPC/HOM/BP)

## Slide 17: HOM and FP performance at FNAL pCM
Cavity | HOM1 Qext | HOM2 Qext | Field Probe Qext | HOM1 Power @16MV/m (W) | HOM2 Power @16MV/m (W)
TB9AES021 | 1.6e13 | 5.0e13 | 2.04e12 | 0.017 | 0.005
TB9AES019 | 3.8e13 | 1.1e12 | 8.26e11 | 0.007 | 0.248
TB9AES026 | 3.0e12 | 6.5e12 | 7.48e11 | 0.091 | 0.042
TB9AES024 | 4.5e13 | 2.7e12 | 7.40e11 | 0.006 | 0.101
TB9AES028 | 5.0e11 | 2.4e12 | 4.61e11 | 0.545 | 0.114
TB9AES016 | 8.1e11 | 2.6e12 | 1.07e12 | 0.336 | 0.105
TB9AES022 | 1.8e13 | 1.3e12 | 5.48e11 | 0.015 | 0.210
TB9AES027 | 6.8e11 | 1.4e12 | 1.60e12 | 0.401 | 0.195
Specification: HOM Qext > 2.7e11 and 1 W maximum
All have < 1W @ 16MV/m
At 20 MV/m, P_HOM ~ 1.56 W specification.
Tuner side
Coupler side

## Slide 18
HOM performance: Effect of RF losses in HOM cable
HOM power heat cable  heating of HOM antenna & FT  antenna quench
Expected HOM power from 0.3mA beam < 5W, system designed for 10 W.
Cav#8 HOM1 cable (coupler side) powered at 2GHz up to 5W, full reflection Ptot=10W
HOM FT
HOM1 can
Beam tube
Gradient 16MV/m
Test Summary
No antenna/FT overheating
FT static T=5.3K (<50mW from cable)
RF power in cable 5.1W; ΔTFT< 0.9K. - Same ΔTFT for 16MV/m
Temp of HOM can & beampipe is not sensitive to cable heating; ΔT<0.04K
At 16MV/m: ΔTHOMcan~0.3K; ΔTbeampipe~ 0.4K (FPC power & Eacc)

## Slide 19: Lessons Learned
Coupler warm conditioning may causes cavity surface contamination  MP
Coupler has acceptable 2K heat load (<1W @ 3.5kW), even at relatively high temperature of the 50K/5K intercepts (~200K/20K).  small Q0 degradation due to FPM heating.
FPC thermal intercept design is improved in production CMs, incl. JLAB pCM. (next slide)
Antenna heating changes QL ~10% (16MV/m) at ~10 hrs timescale
HOM coupler performance meet specification
  Power leak < 1W at 16MV/m
  Small static heat load from HOM cable
  Cable can handle up to 10W of HOM power w/o overheating antenna

## Slide 20
Thermal intercept improvements in production CM (vs. pCM)
Use XFEL FPC design (vs.TTF3 in pCM). Better AL can -flange thermal contact
Thermal strap is connected close to 50K pipe (vs. 50K shield-see thermal analysis)
Better thermal contact between braid and copper extension (flat surfaces)
JLAB pCM already has this feature
pCM: Thermal analysis – R.Fischer/ANL
zoom
5K thermal
Intercept
50K thermal
intercept
pCM
Production CM
120K
110K
55K
150K

## Slide 21
Summary
No multipactoring, trips at FPC upto 4kW cw
See overheating on 50K and 5K flange at 3.5kW.
- Max Temp 220 (50K) and 20K at 5K
Effect of overheating on cavity Q0 looks small (<10%), simulations and T-map predicts power to 2K ~0.3-0.8 W
Thermal intercept improved for in production CM (and JLAB pCM)
HOM performance meet specs. Cable heating up to 10W not limit HOM performance

## Slide 22
Back-Up slides

## Slide 23: Simulations
Pin=3.5kW, 10um on outer, 150um on inner, roughness 10%, ε=9.8, tan=3e-4
320 K
220 K
320 K
320 K
Tmax ~ 430 K
TIR ~ 390 K
15 K

## Slide 24
WG flange float
SLAC -3D simulations; 3.5kW pCM conditions
TIR=370K
Tmax=391K

## Slide 25: Total Heat Load Results @ Qin=1e7 w/o Radiative Cooling in Cold Section
Pin=3.5kW | Temps (K) | Power (W)
Cavity Beam Pipe | 3.4 | 0.13
5K Copper ring | 22 | 1.21
CF100 Al plate | 220 | 15.2
300 K flange | 300 | 1.71
WG flange | 300 | 5.24
Max. T | 384 | Total: 23.49
Pin=3.5kW | Temps (K) | Power (W)
Cavity Beam Pipe | 2 | 0.025
5K Copper ring | 10 | 0.754
CF100 Al plate | 100 | 14.35
300 K flange | 300 | 1.0
WG flange | 300 | 4.66
Max. T | 339 | Total: 20.79
Ideal case As Ref.
FNAL pCM case.

## Slide 26
Simulation results for HTS condition: 4kW, cavity ON-resonance
Simulation of 4kW cavity on-resonance with the last set of parameters from table. Nominal parameters are: 10/100um copper plating, no roughness, e=9; tan=3.e-4; RRR=50 (ASE included RRR=35).
Test result