## Slide 1: Summary Notes for pCM testing
M Drury, G Wu

## Slide 2: Minimum Acceptance Criteria Review
Vacuum specification
  Fermilab pCM beam line vacuum is 5e-10 torr.
  JLAB pCM beam line vacuum is 1e-11 torr.
  Acceptance specification for beamline vacuum is 1e-10 torr.
Microphonics specification
  It is facility dependent. Not appropriate for acceptance criteria.
  However, excessive microphonics like current cryomodules are not acceptable.

## Slide 3: pCM Testing Issues
Processing of low performing cavities.
  12 MV/m is acceptable if total voltage meets specification of 128 MV.
  Processing may be possible, but carry risks.
  Processing requires case by case evaluation
Testing Schedule
  Calibrations may be able to skip due to repeatability
  Operator available at FNAL during off hours.
Raise admin limit to 21 MV/m
  Due to SSA and FPC coupling
  Require case by case evaluation when in doubt
  Fermilab limit was 20 MV/m
  Jlab limit was 19 MV/m
Operational Eacc 0.5MV/m below quench limit.

## Slide 4: Testing Schedule
Fermilab reported production test schedule can be met based on pCM test schedule and testing time allocation
  Calibrations may be able to be skipped due to repeatability
  Operators are available at FNAL during off hours.
JLAB is still evaluating experience of pCM testing

## Slide 5: Cavity Performance
Fermilab pCM experienced multipacting consistently
  Decided not conditioning coupler at room temperature or cold.
  The copper plating in coupler tends to have high concentration of hydrogen
  Fermilab tested Nitrogen filled single cell cavity and ruled out nitrogen residual gas as a potential cause for multipacting.
  Fermilab is studying effect of hydrogen residual gas on multipacting
  Fermilab pCM exceeds total voltage, heatload specification
JLAB has no multipacting during the initial gradient test
  JLAB did not condition the coupler
  Will investigate whether CAV4 quench can be processed to confirm multipacting or not.
  Cavity testing is in progress

## Slide 6: Coupler performance
Fermilab reported power couplers exceed specification
  2K test confirmed the 2.1K measurement
HOM antenna and cable heating was tested simulating 5W beam power. Heating was very small and did not degrade cavity performance.
JLAB reported 4 couplers has low Qext that cannot be adjusted
  Use stub tuners to reduce coupling (raise Qext)
    Cavity 2 raised from 1.8E7 to 3.9E7 –working well
    Duplicate the setup for other three couplers. (CAV8 may have some issues)
  Fix the mechanical component during next warm up.

## Slide 7: JLAB Cryogenic
CAV5 flux gate reads 4.5 mG
First cooldown was very slow. Issues resolved to allow faster cool down in future.
Inlet JT T swings, but will improve after JT HX works.
  Current inlet T is 4-5K average.

## Slide 8: Fermilab Cryogenics – vibration consideration
Warm mode (kinney pump) bypasses the heat exchanger that resulted 2-phase flow >4.5K at inlet. By the time it reaches CM, liquid percentage suffers a big loss. More gas turbulence is expected with high flow rate.
0.5” JT line further increased the flow velocity
  19m/s for LCLS-2 design
  57 m/s at CMTF (70% of sound velocity)
JT experienced Thermal Acoustic Oscillation (TAO).
  Thermal strapping of the JT out shell did not solve the icing problem.
  According to JT valve vendor, there is a removable stem wiper from vendor can be used to retrofit the current JT valves.
  Increase JT line size is being considered.
    Need to know velocity of large diameter JT line.
  Turn JT valve around is another option which will be evaluated.
Cooldown line heater: have large leads that may have high thermal leak. Leads shield station to the 40K shield.
Check the valve in feedcap between 300mm pipe and 2-phase. That does not seem to have a problem.
Liquid level instability
  Vapor flow dragging the liquid to the riser and to the down stream.
  Baffle installed to avoid direct spraying of 2-phase flow to liquid surface

## Slide 9: Fermilab pCM Microhonics
Fermilab reported microphonics measurement
  Mass flow matched harmonic of the frequency detuning.
  Highly correlation between mass flow and microphonics were found
JT icing is completely abnormal. No conclusions should made until this is solved. (T. Peterson)
Alternatively, there maybe other method to prevent TAO
  Check the holes in the JT valve.(E Daly)

## Slide 10: JLAB pCM Microphonics
Two cavities were measured
  Limited data
  Preliminary data show CAV3 has 70 Hz pp and CAV4 has 20 Hz pp
Cryomodule is leveled.
Low flow rate was seen in JLAB pCM
Much less JT icing was observed.

## Slide 11: JLAB C100 Experience on Microphonics
C100 experience show great details of microphonics and how they are mitigated.
  Adding weight
  Stiffen the structure
  Waveguide anchoring to the wall and stone filling at penetration.
  Mostly caused by external sources
  No microphonics were contributed by high heatload related mass flow
    The cryogenic supply is more forgiving since there are three supplying points
Typical 30Hz pp
Increased the tuner plate thickness that showed great effect of microphonics reduction

## Slide 12: JLAB pCM modal measurement
Accelerometers were installed and vibration were measured
  Data is being analyzed

## Slide 13: Microphonics action items
JLAB verifies the JT icing when mass flow is elevated.
JLAB measures pCM microphonics as soon as possible
  Priority: JLAB measures CAV1 microphonics when flow is as is.
  Priority: JLAB measures CAV1 microphonics when flow is higher (5 g/s, 8 g/s)
    Use heater to raise mass flow.
Fermilab
  Continue to analyze data and complete the remaining tests
  Implement JT valve TAO mitigation as soon as possible on Fermilab pCM
  Implement cryocircuit design changes on Fermilab CM02
  Cryo Flow optimization as soon and as practical as possible for FNAL cryo