## Slide 1
Accelerator Division Status
Daniel Johnson
All Experimenters’ Meeting/Lab Status Meeting
23 January 2017

## Slide 2: Content Slide [22pt Bold]
Bullet points are optional. If preferred, only first level bullets can be used or bullets can be set to “NONE.” [18pt Regular]
First level bullet [18pt Regular]
  Second level bullet [16pt Regular]
    Third level bullet [15pt Regular]
      Fourth level bullet [14pt Regular]
        Fifth level bullet [14pt Regular]

## Slide 3: Accelerator Operations Summary
From: January 09, 2017 (0000 hours)
To: January 16, 2017 (0000 hours)
Calendar Week # 02
NuMI Weekly Integrated Intensity 1.17 E19 protons
Beam Hours To NuMI 116.6 hours
BNB Weekly Integrated Intensity 8.39 E18 protons
Beam Hours To BNB 142.0 hours
NMuon Weekly Integrated Intensity 1.18 E16 protons
Beam Hours To NMuon 41.2 hours
MTest Weekly Integrated Intensity 1.63 E13 protons
Beam Hours To MTest 21.9 hours
MCenter Weekly Integrated Intensity 0.00 E12 protons
Beam Hours To MCenter 0.0 hours

## Slide 4: Accelerator Operations Summary
From: January 16, 2017 (0000 hours)
To: January 23, 2017 (0000 hours)
Calendar Week # 03
NuMI Weekly Integrated Intensity 1.48 E19 protons
Beam Hours To NuMI 134.9 hours
BNB Weekly Integrated Intensity 7.01 E18 protons
Beam Hours To BNB 148.1 hours
NMuon Weekly Integrated Intensity 9.71 E15 protons
Beam Hours To NMuon 77.8 hours
MTest Weekly Integrated Intensity 6.12 E13 protons
Beam Hours To MTest 25.2 hours
MCenter Weekly Integrated Intensity 4.80 E11 protons
Beam Hours To MCenter 1.7 hours

## Slide 5: NuMI Operation

## Slide 6: BNB Operation

## Slide 7: Content and Caption Slide [22pt Bold]
Click to add caption text [13pt Bold]
First level bullet [18pt Reg]
  Second level bullet [16pt]
    Third level bullet [15pt]
      Fourth level bullet [14pt]
        Fifth level bullet [14pt]

## Slide 8: Complex Status
LINAC
  Running well
  Testing Marx modulator on LRF5
Booster
  Running well
  New shielding assessment
MI/RR
  Slipstacking 6+6
  Tuning
NuMI
  Running at ~630 kW with Switchyard
  Ran at ~690 kW without Switchyard
Booster Neutrino Beamline (BNB)
  Running well
Switchyard
  MCenter, MTest, and SeaQuest
  Beam available
General
  No Downtime Planned
    Next Downtime in late February or early March
    Coordinating downtime with MSS commissioning

## Slide 9: MI-12 Communication Duct
Summary
Emergency Repair Plan In Place
  Need 2 hour notification
  Vendor has cable
New Communications Duct Plan
  Communications duct installation
    New duct installed
  New fiber cable has been delivered
    Electricians notified
    Installation pending
  Hope to move to new cable in March
    Coordinate downtime with Master SubStation outages
Damaged on 10/24/16
Protected from further damage
Provides timing/date to Neutrino Experiments
Experiments running fine

## Slide 10: MS1 Bus Failure
All power supplies cabled into breaker panel
Work completed

## Slide 11: PIP-II Injector Test & FAST Status
PIP-II Injector Test
  RFQ operation
    Emittance measurements with new scanner look good
    Shutdown to install 30 degree bend magnet in Low Energy Beam Transport (LEBT)
    Down for ~4-5 weeks
    Performed maintenance
  Plans for the week
    Shutdown for magnet installation
FAST
  No gun operation
    Drive laser aligned in laser lab
  Shutdown for 300 MeV upgrade
    Toroids arrived and being cleaned for leak check
  Magnet and stand installation
    Stands installed and aligned
    Magnet supports being added
    Magnets to follow

## Slide 12: CMTS1 Status
LCLSII Prototype Cryo Module
  Cryo
    Operation at 2K restored
  Accomplishments
    On Friday, January 13th all 8 cavities of pCM and magnet were powered to nominal gradient.
    Achieved voltage of 129 MV (128MV specification)
    Completed Q0 measurements
    Gathering lots of microphonics data
  Plan for the week
    Slow cooldown in progress
    Power all 8 cavities of pCM and magnet for endurance test (>10 hours)
    Microphonics as needed
    Turn off February 17th for ICW work

## Slide 13: ICW Reduction
Flow reduction began Thursday, December 29th (Complete)
  Flow rates reduced < 4300 GPM
  Contingency week was needed
    Weather added to the challenge
    Flow reduction ended Friday, January 20th
    Running on one 400 hp pump with
    addition pumps ready as needed
  Stakeholders impacted
    AD, TD, PPD, CD, FESS
Thank You!

## Slide 14: February 2017

## Slide 15: March 2017

## Slide 16: February 15th

## Slide 17: February 27th

## Slide 18: February 28th

## Slide 19: March 1st

## Slide 20: March 2nd

## Slide 21: Schedules and Links
Schedule can be accessed from the Operations Department Home Page
  Schedules -> Operations Schedule
Direct link to schedule
  http://www-ad.fnal.gov/ops/schedule.html

## Slide 22: Collaborations / Partnerships / Members [22pt Bold]