## Slide 1: Mechanical Design of SC Cavities
Ivan Gonin
PIP-II Machine Advisory Committee Meeting
10-12 April 2017

## Slide 2: PIP-II Layout
2
Section | Freq | Energy (MeV) | Cav/mag/CM | Type
RFQ | 162.5 | 0.03-2.1 |  | 
HWR (opt=0.11) | 162.5 | 2.1-10.3 | 8/8/1 | HWR, solenoid
SSR1 (opt=0.22) | 325 | 10.3-35 | 16/8/ 2 | SSR, solenoid
SSR2 (opt=0.47) | 325 | 35-185 | 35/21/7 | SSR, solenoid
LB 650 (g=0.61) | 650 | 185-500 | 33/22/11 | 5-cell elliptical, doublet
HB 650 (g=0.92) | 650 | 500-800 | 24/8/4 | 5-cell elliptical, doublet

## Slide 3: SC Cavities
HWR β=0.11 RF and Mechanical design are developed at ANL
SSR1 β=0.22 RF and Mechanical design developed at Fermilab
SSR2 β=0.47 RF Fermilab design, Mechanical design is under development at BARC, India
LB 650 MHz β=0.61 cavities VECC/Fermilab collaboration – RF bare and dressed cavity mechanical design and fabrication. April 21, Cavity Preliminary design review
HB 650 MHz β=0.9 cavities:
CW operation. Priority dF/dP minimization
Beam current 1 mA
HB 650 MHz β=0.92 cavities :
Pulsed operation. Priority LFD minimization
Beam current 2 mA

## Slide 4
The Scope of EM-Mechanical Design Issues
Minimize a sensitivity to microphonics due to He pressure fluctuations (df/dP) and mechanical vibrations
Minimize a Lorentz Force Detuning (LFD) coefficient
To keep the stiffness and tuning sensitivity at suitable level to allow for tuning.
Keep provision for slow and fast tuner integration.
Dressed cavity has to be qualified in 5 different load conditions by stress analysis
Warm Pressurization
Cold operation at maximum pressure
Cool down and tuner extension
Cold operation at maximum pressure and LHe weight
Upset condition – Insulating and beam vacuum failure

## Slide 5
Material Properties
The Dressed SRF Cavity is constructed of three materials:
Pure niobium (RRR 300),
Ti-45Nb alloy, and Grade 2 Titanium.
The material properties and allowable stresses are defined in Fermilab Technical Division Technical Note TD-09-005.
Stress analysis is intended to demonstrate that the PIP-II SRF cavities conform to the ASME Boiler and Pressure Vessel Code (the Code), Section VIII, Div. 1, to the greatest extent possible.

## Slide 6
Allowable Stresses (MPa)
 | Allowable Stress (S) for materials |  | Allowable Stress (0.6xS) for weld joints | 
Material | 2 K | 293 K | 2 K | 293 K
Nb | 171 | 25 | 102.6 | 15
Ti-45Nb | 156 | 156 | 93.6 | 93.6
Gr. 2Ti | 319 | 99 | 191.4 | 59.4
Material | Stress Category |  |  |  |  |  |  | 
 | Pm |  | PL |  | Pm ( or PL ) + Pb |  | Pm ( or PL ) + Pb + Q | 
 | 2 K | 293K | 2 K | 293K | 2 K | 293K | 2 K | 293K
Nb | 171 | 25 | 256.5 | 37.5 | 256.5 | 37.5 | 513 | 75
Ti-45Nb | 156 | 156 | 234 | 234 | 234 | 234 | 468 | 468
Gr. 2Ti | 319 | 99 | 478.5 | 148.5 | 478.5 | 148.5 | 957 | 297
Nb Welds | 102.6 | 15 | 154 | 22.5 | 154 | 22.5 | 308 | 45
Ti-45Nb Welds | 93.6 | 93.6 | 140.4 | 140.4 | 140.4 | 140.4 | 280.8 | 280.8
Gr. 2Ti Welds | 191.4 | 59.4 | 287 | 89 | 287 | 89 | 574 | 574
Pm = primary membrane stress; P L= primary local membrane stress Pb = primary bending stress Q = secondary stress |  |  |  |  |  |  |  | 
Technical Division Technical Note TD-09-005.

## Slide 7: HWR Cavities FRS

## Slide 8: HWR Cavities Stress analysis

## Slide 9: SSR1 Cavities FRS

## Slide 10: SSR1 Cavities: Pressure sensitivity

## Slide 11: SSR1 Cavities: LFD
The design of Helium Vessel was optimized to keep LFD within specifications.
A spring constant of ~ 30 kN/mm is expected at the interface

## Slide 12: SSR1 Cavities: Mechanical Resonances

## Slide 13: SSR1 Cavities: MAWP Requirements
Jacketed SSR1 cavities meet the requirements of maximum allowable working pressures according to Fermilab ES&H Manual chapter 5031.6. The assembly represents a sound mechanical structure that poses no hazard to personnel or equipment.
D. Passarelli

## Slide 14: HB 650 MHz Cavity Helium Vessel
components:
Long Cylinder
Transition ring MC end
Transition ring FP end
Bellow assembly
Support lugs
Lifting lugs
Helium inlet
2-phase pipe assembly
Tuner mounting lugs
Bellow restrains
Magnetic shielding (external)
Long Cylinder
Transition ring MC end
Transition ring FP end
Bellow assembly
Support lugs
Helium inlet
2-phase pipe assembly
Tuner Support
Lifting lugs

## Slide 15
Performance parameters for beta=0.9&0.92 cavity

## Slide 16: HB 650 MHz Cavity Helium Vessel
Similarities
Diameter is same
Same supporting lug gap
Same tuner lug location
Same Helium inlet stubs
Similar Magnetic shielding
Differences
Length for b = 0.92 is more
Cavity stiffness is different
Bellow position nominal dia is different
End groups are different
b = 0.9
b = 0.92

## Slide 17: FE mesh
Figures below shows the typical 3D and 2D FE meshes used in COMSOL analysis. 1.2 Million of 2-nd order 10-nodes tetrahedral elements was used in 3D analysis and ~70K 2-nd order 6-nodes triangular elements in 2D analysis. To increase the accuracy, mesh has been dense in critical areas like bellow, irises, axis line etc.

## Slide 18: Cavity stiffness, wall thickness 3.75 mm
F, N | 1000
x1, mm | 0.295
x2, mm | 0.016
VM σ bellow, MPa | 52
VM σ cavity, MPa | 10
F
x1
R2
x2

## Slide 19: LFD and dF/dP simulations algorithm
LFD ~ -1.33 Hz/(MV/m)^2
CAVITY SENSITIVITY ~ 160 Hz/μm
dL~2.01μm
dL~0.418μm

## Slide 20: LFD and dF/dP simulations algorithm
COMSOL Multiphysics algorithm to evaluate LFD, dF/dP consists from 5 following steps.
Running RF analysis of 2D CAD model in RF domain to calculate the initial fundamental frequency
Running Solid Model analysis with boundary conditions showing on Fig. 2, normalized Lorentz forces applied to cavity surface according to EM field from step 1 and applied tuner stiffness or apply He pressure.
Running Moving mesh COMSOL module to update initial mesh according to wall displacements from step 2
Running again RF analysis of 2D CAD model in updated RF domain to calculate a new fundamental frequency
Calculate LFD, dF/dP coefficient based on the difference of frequencies from steps 1 and 4

## Slide 21: LFD
Chart: LFD vs. Tuner Stiffness
| 0 | 5 | 10 | 20 | 40 | 60 | 80 | 100
0.9 Thickness 4 mm | -1.733 | -1.525 | -1.397 | -1.247 | -1.108 | -1.042 | -1.003 | -0.978
0.9 Thickness 3.75 mm | -1.896 | -1.655 | -1.511 | -1.347 | -1.197 | -1.127 | -1.087 | -1.06
0.92 Thickness 4 mm | -1.65 | -1.16 | -0.853 | -0.736 | -0.674 | -0.636
0.92 Thickness 3.75 mm | -1.95 | -1.37 | -1.008 | -0.869 | -0.796 | -0.752
FRS

## Slide 22: dF/dP
Chart: dF/dP vs. Tuner Stiffness
| 0 | 5 | 10 | 20 | 40 | 60 | 80 | 100 | 150 | 200 | 1000
0.9 Thickness 4 mm | 57 | 43.1 | 33.9 | 23.6 | 14 | 9.4 | 6.8 | 5
0.9 Thickness 3.75 mm | 60 | 43.7 | 34 | 22.9 | 12.8 | 8.1 | 5.4 | 3.6
0.92 Thickness 4 mm | 13.29 | 12.36 | 11.57 | 11.28 | 11.1 | 11 | 10.99 | 10.98
0.92 Thickness 3.75 mm | 14.75 | 14.05 | 12.76 | 12.35 | 12.11 | 12.05 | 12.03 | 12.015
FRS

## Slide 23: Modal analysis
Frequencies of 3 lowest Longitudinal Modes vs. Stiffness of the beta=0.92, tuner stiffness 0 kN/mm, thickness =3.75 mm
Chart: Frquency, Hz vs. Tuner Stiffness, kN/mm
| 0 | 1 | 5 | 10 | 20 | 40 | 70 | 100
R=100 mm | 48.1325 | 59.2184 | 81.3116 | 91.3918 | 98.0943 | 101.7291 | 103.3019 | 103.9292
 | 137.0576 | 140.5577 | 155.3054 | 170.4877 | 186.2046 | 195.2586 | 199.1821 | 200.478
 | 223.0813 | 224.2256 | 229.5741 | 237.1427 | 254.9303 | 269.8237 | 275.4119 | 277.2245

## Slide 24: Stress analysis. 5 Load cases

## Slide 25: Load cases and results
SCLs
Different loads applicable to cavity
Gravity
Liquid helium pressure head
P1 = 2 bar at room temp. p2=p3=0
Cool-down shrinkage to 2K
P1 = 4 bar at 2K, p2=p3=0
Tuner extension and
Cavity vacuum failure loads p3=1bar

## Slide 26: Load Case 1
Material | SCL | Pm | Sa | Ratio
NbTi-Ti | 6 | 4.32 | 93.6 | 0.05
NbTi-Ti | 15 | 1.11 | 93.6 | 0.01
Ti | 16 | 1.46 | 59.4 | 0.02
Ti | 17 | 31.6 | 99 | 0.32
Ti | 18 | 19.95 | 99 | 0.20
Ti | 19 | 51.98 | 59.4 | 0.88
Ti | 20 | 18.93 | 59.4 | 0.32
Ti | 21 | 5.41 | 59.4 | 0.09
Ti | 22 | 2.62 | 59.4 | 0.04
Material | SCL | Pm+Pb | Sa | Ratio
NbTi-Ti | 6 | 6.88 | 140.4 | 0.05
NbTi-Ti | 15 | 5.26 | 140.4 | 0.04
Ti | 16 | 17.05 | 89 | 0.19
Ti | 17 | 43.11 | 148.5 | 0.29
Ti | 18 | 141.1 | 148.5 | 0.95
Ti | 19 | 82.9 | 89 | 0.93
Ti | 20 | 37.30 | 89 | 0.42
Ti | 21 | 6.28 | 89 | 0.07
Ti | 22 | 5.13 | 89 | 0.06
5 load cases with different combination were qualified.
All applicable stress categories have been evaluated at the stress classification lines.
It was found that in all cases the stresses are below the allowable values.

## Slide 27: Summary
HWR cryomodule is under development in ANL. Completion ~ end of 2018
SSR1. The design status of the cryomodule completion ~ March 2019.
SSR2. RF design is done in FNAL. Mechanical design is under development in BARC, India
LB 650 MHz cavities
  RF and Mechanical design will provide by VECC, India
HB 650 MHz cavities RF and mechanical design has been done
  Stiffening ring, end group, HV are optimized to satisfy LFD FRS
  dF/dP, natural modes are satisfied to FRS
  All load cases are examined and found to be satisfactory