## Slide 1: RF Sources
David W. Peterson
PIP-II Machine Advisory Committee
10-12 April, 2017

## Slide 2: Outline
Scope of RF Sources
Amplifier Requirements
Installed Equipment
  Amplifiers
  Circulators
  Distribution
Equipment to arrive
India Collaboration Amplifiers
Lessons Learned
Summary

## Slide 3: Scope of RF Sources
“RF Power” includes
  Amplifiers
  Circulators
  RF Distribution
    Coax transmission lines and waveguide
    Connectors, elbows, adapters, etc.
    Directional Couplers
    Loads
  Controls & Interlocks (where not otherwise provided)
    Reflected power and RF leakage detection
    Interface to Accelerator Control Network

## Slide 4: Amplifier Requirements
Section | Qty | Freq (MHz) | Power (kW) | Duty | Source
RFQ | 2 | 162.5 | 75 | CW | FNAL
Buncher | 4 | 162.5 | 3 | CW | FNAL
First HWR | 1 | 162.5 | 3 | CW | FNAL
Other HWR | 7 | 162.5 | 7 | CW | FNAL
SSR1 | 16 | 325 | 7 | Pulse/CW | IIFC
SSR2 | 35 | 325 | 20 | Pulse/CW | IIFC
LB650 | 33 | 650 | 40 | Pulse/CW | IIFC
HB650 | 24 | 650 | 70 | Pulse/CW | IIFC
V. Lebedev, FNAL, The PIP-II Conceptual Design Report
= Room Temperature Cavities
= Superconducting Cavities

## Slide 5: Installed Equipment – RFQ Amplifiers
SigmaPhi 162.5 MHz, 75 kW amplifiers for RFQ are operational.
  First RF out of amplifier #1 Sept 2014 & #2 Nov 2014
  First power to RFQ February 15, 2016
SigmaPhi 162.5 MHz 75 kW Amplifiers
  Over 37.6 million pulses and 368 hours of CW operation
  Some failures
    RF “Slices” had some poor solder and water tubing joints
    480VAC input terminals insufficiently torqued
    Some intermittent CAN Bus and Ethernet communications
  Work continues on the module and slice test stand.

## Slide 6: Installed Equipment – MEBT Amplfiers
Front Panel Display
Rear View
Comark/Technalogix 162.5 MHz, 3 kW amplifiers
  RF performance meets specifications
    Gain, Gain and Phase vs Power, 1dB Compression, Spurious and Harmonics, Pulse performance
    >100 hour continuous duty burn-in at 2 kW
    Buncher 1 Cavity operational
    Buncher 2 amplifier ready
  Final revision accepted
    Two amplifiers at Fermilab
    Three more on the way
    Improved filtering
    Robust digital I/O
    Combines RF and Power Supply units
Spurious output: +/-3.9 kHz, -62.1 dBc.

## Slide 7: Installed Equipment - Circulators
UTE 3 kW Circulator
UTE Circulator and Buncher 1 Cavity
McManus 7 kW Circulator Test
Ferrite Co. Inc. 162.5 MHz, 75 kW circulators for the RFQ
  Require LCW to be 83F for proper operation at high power
  RF leakage corrected by application of copper tape at the water tubing entry
Comark provided UTE Circulator
  Sufficient for Buncher1 cavity
  Does not provide sufficient isolation for HWR operation: ~ 6 dB with short circuit
McManus 162.5 MHz, 7 KW Circulator
  Passed 3 kW and 7 kW tests
    7 kW Insertion loss <0.33 dB
    Isolation 23.1 dB @ 162.5 MHz, >20 dB across 6 MHz BW
    Short Circuit return loss 13.7 dB
  Will be used in the 3 kW and 7 kW systems

## Slide 8: Installed Equipment – RF Distribution
RF Distribution in place for RFQ and Buncher 1.

## Slide 9: Equipment to Arrive
Four McManus 162.5 MHz, 7 kW circulators are due at beginning of May.
RFQ for 162.5 MHz, 7 kW CW amplifiers is out to vendors
  Bids due April 10
  One unit to be procured in FY2017
  Up to 7 more units to be procured in FY2018

## Slide 10: India Collaboration Amplifiers - 325 MHz
A 3 kW Solid State RF Amplifier (SSRA) system was developed based on FRS of Dec. 2010 by DAE and was jointly tested successfully at Fermilab in late 2015.
BARC 325 MHz, 3 kW Amplifier at Fermilab
Plot of 9 days of continuous CW operation

## Slide 11: India Collaboration Amplifiers - 325 MHz
7kW prototype based on original specifications already tested at BARC.
New specifications based on experience with 3kW prototype complete.
7kW RF Power Amplifier TRS in Teamcenter ED0004290-Rev A.
Development and Testing in the scope of the R&D phase of PIP-II.
325 MHz, 7 kW Solid State Amplifier at BARC

## Slide 12: India Collaboration Amplifiers - 650 MHz
30 kW prototype based on early specifications constructed and tested.
Design modifications for 40 kW prototype underway; final specifications nearly complete.
40kW, 650 MHz Solid State RF Power Amplifier TRS in Teamcenter ED0005489-Rev (-).
Development and Testing in the scope of the R&D phase of PIP-II.
650 MHz, 30 kW Amplifier at RRCAT

## Slide 13: India Collaboration Amplifiers – Design Experience
REVIEW OF SCIENTIFIC INSTRUMENTS 85, 024707 (2014)
System efficiency analysis for high power solid state radio
frequency transmitter
Akhilesh Jain,1,a) D. K. Sharma,1 A. K. Gupta,1 M. R. Lad,1 P. R. Hannurkar,1
and S. K. Pathak2
1RF Systems Division, Raja Ramanna Centre for Advanced Technology, Indore 452013, India
2Electromagnetics and Microwave Engineering, Institute for Plasma Research, Gandhinagar 382 428, India
RRCAT Amplifier Design
75 kW 505.8 MHz
Solid State Amplifier
for Indus-2
India has settled on designing a solid state 70 kW amplifier for 650 MHz.

## Slide 14: Lessons Learned
Solid State Amplifier technology continues to rapidly improve
  Increasing efficiency thus reducing size and power needs.
  Increasing individual device output power.
  Improved power combining schemes.
  System costs are dropping.
Amplifier external control interface standards and protocols vary widely
  Remote control is essential.
  Some vendors understand the requirements and use industry standards, others use odd protocols or marginal circuitry. We provide guidance as needed.
RF Circulators require careful evaluation
  Manufacturers of quality high power units are rare. We must choose carefully.
  Many of them do not have the capability of testing their units at design power. We need to be prepared to test the units when they arrive.
  Some effects are only fully revealed at high power
    Detuning
    Poor reverse isolation
    Arcing
    Poor insertion loss
  Circulators are temperature sensitive and the thermal effects are difficult to compensate. We may want to consider bias coils and alternative temperature regulation.

## Slide 15: Summary
RF amplifiers along with circulators and RF distribution are installed and running for the PIP-II Injector Test RFQ and Buncher1 cavity.
The full compliment of 3 kW, 162.5 MHz amplifiers arrived last week.
7 kW, 162.5 MHz circulators are due in May.
Bids for 7 kW 162.5 MHz amplifiers will be coming in April.
India has working amplifiers at 7 kW 325 MHz and 30 kW 650 MHz. They have experience with a 75 kW 505.8 MHz amplifier and are designing a 70 kW, 650 MHz SSA.
The R&D phase is providing valuable experience with solid state amplifiers and related high power technology.