## Slide 1: The Axion Resonant InterAction Detection Experiment (ARIADNE)
A. Arvanitaki and AG., Phys. Rev. Lett. 113,161801 (2014).
Mark Cunningham (UNR)
Mindy Harkness (UNR)
Jordan Dargert (UNR)
Chloe Lohmeyer (UNR)
Asimina Arvanitaki (Perimeter)
Aharon Kapitulnik (Stanford)
Eli Levenson-Falk (Stanford)
Sam Mumford (Stanford)
Josh Long (IU)
Chen-Yu Liu (IU)
Mike Snow (IU)
Erick Smith (IU)
Justin Shortino (IU)
Mofan Zhang (IU)
Andrew Rusch (IU)
Yannis Semertzidis (CAPP)
Yun Shin (CAPP)
Yong-Ho Lee (KRISS)
DOE Cosmic Visions Workshop, Mar. 22, 2017
A. Geraci, University of Nevada Reno

## Slide 2: QCD Axion parameter space
ARIADNE
DM Radio
LC Circuit
ABRACADABRA
Adapted from http://pdg.lbl.gov/2015/reviews/rpp2015-rev-axions.pdf

## Slide 3: Axion Parameter space
ARIADNE
Orpheus
CASPEr
DM Radio
LC Circuit
ABRA-CADABRA
Adapted from Graham, arxiv: 1602.00039

## Slide 4: Axion and ALP searches
Dark Matter (Cosmic) axions | ADMX, ADMX-HF DM Radio, ABRA- CADABRA,LC Circuit Orpheus, CULTASK | CASPEr-Electric CASPEr-Wind
Solar axions | CAST IAXO | 
Lab-produced axions | Light-shining-thru-walls (ALPS, ALPS-II) | ARIADNE
Source
Photons
Nucleons
Coupling

## Slide 5: Axion-exchange between nucleons
Scalar coupling qQCD
Pseudoscalar coupling
Monopole-monopole
Monopole-dipole
dipole-dipole
Axion acts a force mediator between nucleons
N
N

## Slide 6: Spin-dependent forces
Monopole-Dipole axion exchange
mf
s
r
Different than ordinary B field
Does not couple to angular momentum
Unaffected by magnetic shielding
Fictitious magnetic field

## Slide 7: Using NMR for detection
mf
s
r
Spin ½ 3He Nucleus
Bloch Equations
Spin precesses at nuclear spin Larmor frequency
Axion Beff modifies measured Larmor frequency

## Slide 8: Constraints on spin dependent forces
Magnetometry experiments
G. Vasilakis, et. al, Phys. Rev. Lett. 103, 261801 (2009).
K. Tullney,et. al. Phys. Rev. Lett. 111, 100801 (2013)
P.-H. Chu,et. al., Phys. Rev. D 87, 011105(R) (2013).
M. Bulatowicz,et. al., Phys. Rev. Lett. 111, 102001 (2013).
G. Raffelt, Phys. Rev. D
86, 015001 (2012).
nEDM bound
Standard Model lower bound

## Slide 9: ARIADNE: uses resonant enhancement
Spin ½ 3He Nucleus
Bloch Equations
Time varying Axion Beff drives spin precession
 produces transverse magnetization
Oscillate the mass at
Larmor frequency
Amplitude is resonantly enhanced
by Q factor ~ wT2.
Can be detected with a SQUID
Beff

## Slide 10: Concept for ARIADNE
Unpolarized (tungsten) segmented cylinder sources Beff
Laser Polarized 3He gas senses Beff (Indiana U)
squid pickup
loop
Superconducting shielding (Stanford)
Applied Bias field Bext
A. Arvanitaki and A. Geraci, Phys. Rev. Lett. 113,
161801 (2014).
Limit: Transverse spin projection noise
Y.-H. Lee (KRISS)
Notes: Similar techniques used in short-range gravity experiments

## Slide 11: Hyperpolarized 3He
Ordinary magnetic fields cannot be used to reach near unity polarization
Metastability exchange optical pumping
Optical pumping techniques
M Batz, P-J Nacher and G Tastevin, Journal of Physics: Conference Series 294 (2011) 012002
Rev. Sci. Instrum. 76, 053503 (2005)
Indiana U. MEOP apparatus

## Slide 12: Experimental parameters
4 mm
11 segments
100 Hz nuclear spin precession frequency
2 x 1021 / cc 3He density
10 mm x 3 mm x 150 µm volume
Separation 200 µm
Tungsten source mass (high nucleon density)
Rotational stage
source mass
3 sample chambers

## Slide 13: Sensitivity
A. Arvanitaki and AG., Phys. Rev. Lett. 113,161801 (2014).

## Slide 14: Experimental challenges
Magnetic gradients
Nonlinearities
Barnett Effect
Trapped magnetic flux
Vibration isolation
Magnetic noise from thermal currents
Design/Simulation Work: Magnetic gradient reduction strategy
Experimental testing in progress: Vibration tests, Shielding factor f test thin-film SC

## Slide 15: Superconducting Magnetic Shielding
Meissner Effect
No magnetic flux across superconducting boundary
Method of Images
Make “image currents” mirrored across the superconducting boundary
Dipole with image
T > Tc
T < Tc
 Essential to avoid Johnson noise
Notes: Magnetic shielding operates on the Meissner effect
No flux across superconducting boundary
Think of it like a perfect conductor is a perfect diamagnet, so Faraday’s Law means no flux
Superconducting boundaries have surface currents that are hard to analyze
We use the method of images instead
Treat the boundary like a “mirror” that reflects magnetic sources
The reflections are called “images”

## Slide 16: The Problem of Unwanted Images
ARIADNE uses magnetized spheroid
  Constant interior field
Magnetic shielding introduces “image spheroid”
  Interior field varies
 variations in nuclear Larmor frequency!
3He
3He
3He
3He
3He
3He
But want to drive entire sample on resonance
Notes: ARIADNE detects + “transduces” axion forces w/ He-3 spheroid
  Spheroids are nice b/c of constant field parallel to individual moments
When superconducting shielding is introduced, “image” spheroid appears
  Field neither constant nor parallel to moments
We care about this b/c of…

## Slide 17: Flattening Solution
Spheroid
Symmetry
1 coil
(circular)
1 coil – simple configuration
Expected field from spheroid ~1 μT
  I on the 0.1 – 1 A range
Notes: Firstly, to flatten the field
Take advantage of the symmetry of the spheroid + block – any coil configuration must be symmetric
1 coil is easy to manufacture and means only 1 hole in the shield
Current constraints from expected field

## Slide 18
No cancellation
Gradient cancellation
Sample
area
98 times flatter
I = 1.6 A
sFrac = 0.17%
Gradient Cancellation
enabling T2 of ~100 s
Notes: Gradient cancellation 98x flatter!
Maybe recover T2 O(100 s)
  Compare to T2 O(1 s) w/o cancellation

## Slide 19: Tuning Solution – “D” Coils
Spheroid
Tune field with Helmholtz coils
  Helmholtz field only flat near the center
  Geometry restrictions prevent the spheroid from being centered in traditional Helmholtz coils
Inner straight-line currents cancel
Outer currents do not
One “D” coil and image (bird’s eye view)
“D” coils
    “D” coils look like Helmholtz coils when their images are included
I
Notes: Standard tuning solution is Helmholtz coils
  Helmholtz field only flat near center
Geometry (spheroid near wall) disallows “regular” Helmholtz field w/ spheroid @ center
  Images would cause problems anyway
“D” coils actually make use of images
  With the image included the coil looks like a Helmholtz coil
  Inner straight-line currents cancel, leaving a circle

## Slide 20: Rotary stage vibration and tilt
Build an interferometer to measure the change in distance (d).
We can find theta (Ө) from:
Ө= cos-1((L-d)/L)
We can solve for the wobble distance (X) by:
X= Lsin(Ө)
Interferometers
Rotary test chamber

## Slide 21: Fiber-coupled laser interferometers
Laser Source
Reference Photodiode
Signal Photodiode
90:10 fiber coupler
Reflector
Fiber Tip
PZT
Fringe visibility
~0.13
Sensitivity
~160 nm/V
Shot noise limit
~20 pm/Hz1/2

## Slide 22: Speed stability test - direct drive stage
Stage speed stability error – unloaded, in air
Rotation speed control
8.3 Hz ~ 1 part in 10000
RMS ~ 1 part in 3000
Allows utilization of T2 > 100s
Optical encoder
Current feedback control

## Slide 23
SQUID Magnetometers
Chart: 
Frequency (Hz)
Field noise (fTrms/√Hz)
4.5 fTrms/√Hz
Measured inside a magnetically shielded room (without Nb tube)
Y.H. Lee, KRISS
1 cm

## Slide 24
Applied field: 10-100 μTpp range (at 8 Hz)
Preliminary test of superconductive shielding
SQUID magnetometer: Near the center of Nb tube
Shielding factor: ≒(0.5-3) x109 for transverse field
Nb tube:
23 mm ID
1 mm thick
Length 200 mm
L-He dewar
Field coil
Goal: 108 with thin film Nb SC shield – tests planned Apr 2017
Y.H. Lee, KRISS,
Yun Shin (CAPP)
Eli Levenson-Falk (Stanford)

## Slide 25: R&D and Operating Costs/Timeline
Current funding for 1yr ($270k) for R&D, initial testing -- thank you!
Approx. 2-3 years to finish design/construction and bring to commissioning phase ($0.6 M/yr)
3 years data taking phase to reach QCD axion / R&D for upgrades ($0.6 M/yr)

## Slide 26: Summary
ARIADNE  New resonant NMR method
Gap in experimental QCD axion searches
0.1 meV < ma < 10 meV
Complementary to cavity-type (e.g. ADMX) experiments
No need to scan mass, indep. of local DM density
Next tests – shielding (Stanford/Korea), vibration (UNR), 3He system (Indiana)

## Slide 27
Thank you
Andrew Geraci (PI)
Jordan Dargert (G)
Gambhir Ranjit (PD)
Mark Cunningham(G)
Chloe Lohmeyer(UG)
Cris Montoya (G)
Acknowledgements
PHY-1205994
PHY-1506431
PHY-1509176
1510484, 1509176
Not pictured: Apryl Witherspoon (UG),
Ohidul Mojumder (UG), Hannah Mason (UG)
Kirsten Casey (UG)
Mindy Harkness (UG)
Jacob Fausett (UG)
Bella Rodriguez(UG)
Chethn Galla (G)
Jason Lim (UG)
Ryan Danenberg (UG)