## Slide 1: A 8Be IPC Decay Measurement at the Notre Dame-NSL
In design stage. Location: Nuclear Science Laboratory (NSL) at Notre Dame.
Initial goal: confirm/refute Atomki measurement using different technique.
Use 7Li(p,g) reaction to produce 18.15 MeV state in 8Be.
Proton provided by 5 MV, 200 mA 5U accelerator gives factor of 200 increase in beam intensity relative to previous measurement.
Experimental setup: solid 7Li target surround by 4p array of Si strip detectors
Increase production rates, better angular and E resolution vs. Atomki.
$750k to proceed with initial confirmation measurement, includes manpower.
Time scale: 1-2 years after receiving funds.
7Li target
p beam
Si strip detector
Thick Si wafer
e-
e+
Sketch of detector system
(Not shown: front and back annular Si detectors)
M. Brodeur (U. Notre Dame) and K.G. Leach (Colorado School of Mines)
Electroweak Interactions Group

## Slide 2: The Nuclear Science Laboratory of the University of Notre Dame
10 MV FN tandem accelerator
Max current ~ 10 mA
5 MV single-end 5U accelerator
Max current ~ 200 mA
Possible location for 8Be decay station
Proton beam
Electroweak Interactions Group