## Slide 1
WA105 TB
CERN – 01 February 2017
HV PS, HV feedthrough and SFTC
Franco Sergiampietri
1

## Slide 2
2
Tasks and progresses for the 6x6x6m3 and the 3x1x1m3
HV power supplies and FTs
1.1 300 kV HV PS for the 6x6x6-DP has been ordered (DAI 6649716).
1.2 Offer for 100kV PS arrived (12,019.0 €). Order to be done (ETHZ?)
1.3 Configuration: a) Present 300kV PS do be used for ProtoDUNE-SP: new cable male connector to the new HVFT or modified HVFT female connector.
b) New 300kV PS with larger diameter cable for ProtoDUNE-DP with HVFT adapted female connector.
c) 100kV PS for the 3x1x1: new cable male connector for smaller cable.
2. HV FTs
2.1 Drawings for 300kV HVFT for ProtoDUNE-DP:
a) 3D drawing: to be completed
b) quoted tables: to be done
c) offer: to be requested.

## Slide 3
3
3. HV transmission from HVFT to the cathode
Cu FLAT BRAID to the cathode
3.1 3D drawing: done.
3.2 Options to be decided: with or without rings connected to the field cage voltage degrader. Last ring always connected to the cathode.
Without the rings and the G10 spacers, with the inner SS pipe replaced by a SS rod, the weight is 36.3kg in air and 1.7 kg in LAr
Crossing pipe with inner diameter Din≥~150mm

## Slide 4
4
4. SFTC chimneys
3D drawing: done and passed to Adamo for their penetration in the cryostat. Internal details to be finalized.
Purge valve in the crossing pipe (to be remarked for cryostat design)
Crossing pipe with inner diameter Din≥~260mm
Outer pipe with diameter Dout=254mm