## Slide 1
1
HV power supplies, HV cables and HVFTs for the 666 SP and DP and the 311 DP
HV power supplies
1.1 300kV HV PS (300kV-1) at present connected to the 311-DP with cable Ø22mm (Cable 2) to be used for 666-SP.
1.2 300kV HV PS (300kV-2) for the 666-DP has been ordered (DAI 6649716) with cable Ø38.2mm (Cable 3).
1.3 100kV HV PS (100kV) for the 311-DP has been ordered (DAI 6673424) and will replace the 300kV-1with Cable Ø14mm (Cable 1).
1.4 200kV HV PS (200kV) as spare for the 666-SP: the cable (Cable 4) appears the same as Cable 3.
Cable 1
Cable 2
Cable 3 (X-Ray 2236)
Cable 4
Ø6.6
Ø32.5
Ø38.2

## Slide 2
2
HV power supplies, HV cables and HVFTs for the 666 SP and DP and the 311 DP
2. Male connectors to the HVFTs
2.1 Male connector Type1 (N.1): Øin=22mm for Cable 2 to the new HVFT for 666-SP connected to the 300kV-1 PS.
2.2 Male connectors Type2 (N.2): Øin=38mm for Cable 3 and Cable 4 to the new HVFT for 666-DP connected to the 300kV-2 PS and for 666-SP connected to the 200kV PS.
2.3 Male connector Type3 (N.1): Øin=14mm for Cable 3 to the present HVFT for 311-DP connected to the 100kV PS.

## Slide 3
3
HV power supplies, HV cables and HVFTs for the 666 SP and DP and the 311 DP
3. HV FTs
3.1 Drawings for 300kV HVFTs and cable male connectors for ProtoDUNE-DP and ProtoDUNE-SP:
a) 3D drawing: to be completed
b) quoted tables: to be done
c) offer: to be requested for the 4 male connectors and the 2 HVFTs (completely assembled) + details for a 3rd one as spare (after discussion with Marzio).