## Slide 1: Beam Studies
Yannis Karyotakis and Nikos Charitonidis
WA105 general meeting
March 22nd, 2017

## Slide 2: The beam for WA105
Requirements /
  Beam momentum ~1GeV to 12 GeV/c, p, K, p, e
  Trigger for WA105
  Particle Id
  Momentum measurement
  Beam profile for beam tuning
  Log and use off-line beam data
Use a set of dedicated (material and size) targets Cu, W
3 Scintillator plates & Cherenkov
2 Cherenkov counters and moderate TOF
Spectrometer with 3 position measurements
x,y position measurements at different z values
Use White Rabbit to synch Lar + Beam data
Implementation

## Slide 3
Courtesy: V. Clerc

## Slide 4
Position detectors based on scintillating fibres read out with silicon photomultipliers.
SiPM board
Scintillating
fibres
One layer of 1mm square fibres.
200 channels.
Individual MPPC for every fibre.
Courtesy: CERN BE/BI & EN/EA

## Slide 5: Target station
3 targets (2 hadron and one electron targets)
   Implementation under study
Horizontal remote configuration
Table / design/ integration by EN/EA, adjusted to the dimensions of the targets for H2/H4.
One of the two targets easily removable if needed (1/2h intervention)
Targets cut in order to easily change the length in order to enchance/suppress several particles if needed.
Courtesy: D. Brethoux

## Slide 7: H2 Final PID Schema
TOF with BPROF’s – distance ~32 m
1 “low pressure” XCET - < 3 bar pressure (“C1”)
1 “high pressure” XCET - ≥ 15 bar pressure (“C2”)
No K/p separation between 3 - 5 GeV No e- tagging in the ‘high energy’ regime 5-12 GeV

## Slide 8: H2 PID Schema – TOF
‘Moderate’ TOF needed
  If s = 2ns  p/π up to 2 GeV
  If s = 0.5 ns  p/π up to 4.5 GeV

## Slide 9: H2 PID Schema – XCET – Only CO2
1 high and 1 low pressure XCET
p/π from 2 GeV – C2 @ 6-7 bar
p/π from 3 GeV – C2 @ 3.5-5 bar
5 p.e

## Slide 10: H2 - If TOF fails – Backup solution with R134a
If TOF fails then we can ‘salvage’ with R134a :
p/π from 2 GeV – C2 @ 3.5 – 4 bar
T > 30 deg (cover of the gas system)
Maybe R134 (not “a”) could be tested in May @ T9 ?

## Slide 11: Estimating the R134a index
Dedicated experiment at PS, T9, November 2016
Both Cherenkovs filled with CO2 n-1=425×10-6
Ch-B filled with R134a
-3GeV/c e- enhanced target
7GeV/c
Scint 1,2
R134a n-1=700×10-6

## Slide 12: Hardware status
CERN BE-BI and EN-EA groups are responsible to produce the detectors, and provide the data
  Cherenkov needs all decided, green light to produce and install
  Position monitors : mechanics ok, electronics under development, 1st prototype Sept 2017, test on beam Oct 2017.
  TOF same mechanics as position monitors, dedicated electronics and DAQ
  Install electronics barrack
WA105 responsibility
  Build the trigger
  Install a dedicated TOF electronics
  Beam data handling
  Aim to install the system by fall 2017 for a fake beam test

## Slide 13: Improved G4BeamLine simulation
Exact beam layout implemented, tilted magnets, …..
Included all shielding in place
Background characterization and shielding

## Slide 14: Muons and other Background
High energy muons from primary/secondary target and other beams
Low energy muons, hadrons and electrons
Updated numbers for the LAr position, survey is coming soon
12 GeV beam

## Slide 16
Background for cryostat height = 100mm
~2.2KHz m,e p ~3 KHz, Total ~ 7.5KHz
Height=100mm
Height=800mm
More detailed simulations to follow soon (+ electron beams)

## Slide 17: Conclusion
Beam instrumentation well defined
Next priorities
  Follow up construction
  Integrate beam signals to WA105 control room
  Integrate Beam Data to LAr data
  Continue background studies