## Slide 1: H2 Beam status
Yannis Karyotakis
10 May 2017

## Slide 2: Main activities
Understudying and shielding background.
  Long simulation process, identifying the origin, shield, start over
  Version -1 numbers in KHz
  The detector vertical position is critical for the muon halo
Implementation of the H4 Beam line in the same geometry as H2. Estimate the H4 induced background to H2 when running simultaneously
Latest simulation version available this week. New ‘final’ simulation data for all energies next week

## Slide 4: Hardware status
Beam profile fiber detectors
  First 2-3 prototypes available in October for beam profile monitors and trigger counters. Same fibers but different read-out scheme (SiPMs and PMs)
Two high pressure Cherenkovs will be available by April 2018. Two possible gases, CO2 or R134a
Beam Data : Profile monitors and Cherenkovs will be handled by CERN and tagged with WR. We must extract them from CERN DB
TOF, 2 options
  SiPM read-out, expect <1ns resolution. Probably DAQ problems and compatibility with WR
  Use the trigger counters and electronics + WR TDC. Expect 1.5-2 ns resolution
    Data handling is OUR responsibility

## Slide 5
Tests foreseen
  TOF(b) with LEDs ASAP. All material in hands, measure resolution
  TOF(b) + profile monitors + WR + DAQ at T9 PS, October – November
Manpower issues
  DAQ person to handle beam data.
    Retrieve CERN beam data and store them on our side
    Read WR TOF board and store data
Installation issues
  Signals from CERN BI to our counting room
    NIM crate to handle ‘raw’ signals (S1, S2, S3, Ch1, Ch2) and form the trigger
    Dedicated PC for TOF + Beam Data retrieval