## Slide 1: Cosmic Frontier DAQ needs
Paul O’Connor
BNL Instrumentation Division
DAQ R&D workshop
Albequerque NM 20171011

## Slide 2: Disclaimer and prejudices
My background is not in DAQ…
  1990 – 2000
    RHIC and ATLAS ASIC-based FEE
  1995 – 2005
    ASIC FEE for medical, photon science, DHS WFO
  2003 – present
    LSST CCDs & readout
  2016 – present
    LDRD on 21cm

## Slide 3: CF Landscape
OHEP experimental programs
Cosmic Frontier
Intensity Frontier
Energy Frontier
Cosmic Acceleration
Dark Matter
Cosmic- and Gamma-ray
Massive galaxy spectroscopic survey
Stage IV CMB
21cm intensity mapping
Color-sensitive sensors
Fiber-fed spectrographs
Low-resolution spectroscopy

## Slide 4: CF Landscape
OHEP experimental programs
Cosmic Frontier
Intensity Frontier
Energy Frontier
Cosmic Acceleration
Dark Matter
Cosmic- and Gamma-ray
Massive galaxy spectroscopic survey
Stage IV CMB
21cm intensity mapping
Color-sensitive sensors
Fiber-fed spectrographs
Low-resolution spectroscopy

## Slide 5: CF Landscape
OHEP experimental programs
Cosmic Frontier
Intensity Frontier
Energy Frontier
Cosmic Acceleration
Dark Matter
Cosmic- and Gamma-ray
Massive galaxy spectroscopic survey
Stage IV CMB
21cm intensity mapping
Color-sensitive sensors
Fiber-fed spectrographs
Low-resolution spectroscopy

## Slide 6: CF Landscape
OHEP experimental programs
Cosmic Frontier
Intensity Frontier
Energy Frontier
Cosmic Acceleration
Dark Matter
Cosmic- and Gamma-ray
Massive galaxy spectroscopic survey
Stage IV CMB
21cm intensity mapping
Color-sensitive sensors
Fiber-fed spectrographs
Low-resolution spectroscopy

## Slide 7
OHEP experimental programs
Cosmic Frontier
Intensity Frontier
Energy Frontier
Cosmic Acceleration
Dark Matter
Cosmic- and Gamma-ray
Massive galaxy spectroscopic survey
Stage IV CMB
21cm intensity mapping
Color-sensitive sensors
Fiber-fed spectrographs
Low-resolution spectroscopy

## Slide 8: Next-generation galaxy spectroscopic surveys
Extend to higher redshift
Extend to higher sky coverage
To achieve survey speed, require collecting spectra of 104 – 105 targets simultaneously
Can trade off resolution, field of view, limiting magnitude
2 basic strategies:
  Low-resolution spectra with color-sensitive detectors or low-dispersion prism
  Massively parallel fiber-fed spectrographs

## Slide 9: Color-sensitive detectors for low-resolution redshift survey
Improve photo-z over broadband filters while preserving throughput
Filterless, dispersionless spectroscopic imaging
Semiconductor and superconductor options
  Multicolor CCDs
  MKIDs: single-photon sensitive with R~30
  Photon absorption breaks Cooper pairs, changes inductance, measure phase and amplitude change
  Each resonator (pixel) has a unique resonant frequency in the GHz range
  A comb of sine waves is generated and sent through the device
  Thousands of resonators can be read out on a single microwave transmission line (FDM)
Microwave Kinetic Inductance Detector (MKID)
Muti-color CCD (simulation)
B. Mazin

## Slide 10: Example: 100,000-element MKIDs array
DAQ challenges:
Scale-up:
  2K camera demonstrated (ARCONS, arXiv:1306.4674)
  30K camera in development (KRAKENS, arXiv:1506.03458)
Multi-GHz RF data transport in/out of sub-1K cryostat
Warm electronics: “software-defined radio” technique, massive GSa/s rate, need for real-time pipeline
Calibration (laser scan?)
Giga-z concept (Marsden 2013)
Possible readout/DAQ architecture (FNAL)
Multiplexed MKID string

## Slide 11: Data rates and volumes for 100,000 element MKIDs low-resolution spectroscopic survey
Input to DAQ:
  GHz-rate FDM on 50 feedlines (2000 MKIDS each) digitized at ~4GSa/a, 12b  300GB/s
Intermediate output:
  Each photon arrival tagged with position (17 bits), energy (7 bits), time (5ms/15s = 22bits) = 46 bits  6 Bytes
  Broadband sky signal ~ 300photons/macropixel/s; 80% of pixels have galaxy sources ~ 10X sky rate
  2700ph/pix/s × 105 pix × 6Bytes/pix = 1.6GB/s (200X reduction from raw rate)
Data volume if intermediate output is stored:
  Assume 1000 hours/yr on-sky time for 5 years  29PB

## Slide 12
OHEP experimental programs
Cosmic Frontier
Intensity Frontier
Energy Frontier
Cosmic Acceleration
Dark Matter
Cosmic- and Gamma-ray
Massive galaxy spectroscopic survey
Stage IV CMB
21cm intensity mapping
Color-sensitive sensors
Fiber-fed spectrographs
Low-resolution spectroscopy

## Slide 13: Fiber-fed spectrographs beyond DESI
Existing surveys (DESI) still not statistics limited
Extend to 100M galaxies, z > 1.5
4-arm spectrographs including l > 1000nm channel
Leverage LSST imaging
Existing or new large S. hemisphere telescope
DAQ/control issues:
Leverages DESI experience
Control/alignment of dense (30X DESI) fiber positioner array
Dawson
Future Cosmic Surveys 2016

## Slide 14: Fiber-fed spectrographs
Assumptions:
  100k fibers
  1 hour/exposure, 1 min./readout
  10000 hours open-shutter time over 10 years
  200 4-arm spectrographs, 500 fibers/spectrograph, 4K2 pixels/detector, 16bit resolution
 26GB raw data per exposure
 430MB/s rate
 260TB total
Incremental advance over present CCD readout
Schlegel
Future Cosmic Surveys 2016

## Slide 15
OHEP experimental programs
Cosmic Frontier
Intensity Frontier
Energy Frontier
Cosmic Acceleration
Dark Matter
Cosmic- and Gamma-ray
Massive galaxy spectroscopic survey
Stage IV CMB
21cm intensity mapping
Color-sensitive sensors
Fiber-fed spectrographs
Low-resolution spectroscopy

## Slide 16: Stage IV CMB
A Conceptual Design Team with representatives fro 4 labs has been working to define the science case and technology implementation for a ground-based CMB survey:
  Array of mm-wave telescopes, 4 bands, measure r, Neff
  Cryogenic focal plane, <<1K
  2 sites: S. Pole, Chile
  500K detector elements (10X Stg.3, higher sensitivity), up to 50K/telescope
  In-cryostat frequency-domain multiplexing with MHz or GHz carrier (time- and code-division mux also considered, or hybrid approach)
  Backend electronics similar to MKID and a universal platform is considered.

## Slide 17: CMB-S4 readout architecture (GHz FDM)
Frequency comb in
Encodes element position along string
Flux-coupled TES resonators
Incident radiation shifts phase of resonance
Backend digital: probe comb generation, transmitted wave sampling and demux

## Slide 18: DAQ R&D issues for CMB-S4
Investigate alternative ways to reach higher multiplexing ratios:
  High-bandwidth FDM
  MKIDs vs TES
  Higher sampling rates in warm backend
Packaging approaches to reduce wire count between thermal stages in cryo
Clock distribution stability
Algorithms to go from sampled FDM domain  Time-Ordered-Data domain  cleaned TOD  Map domain: what should be part of DAQ? Couple with simulation effort
Final data volumes: increased over S3 but not challenging
CMB S4 data pipeline
Growth of data volume (and computing)

## Slide 19
OHEP experimental programs
Cosmic Frontier
Intensity Frontier
Energy Frontier
Cosmic Acceleration
Dark Matter
Cosmic- and Gamma-ray
Massive galaxy spectroscopic survey
Stage IV CMB
21cm intensity mapping
Color-sensitive sensors
Fiber-fed spectrographs
Low-resolution spectroscopy

## Slide 20: 21cm intensity mapping
Detect redshifted 21cm emission from neutral hydrogen (or CO)
Design telescope with beams to make maps (like CMB) with just enough angular resolution to detect Large Scale Structure – no need to resolve individual galaxies
Narrow 1.420GHz emission line gives precise redshift automatically

## Slide 21: 21cm readout
At frequencies < 1GHz, one can just directly sample the electric field (after amplification and bandpass filtering), Fourier transform and square to get intensity as a function of frequency.
Multiple antennas can be operated as an interferometer, increasing collecting area and allowing higher angular resolution
Interferometer of N antennas requires N2/2 cross-correlators at RF
LNA
Browne 2012
Consider digitizing from here and performing subsequent processing in FPGA or GPU
Single-dish (imager) configuration
Single-dish correlation receiver

## Slide 22: Example 21cm signal chain (single dish)
Antenna
Pulsed calibration injection
[cooled] amplifiers + filters
Digitizer
RFI identification and excision
|Fourier transform|2
Accumulate
Calibration signal processing
Waterfall chart
Offline processing: calibration, foreground removal, map-making
For interferometer of N antennas, a set of N2/2 correlators is required.

## Slide 23: DAQ R&D issues for 21cm IM
Take maximum advantage of high speed digital sampling and processing hardware (ADCs, FPGAs, GPUs) as they will exist in 2025
Leverage digital RF and high-speed DAQ expertise within Labs
RFI mitigation (neural networks?)
Ensuring receiver gain and phase stability
Waterfall chart (BNL)
For interferometers:
  Correlator architecture study using proper FoM to optimize system-level cost and power consumption
  Stable distribution of signals (RF over fiber?)

## Slide 24: Lessons learned from LSST
Importance of early integration (vertical slice tests)
  Expose system-level problems not seen in component-level tests
Ensure test stand DAQ is ready for production tests
  Decide if science DAQ will be used for test stands
  Test stand DAQ needs to be ready earlier, and with possibly more features/functionality than science DAQ
Importance of a good detector emulator
Importance of DAQ for diagnostics and hazard mitigation
  Especially important for detectors in cryo

## Slide 25: LSST DAQ lessons learned
Vertical Slice Test
Scan mode diagnostics
Triple CCD emulator

## Slide 26: Summary
Next-generation large-scale cosmic acceleration experiments in planning stages
Several areas of common R&D interest:
  Digital RF signal generation and processing
  Algorithms for on-the-fly calibration and data cleaning
  Analog data transport into/out of cryostats
  Test stands and calibration
For galaxy spectroscopic survey:
  Viability of MKIDs at 105-pixel scale
  Control and alignment of 105 fiber positioners
For CMB:
  Choice of detector and multiplexing method
For 21cm:
  Leveraging high-speed digital sampling and processing to minimize cost and power