## Slide 1
Doneisha Steele
SIST/GEM Final Talks
15 August 2017
Analyzing Lock-In Amplifier Techniques Using Python

## Slide 2: Objectives
Statistical analysis of two mathematical approaches for the implementation of a lock-in amplifier to aid in noise reduction
Develop lock-in amplifier simulation in Python

## Slide 3: Background – Particle Detectors
Icarus
Detect, track and identify ionizing particle
Major challenges include background noise, high detection rates , neutron neutrality, and low neutron energies.

## Slide 4: Ground Impedance Monitor
Measures the impedance between the “isolated” detector ground and building ground
Built for the ProtoDUNE, Icarus, SBND and DUNE

## Slide 5: Ground Impedance Monitor
Detector
Current Transformer
Audible Alarm
Impedance Display/Monitor

## Slide 6: Lock – In Amplifier
The output of the PSD is simply the product of two sine waves. Vpsd = VsigVLsin(wrt + θsig)sin(ωLt + θref) = 1/2 VsigVLcos([ωr - ωL]t + θsig - θref) - 1/2 VsigVLcos([ωr + ωL]t + θsig + θref)

## Slide 7: Python

## Slide 8: Simulation

## Slide 9: Results
Square Wave
Sine Wave

## Slide 10: Results
Average : 9.99394
Error: -0.06053 %
Standard Deviation: 0.01531
Run Time: 1.37s
Average : 9.97856
Error: -0.21434 %
Standard Deviation: 0.01123
Run Time: 1.67s

## Slide 11: Results
Average : 9.99501
Error: -0.04984 %
Standard Deviation: 0.01587
Run Time: 9.26s
Average : 9.98916
Error: -0.10831 %
Standard Deviation: 0.01744
Run Time: 15.68s

## Slide 12: Conclusion/Future Work
Sine wave provides better return on accuracy and run time
Increasing the number of runs increases the accuracy
In the future, remove all the noise, eliminate bias
# of Runs | Time | Average | Error | Std. Dev.
10 | 1.37s | 9.99394 | -0.06053% | 0.01531
 | 1.67s | 9.97856 | -0.21434% | 0.01123
100 | 1.52 | 9.99585 | -0.41450% | 0.01778
 | 1.99s | 9.9927 | -0.07227% | 0.01573
1000 | 2.08s | 9.99417 | -0.58290% | 0.01588
 | 2.14s | 9.98967 | -0.10326% | 0.01778
10000 | 9.08s | 9.99501 | -0.04984% | 0.01587
 | 15.68s | 9.98916 | -0.10831% | 0.01744

## Slide 13: References
Armen , Dr. G. Bradley. “Phase Sensitive Detection: the Lock-in Amplifier .” The University of Tennessee , 2008.
Rubinov, Paul, and Michael Utes. Ground Impedance Monitor. 4 June 2017.
“An International Mega-Science Project.” Deep Underground Neutrino Experiment, www.dunescience.org/
Doneisha Steele | Analyzing Lock-In Amplifier Techniques Using Python

## Slide 14
FIN