## Slide 1: The LIEBE high-power target: Offline commissioning results
Ferran Boix Pàmies

## Slide 2: Outline
Introduction/Context
LIEBE prototype design & completed assembly
Offline commissioning
Conclusions

## Slide 3: Introduction/Context
High power target for exotic species
Enhance the release of short-lived isotopes through:
  Droplet formation
  Lower density of the liquid
Primary beam heat deposition dissipation:
  Custom-made heat exchanger
Concept scheme, E. Noah et all, EURISOL-DS
Concept
Prototype
Offline commissioning
Online tests

## Slide 4: LIEBE: LIquid Eutectic lead Bismuth for Eurisol
LBE Velocity preferred: 2 m/s Q=0.13 l/s
Ø0.4 mm droplets factor 5 increase in release efficiency
Target material: LBE
Operational temperature [200-600]°C
Targeted isotope: 177Hg (130ms half-life)
Introduction/Context
Images from Melanie Delonca CERN Ph.D thesis
0,4mm
Prospects for the production of 100Sn ISOL beams at HIE-ISOLDE, EMIS 2018

## Slide 5: LIEBE prototype design & completed assembly
The target:
  Compatible with existing target handling at ISOLDE
Chimney

## Slide 6: LIEBE prototype design & finished assembly
The EM pump:
Dedicated trolley
Magnetic wheel
Alignment table
Coupling rails
Double Hallbach array axisymmetric
P=2,2kW , B=1,1T

## Slide 7: Offline commissioning: Flow assessment
Test objectives:
  Operate in the absence of cavitation
  Reach the desired flow for release optimization (0,13L/s)
Increased diameter: Ø10mm Ø16mm
Flow assessment in previous tests at IPUL

## Slide 8: Offline commissioning: Flow assessment
Tests done with a LIEBE loop replica at IPUL
Screenshot of the tests setup

## Slide 9: Offline commissioning: Flow assessment
Results:
  Drift observed between measurements due to clogging of the sensors
  LBE oxide formation in contact with air
Chart: Q[L/s]
| 0.16397026130653261 | 0.14077780952380953 | 7.4813848837209346E-2 | 9.5961096999999995E-2 | 0.14644663699999999 | 0.176223504 | 0.18054993388429749 | 0.17549747692307691 | 0.1199654117647059 | 8.938005468750003E-2
Fr=35Hz | 1.4918 | 1.8272 | 2.3767 | 2.3387 | 1.898 | 1.5695 | 1.8346 | 1.8716 | 2.2642 | 2.428
Fr=37.5Hz | 1.9338 | 2.0525 | 2.413 | 2.0881 | 2.6056 | 1.6028 | 1.9006 | 2.4676 | 1.6889 | 2.5358 | 1.853
Fr=40Hz | 1.8233 | 2.3374 | 2.6554 | 1.8833 | 2.2684 | 2.7341 | 2.1984 | 2.1977 | 2.6887
 | -0.5 | 100
Fr=42.5Hz | 2.8926 | 2.4325 | 2.2506 | 1.9193 | 1.7434
0,13

## Slide 10: Offline commissioning: Alignment/vibration tests
Vibration tests:
  Check vibration transmission
  Evaluate the level of vibration for each rotational frequency
Empirically measured maximum distance in case of perfect alignment
Test setup after alignment

## Slide 11: Offline commissioning: Alignment/vibration tests
Rotor Fr= 20Hz
Rotor Fr= 40Hz
  Good/satisfactory vibration levels for operational frequencies of LIEBE
  No misalignment of the setup during the test
  Addition of an accelerometer to monitor the vibration throughout operation with LBE
Results:
  Vibration increase due to excitation of target natural resonant frequencies

## Slide 12: Offline commissioning: Leak issue
Leak emergence:
  Appropriate vacuum level with cold target
  Leak appearing when heating up the ion source to 1700 ºC
Ansys mechanical static structural simulation

## Slide 13: Offline commissioning: Remaining tests
Full operation of the loop with molten LBE in an offline mass separator:
  Thermal control (Heat exchanger)
  Safety measures:
    Pressure sensor
    Accelerometer
  Mass scans
LIEBE target coupled to offline separator

## Slide 14: Conclusions
Flow developed by the EM pump within the calculated values for isotope release
Satisfactory vibration levels
New base design coping with the leak issue at high temperature
Remaining full operational tests in an offline separator before final online test with proton beam

## Slide 15: Acknowledgements
Contribution of many people from different disciplines:
Melanie Delonca, Thierry Stora, TISD team, Laurent Prever-Loiri, Thierry Feniet, Kalvis Kravalis, Donald Houngbo, Vincent Barozier, Edouard Grenier Boley, Ana–Paula Bernardes, Antje Behrens, Alexandre Beynel, Lukasz Jerzy, Giordano Lili, Jean-Louis Grenard, Carlos Veiga Almagro, Pascal Fernier, EN-STI, EN-HE, HSE-RP, EN-SMM
7th High Power Targetry Workshop

## Slide 16
Thank you for your attention

## Slide 17
Backup slides

## Slide 18: The main loop part
  Filling tank
  Heat Exchanger (HEX)
  Irradiation & diffusion chamber
  Hypertaks/feedthroughs
  Water connectors
  Electrovalves
  Bellows
  Extraction line and ion source -> standard VADIS ion source

## Slide 19: LIEBE: Heat Exchanger
1
2
3
5
4
5 LBE temperatures (200-600degC)
CFX Calculations of the heat exchanged for every channel
3D printed steel Heat Exchanger
Chart: Temperature of LBE [°C]
| 200 | 300 | 400 | 500 | 600
1 | 467.959 | 760.4548 | 1082.764 | 1419.076 | 1773.911
2 | 576.407 | 926.507 | 1288.058 | 1661.427 | 2042.951
3 | 633.8471 | 1040.662 | 1467.323 | 1921.356 | 2399.828
4 | 1183.309 | 1971.556 | 2778.174 | 3559.626
5 | 2409.721 | 3955.254

## Slide 20: Offline commissioning: Alignment/vibration tests
Displacement Power Spectral Density comparison, Rotor Fr=30Hz, EM Wheel Fr= 4,11Hz direction +Y
Results:

## Slide 21: Offline commissioning: Alignment/vibration tests
Displacement Power Spectral Density comparison, Rotor Fr=20Hz, EM Wheel Fr= 2,75Hz direction +Z

## Slide 22: Offline commissioning: Alignment/vibration tests
Displacement Power Spectral Density comparison, Rotor Fr=30Hz, EM Wheel Fr= 4,11Hz direction +Z

## Slide 23: Offline commissioning: Alignment/vibration tests
Displacement Power Spectral Density comparison, Rotor Fr=40Hz, EM Wheel Fr= 5,48Hz direction +Z

## Slide 24: Offline commissioning: Leak issue
Attempts to solve it:
  Increasing sealing pressure
  Shielding the ion source
  Only able to operate the source up to 1900 ºC

## Slide 25: Offline commissioning: Alignment/vibration tests
Alignment tests:
  Cylinder axis and pump axis are on the same line within 0.1mm
Best fit distances between EM pump and target
Measurement of the EM pump axis

## Slide 26: Offline commissioning: Flow assessment
Chart: ΔP[bar]
| 1.4917776381909542 | 1.8272238571428572 | 2.3767288953488377
Fr=35Hz | 0.16397 | 0.14078 | 0.074814
Fr=37.5Hz | 0.16913 | 0.15047 | 0.087561
Fr=40Hz | 0.1692 | 0.1319 | 0.094706
Fr=42.5Hz | 0.084073 | 0.16726 | 0.1731 | 0.1736
 | 0.13 | 0.13
Chart: ΔP[bar]
| 1.5478623770491802 | 1.6999733333333331 | 1.8441103333333337 | 2.0844937671232873
Fr=30Hz | 0.16781 | 0.14622 | 0.12313 | 0.082231
Fr=32.5Hz | 0.17434 | 0.16646 | 0.14668 | 0.084435
Fr=35Hz | 0.18055 | 0.1755 | 0.11997 | 0.08938
Fr=37.5Hz | 0.18495 | 0.17312 | 0.1227 | 0.17037 | 0.090552
Fr=40Hz | 0.1801 | 0.17906 | 0.10896

## Slide 27: Offline commissioning: Alignment/vibration tests