## Slide 1: Safety Briefing

## Slide 2: Introduction: 400 MeV/u upgrade for FRIB
Brad Sherrill

## Slide 3: Outline
Welcome
Upgrade of FRIB to > 400 MeV/u
Advantages
Next steps

## Slide 4: FRIB Project is 85% Complete
Civil construction done in 2017
October 2017: First ion beams accelerated by RFQ, argon 40Ar9+ and krypton 86Kr17+
December 2017: Cryoplant operational
July 2018: Beam accelerated to 2 MeV/u in first three cryomodules

## Slide 5: FRIB Opportunity for Upgrade to 400 MeV/u
Space available for upgrade
P. Ostroumov et al.
FRIB design allows the opportunity to operate at higher energy
11 cryomodules with total 55 superconducting elliptical cavities operating at 644 MHz will provide 400 MeV/u uranium
Team exists to deliver the needed cryomodules

## Slide 6: Prototype Cryomodule Under Design (~60%)
The cryomodule is modified from HWR matching cryomodule
2 elliptical cavities instead of 4 HWRs
Design and fabrication of components is proceeding
Testing of the first cavity is planned this year
Clean room assembly
P. Ostroumov et al.

## Slide 7: FRIB-Upgrade Beam Energy
Ion species | Charge state | Energy (MeV/u), FRIB | Energy (MeV/u), FRIB-U
40Ar | 18 | 320 | 540
48Ca | 20 | 264 | 508
86Kr | 35 | 257 | 497
124Sn | 47 | 235 | 464
198Au | 68 | 210 | 421
238U | 78 | 200 | 403
Higher primary beam energy means fragment energy of typically 350-400 MeV/u.

## Slide 8: More than 2x Increase in Rare Isotope Beam Rates from the Upgrade for Most Isotopes
Does not include limitations of the production target
Ratios are estimates
2x additional luminosity from thicker secondary targets
Beam dump is easier
One atom/week limit
O. Tarasov

## Slide 9: Example: Production of 68Ca from 82Se Primary Beam
Case | Target Thickness g/cm2 | 68Ca Rate /s | Gain | Brho Tm
Baseline 200 MeV/u | 1110. | 9.39E-8 | 1.0 | 6.716
120 kW C 400 MeV/u | 4190. | 7.10E-7 | 7.6 | 10.94
200 kW C 400 MeV/u | 6510. | 1.13E-6 | 13. | 9.86
Optimum C 400 MeV/u | 8900. | 1.16E-6 | 13. | 7.73
Optimum Li 400 MeV/u | 10900. | 5.43E-6 | 58. | 7.69

## Slide 10: 400 MeV/u at FRIB Science Themes
Scientific rationale for an upgrade of the FRIB energy:
  Extends the reach of FRIB along the drip lines. Extremely neutron- or proton-rich nuclei provide sensitive tests of nuclear models. Nuclei with skins of 0.7 fm can be produced
  Will improve the constraints on r-process models given by elemental abundance data from stellar observations; access to more neutron rich nuclei important given NS merger results
  Laboratory study of the neutron-matter equation of state at near 2ρ0 and 10x higher pion cross sections; made timely due to observation of gravitational waves from NS mergers
  Significant advantages for nuclear reactions; mapping of nucleon wave functions, excitation of particular channels, …
Experiments along the drip line can be completed in one day instead of 7 days
Following talks will discuss these points in detail

## Slide 11: Status and Next Steps
400 MeV/u cryomodule is under development and proceeding well (Ostroumov); the team is in place to deliver the upgrade in a cost-effective manner. Timely to consider the upgrade.
The 400 MeV/u upgrade was presented to FRIB SAC; closeout comments were positive
This dedicated workshop on August 9th at the Low Energy Community Meeting
  Discussion at the close of the workshop
  Thoughts and consensus to move forward
  Recommendation from the full LECM to explore the opportunity
Community white paper on the science opportunities by end of the year
Please send your input to Alexandra Gade or Brad Sherrill

## Slide 12: Summary
Upgrade of FRIB to > 400 MeV/u
Advantages – higher energy, higher yields for most isotopes
Next steps – Community white paper on the opportunity

## Slide 13: Backup

## Slide 14: Main Cavity/Cryomodule Parameters
Frequency (MHz) | 644
 | 0.65
Number of cells | 5
, (cm) | 71
V0 (MV) | 12.4
Expected residual resistance (nΩ) | 5
Dynamic heat load per cavity at 2K (W) | 17.1
Number of cryomodules | 11
Number of cavities per cryomodule | 5
Number of cavities required for FRIB upgrade | 55
Length of the focusing period (cryomodule plus warm section) (m) | 7.25
Total dynamic heat load at 2K in upgraded segment of FRIB linac (W) | 938
Frequency (MHz) | 644
 | 0.65
Number of cells | 5
 | 71
V0 (MV) | 12.4
Expected residual resistance (nΩ) | 5
Dynamic heat load per cavity at 2K (W) | 17.1
Number of cryomodules | 11
Number of cavities per cryomodule | 5
Number of cavities required for FRIB upgrade | 55
Length of the focusing period (cryomodule plus warm section) (m) | 7.25
Total dynamic heat load at 2K in upgraded segment of FRIB linac (W) | 938

## Slide 15: Beam Energies and Cryogenics Heat Load Estimate
 | Parameter | Value
1 | Number of cryomodules | 11
2 | Number of SC elliptical cavities | 55
3 | Focusing | RT doublets
4 | Uranium beam energy | 403 MeV/u
5 | Proton | 910 MeV
6 | Argon | 530 MeV/u
7 | Krypton | 490 MeV/u
Temperature | FRIB | Upgrade
2K | 2349 | 1048
4.5K | 1195 | 104
38/55K | 7331 | 3803*
*Distribution losses are not included