## Slide 1: Integration Test Status with 40% APA and ProtoDUNE-SP APA
Shanshan Gao on behalf of the LArTPC CE Group

## Slide 2: ProtoDUNE-SP TPC Front End Electronics
Cold Electronics
  120 Front End Mother Board (FEMB) assemblies
  6 sets of cold cable bundles
  6 sets of signal feed-throughs
Warm Interface Electronics
  6 warm interface electronics crates

## Slide 3: Integral APA + CE + WIEC Concept
Cold electronics module and its attachment to the APA frame
ProtoDUNE-SP
Local diagnostics with complete data readout at the feed-through for test and commissioning

## Slide 4: 40% APA Cold Test Result
@BNL

## Slide 5: 40% APA Integration Test Stand at BNL
40% APA
  2.8m × 1.0m Area ~ 2.8m2
  40% of original LBNE APA of 7m × 2.5m
  ~45% of DUNE APA of 6m × 2.3m
  1024 sensing wires  8 FEMBs required
SBND APA
  4m × 2.5m
40% APA and FEMBs
WIEC
Flange
WIENER PS
Cold box
  Length of collection wire (4m) of SBND APA is same as induction wire of 40% APA
Integration test stand

## Slide 6: 40% APA with 8 FEMBs was moving into cold box
8 FEMBs with 7m cold cables
Cold power cable is not shielded and confirmed no effect on ENC measurement
  Hucheng Chen. Electronics and Noise: Experience from MicroBooNE and SBND/ProtoDUNE status. Joint DUNE/SBN Metting: Lesson Learned. May 15, 2017

## Slide 7: Video: LN2 filling in cold box

## Slide 8: Cold test of 40% APA fully submerged in LN2
Cold box with 40% APA
Feed-through + WIEC

## Slide 9: More Pictures
After cold test, 40% APA were still fully submerged in LN2
(~ 400 gallons LN2 was consumed)
APA and FEMBs were fully submerged in LN2
Some channels with extra 82pF/150pF MICA caps

## Slide 10: Video: APA and FEMB fully submerged in LN2

## Slide 11: 40% APA Test Grounding Scheme
Only fiber and power cables are coming out of warm interface electronics crate

## Slide 12: Capacitance Measurement at LN2
FE input capacitance on FEMB
  ~38 pF
Total capacitance of APA + FEMB
  Y plane: ~100 pF
  U/V plane: ~125 pF
  All measurements were done with APA fully submerged in LN2

## Slide 13: 40% APA Test Stand Status Overview
Total number of channels: 128*8 =1024
  Y channels: 56 * 8 = 448
  V channels: 36 * 8 = 288
  U channels: 36 * 8 = 288
Total number of FE channels read out: 1023
  1 FE channel is broken
Among 1023 readout channels
  Short channels: 3 (3V)  high noise
  Open channels: 5 ( 1Y+3V+1U)
  Y channels: 442
  Y channels with 150pF caps: 2
  Y channels with 82pF caps: 2
  V channels: 278
  V channels with 150pF caps: 2
  V channels with 82pF caps: 2
  U channels: 283
  U channels with 150pF caps: 2
  U channels with 82pF caps: 2

## Slide 14: Gain(e-/ADC) is stable at LN2
Top FEMB slot0 (25mV/fC)

## Slide 15: ENC Measurement at LN2
Top FEMB slot0 (25mV/fC)

## Slide 16: ENC Measurement at LN2
40% APA test is using 8 ProtoDUNE-SP FEMBs
  128 FE channels per FEMB
ProtoDUNE-SP decided to use P1 ADC, given the short time scale
DNL of P1 ADC has not been resolved
  The ENC measurement could be affected.
  However, by avoiding the stuck code regions, as will be seen, good noise results have been obtained

## Slide 17: ENC Measurement at LN2
U+150pF
Y+150pF
V+150pF
U+82pF
Y+82pF
V+82pF
Channels affected by stuck code
When ADC offset adjustment is enabled, pedestal could have offset to avoid stuck

## Slide 18: ENC vs. Cd @ LN2 (raw data)
2.3 e-/pF
no wire
Y
U
V
U+82pF
V+82pF
Y+150pF
U+150pF
V+150pF
Y+82pF
ENC is measured with 1us peaking time and 25mV/fC gain

## Slide 19: ENC Projection for SBND/ProtoDUNE-SP (based on raw data)
no wire
Y
U
V
U+82pF
V+82pF
Y+150pF
U+150pF
V+150pF
Y+82pF
×
×
ProtoDUNE-SP
Collection Plane ~500 e-
ProtoDUNE-SP
Induction Plane ~600e-
O
O
SBND
Induction Plane ~500e-
SBND
Collection Plane ~400e-
SBND APA
  U/V wire (max): 5.77m
  Y: 4.0m
ProtoDUNE-SP APA
  U/V wire: 7.39m
  Y wire: 6.0m

## Slide 20: Coherent Noise Diagnostics
Coherent noise filter can be applied to the noise analysis of 40% APA test
Notes: Top FEMB0,

## Slide 21: Comparison of coherent noise in MicroBooNE and 40% APA
As a reference, when Tp = 2us
Noise performance is comparable with MicroBooNE
MicroBooNE |  |  | 
 | Y | V | U
Length /m | 2.5 | 4.8 | 4.8
Pre-filtering / e- | 350 | 490 | 480
Post-filtering /e- | 300 | 380 | 400
40% APA |  |  | 
 | Y | V | U
Length /m | 2.8 | 4.0 | 4.0
Pre-filtering / e- | 332 | 351 | 380
Post-filtering /e- | 318 | 325 | 352

## Slide 22: ProtoDUNE-SP CE Installation and Check Out
@CERN

## Slide 23: ProtoDUNE-SP CE Installation
20 FEMB + CE box assemblies installed on the first APA @ CERN
A check out test has been done on all FEMBs in the week of 09/04
    Built-in electronics calibration circuit has been used to characterize the readout electronics system
    Through averaging calibration response, which is necessary to cope with environmental pick-up to the unshielded APA, functionality of each channel can be checked out
      All 2560 front end channels are confirmed to be 100% functioning well
      Only one front end channel is not connected to APA properly from upstream of cold electronics
Jack Fried and Shanshan Gao – check out test

## Slide 24: ProtoDUNE-SP Cold Box Test @ RT
APA moved into Cold box on 10/13
WIEC
(Only power cables and fibers coming out)
Cryostat reference

## Slide 25: Feed-through flange and cold cables

## Slide 26: Capacitance Measurement @ RT
Capacitance of 128 APA wires (APA B side slot 3) is measured @ RT
  Measurement was done without FEMB plugged in APA
  Y wires (48 channels) —> 87 ± 1.0 pF
  V wires (40 channels) —> 115 ± 2.0 pF
  U wires (40 channels) —> 112 ± 1.8 pF
  Above capacitance values include capacitance from APA wire, CR board and PSL adapter board.
  Capacitance of wire sections in the liquid argon will be increased by 1.5
    A fraction of the wire capacitance is to the frame from the wire wrapping
APA A side | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
APA B side | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1

## Slide 27: Gain(e-/ADC) is stable at RT (Preliminary)
FEMB + CE box on APA B side
APA A side | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
APA B side | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
25mV/fC

## Slide 28: ENC Measurement at RT (Preliminary)
FEMB + CE box on APA B side
APA A side | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
APA B side | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
25mV/fC

## Slide 29: Summary
ENC measurement of 40% APA fully submerged in LN2 at BNL shows satisfactory noise performance
  Noise is comparable to MicroBooNE measurement
Projection of ENC for ProtoDUNE-SP and SBND looks promising
Cold test of ProtoDUNE-SP APA in the cold box at CERN will be performed at CERN when the gas cooling system is ready
40% APA studies will continue at BNL

## Slide 30: Backup

## Slide 31: APA Size Comparison
40% APA
35ton APA
DUNE APA
  6m x 2.3m
40% APA~
  2.8m x 1.0m ~ 2.8m2
  40% of original LBNE APA of 7m x 2.5m
  ~45% of DUNE APA
35ton has 3 sizes of APA
  2m x 0.5m
  1.2m x 0.5m ~ 3m2
  0.8m x 0.5m
SBND APA
  4m x 2.5m