## Slide 1
Light Readout system (example assuming similar photodetectors coverage as in ProtoDUNE-DP)

## Slide 2
A few points of discussion raised at the time of the workshop:
Number of channels for future cards for 10 kton (mail exchange with Cyril: 1632 channels)
Impact:
Bandwidth (with present arrangement shown by Thomas at previous Consortium meeting):
1 link/crate, 9 cards per crate (16 channels/card)  144 channels/crate
14 bits, 2.5 MHz sampling continuous streaming  4.7 Gbit/s per link
 Close to saturation of 10 Gbit/s link if 32 channels/card and still 9 cards/crate
b)Layout: mitigation of long cable connections: Past solution shown by Thomas had 5 crates. Is it worth to increase further the concentration of channels ?
Time resolution to triangulate and localize light emission points for instance for SN neutrino interactions (new concept raised by J. Klein during the workshop). Some considerations about other limiting factors (before electronics) summarized by Slavic